## Slide 1: More Interconnect BIRD Terminal_type Association Table Formats
Mike LaBonte
20 July 2016

## Slide 2: A: Minimal Information
Terminal_type | Terminal_type_qualifier |  |  |  | aggressor
 | pin_name | signal_name | bus_label | pad_name | 
Buf_I/O | X1 |  |  |  | X
Buf_PU_Ref | X2 |  |  |  | 
Buf_PD_Ref | X2 |  |  |  | 
Buf_PC_Ref | X2 |  |  |  | 
Buf_GC_Ref | X2 |  |  |  | 
Buf_Ext_Ref | X2 |  |  |  | 
Buf_Rail |  | X | X |  | 
Pad_I/O | X1 |  |  |  | X
Pad_Rail |  | X | X | X | 
Pin_I/O | X1 |  |  |  | X
Pin_Rail | X2 | X | X |  | 
Notes:
Must be a pin connected to a buffer I/O terminal.
Must be the name of a pin connected to buffer rail terminal(s).

## Slide 3: B: Common Angle Bracket Syntax
Terminal_type | Terminal_type_qualifier |  |  |  | aggressor
 | pin_name | signal_name | bus_label | pad_name | 
Buf_I/O | <pin>1 |  |  |  | Aggressor
Buf_PU_Ref | <pin>2 |  |  |  | 
Buf_PD_Ref | <pin>2 |  |  |  | 
Buf_PC_Ref | <pin>2 |  |  |  | 
Buf_GC_Ref | <pin>2 |  |  |  | 
Buf_Ext_Ref | <pin>2 |  |  |  | 
Buf_Rail |  | <signal> | <bus> |  | 
Pad_I/O | <pin>1 |  |  |  | Aggressor
Pad_Rail |  | <signal> | <bus> | <pad> | 
Pin_I/O | <pin>1 |  |  |  | Aggressor
Pin_Rail | <pin>2 | <signal> | <bus> |  | 
Notes:
Must be the name of a pin connect to a buffer I/O terminal.
Must be the name of a pin connected to buffer rail terminal(s).
Must be the word “Aggressor”, to signify suitability only for aggressor signals in crosstalk simulations.

## Slide 4: C: Double Quotes for Strings
Terminal_type | Terminal_type_qualifier |  |  |  | aggressor
 | pin_name | signal_name | bus_label | pad_name | 
Buf_I/O | pin1 |  |  |  | “Aggressor”3
Buf_PU_Ref | pin2 |  |  |  | 
Buf_PD_Ref | pin2 |  |  |  | 
Buf_PC_Ref | pin2 |  |  |  | 
Buf_GC_Ref | pin2 |  |  |  | 
Buf_Ext_Ref | pin2 |  |  |  | 
Buf_Rail |  | signal | bus |  | 
Pad_I/O | pin1 |  |  |  | “Aggressor”3
Pad_Rail |  | signal | bus | pad | 
Pin_I/O | pin1 |  |  |  | “Aggressor”3
Pin_Rail | pin2 | signal | bus |  | 
Notes:
Must be the name of a pin connected to a buffer I/O terminal.
Must be the name of a pin connected to buffer rail terminal(s).
Must be the word “Aggressor”, to signify suitability only for aggressor signals in crosstalk simulations.

## Slide 5: D: Two Pin Columns
Terminal_type | Terminal_type_qualifier |  |  |  |  | aggressor
 | I/O pin_name1 | Rail pin_name2 | signal_name | bus_label | pad_name | 
Buf_I/O | X |  |  |  |  | X
Buf_PU_Ref |  | X |  |  |  | 
Buf_PD_Ref |  | X |  |  |  | 
Buf_PC_Ref |  | X |  |  |  | 
Buf_GC_Ref |  | X |  |  |  | 
Buf_Ext_Ref |  | X |  |  |  | 
Buf_Rail |  |  | X | X |  | 
Pad_I/O | X |  |  |  |  | X
Pad_Rail |  |  | X | X | X | 
Pin_I/O | X |  |  |  |  | X
Pin_Rail |  | X | X | X |  | 
Notes:
1: Must be the name of a pin connected to a buffer I/O terminal.
2: Must be the name of a pin connected to buffer rail terminal(s).