## Slide 1: Package Die Ports
Walter Katz
IBIS Interconnect
10/31/12

## Slide 2: Overview
Defining Ports of Package and On-Die Interconnect Models
  Minimal change to legacy IBIS files
  On-Die models are
    dependent on die only
    independent of package
  Package models are
    dependent on package only
    independent of die

## Slide 3: Die “Buffer” Ports DieBuf.DQ1 DiePu.DQ1 DiePd.DQ1
Indicates XYZ of Die Buffer Port of On-Die Model

## Slide 4: Die “Pad” Types / Ports DiePad.DQ1
Bump Pad (e.g. Flip Chip)
Bondwire Pad (e.g. Wire Bond)
Indicates XYZ of Die Pad Port of On-Die Model

## Slide 5: Package “Pad” Types / Ports PkgPad.A1
Bump Pad (e.g. Flip Chip)
Indicates XYZ of Pad Port of Package Model
Bondwire Pad (e.g. Wire Bond)

## Slide 6: Package “Pin” Types / Ports PkgPin.A1
Pin (e.g. PGA)
Ball (e.g. BGA)
Pad (e.g. SMD)
Side (e.g. Stacked SOL)
Indicates XYZ of Pin Port of Package Model

## Slide 7: Implicit Port Names
[Pin]
  A1 DQ1 DQ
On-Die Model
  DieBuf.DQ1
  DiePad.DQ1
Package Model
  PkgPad.A1
  PkgPin.A1

## Slide 8: Signal Interconnect Models
.ibs
[Pin]
  A1 DQ1 DQ
  A2 DQ2 DQ
  B1 VDD Power
  B2 VDD Power
  B3 VSS GND
  B4 VSS GND
[Model] DQ
  PuRef VDD
  PdRef VSS
Models
Package
  .subckt A1 PkgPin.A1 PkgPad.A1
  .subckt A2 PkgPin.A2 PkgPad.A2
On-Die
  .subckt DQ1 DiePad.DQ1 DieBuf.DQ1
  .subckt DQ2 DiePad.DQ2 DieBuf.DQ2
Combined
  .subckt A1DQ1 PkgPin.A1 DieBuf.DQ1
  X1 PkgPin.A1 die A1
  X2 PkgPin.A1 die DieBuf.DQ1 DQ1
  .ends A1DQ1

## Slide 9: Power/GND Pins Legacy IBIS No Distributed Die PDN
.ibs
[Pin]
  B1 VDD Power
  B2 VDD Power
  B3 VSS GND
  B4 VSS GND
[Model] DQ
  PuRef VDD
  PdRef VSS
Package Model Ports
PkgPin.B1
PkgPin.B2
PkgPin.B3
PkgPin.B4
PkgPad.VDD
PkgPad.VSS

## Slide 10: Power/GND Pins Distributed Die PDN
.ibs
[Pin]
  A1 DQ1 DQ
  A2 DQ2 DQ
  B1 VDD Power
  B2 VDD Power
  B3 VSS GND
  B4 VSS GND
[Die Pad]
  D1 VDD
  D2 VDD
  D3 VDD
  D4 VSS
  D5 VSS
  D6 VSS
[Model] DQ
  PuRef VDD
  PdRef VSS

## Slide 11: Package an On-Die Ports Distributed Die PDN
Package PDN Model Ports
PkgPinB1
PkgPin.B2
PkgPin.B3
PkgPin.B4
PkgPad.D1
PkgPad.D2
PkgPad.D3
PkgPad.D4
PkgPad.D5
PkgPad.D6
Die PDN Model Ports
DiePad.D1
DiePad.D2
DiePad.D3
DiePad.D4
DiePad.D5
DiePad.D6
DiePu.DQ1
DiePu.DQ2
DiePd.DQ1
DiePd.DQ2

## Slide 12: Conclusions
Only need [Die Pad] section for distributed die Power Delivery Network (PDN)
Implicit naming conventions allow package models independent of die and on-die models independent of package
Can be extended to allow different wire bond models dependent on die used in package