IBIS Survey Results

1-3-97

Research Question:

Basic question we wanted to answer was “Would a >$100k hardware IBIS extraction solution be a viable product?” To look at this we wanted to understand “How are people creating IBIS models today?”

Methodology:

An open ended set of 8 questions were posted on an IBIS reflector site on the WWW.

We had 11 responses, 9 were filled out in a way as to add valuable information, one was a request for information on IBIS applicability, and one was a request to show products at Design Supercon.

Conclusions:

Component suppliers (active digital I/O) would be the best target customer, because of the  existing modeling groups and some budget. Syed Huq from National Semiconductor represents the best contact to investigate further. When asked for new approaches he listed “Automation in creating a model from empirical data and easier tools for model validation.” We’d have to see what Syed actually has in mind.

While component suppliers (active digital I/O) represents the best opportunity, I’d be concerned that we didn’t get responses from the other big digital I/O companies (except SGS-Thomson), and what this says about the size of the market.

CAE vendors who develop IBIS models could also match the product, but I don’t see more than 5-10 potential sales from this area.

PCB simulation users who develop IBIS models don’t have the budget or manpower allocated today to support a >$100k piece of hardware. A simpler curve tracer with software to develop IBIS models would be a better start.

A commercial spice to IBIS converter, supported, documented and simplified would be the best first step, but also has an upper price bound imposed by the availability of the free version.

Detailed Summary:

3 catagories of IBIS model developers

PCB Simulation users	 (3)

Component suppliers	 (4)

CAE vendors		 (2)

How do you go about developing IBIS models?

7 of 7 derive IBIS models from SPICE

4 of 7 also mention deriving IBIS models from measurements

Two of these mentioned SPICE first then measurements

Two of these mentioned measurements first

Measurement based models appear to be low frequency/without slew rates

Curve tracer - IV curves

IC tester

Three or four possible candidates for investigating IBIS model development

PCB simulation users

No “modeling” budget

Designers, not modelers

Not a modeling group

Modeling is just a means to an end

Use existing equipment

Lack of manpower allocated to task

Benefit of IBIS modeling to simulation user

Faster simulation of behavioral models enables being able to simulate full PCBs with layout effects. Selecting drive strengths of chip buffers is design variable designers can control.

Curve tracer sets the expectation for cost and complexity of IBIS development

Not looking for n-outputs on a chip.

Package data comes from other sources

HSPICE seems to be where existing SPICE models come from

Component suppliers

Modeling people do exist and are budgeted

Size of budgets and strength of groups is unknown.

Benefit of IBIS modeling to component suppliers

All are developing IBIS as a response to meet customer requests

Two sub-groups

Active

Looking for automation in creating models from empirical data and validation of models

Passive

Looking for multi-coupled line behavioral models

CAE vendors

Modeling people do exist

Some have IC testers for other purposes

Benefit of IBIS modeling to cae vendors

Builds applicability and sales potential for simulators