## Slide 1: Higher-level Models to Support (rough priority order)
2-tap pre-emphasis
n-tap pre-emphasis
Gate modulation
Self-calibrating output
Pass-thru receiver
Decision Feedback Equalization (DFE)

## Slide 2: Lower-level Primitives / Features (rough priority order)
Parameter passing
Equation-based sources (voltage, current, numeric)
B element with c_comp on/off and table scaling (static/dynamic)
  Hspice can’t do c_comp or dynamic
Expressions in parameters
Table-based PWL sources
Time-controlled sources
  Hspice can not do
If, then, else in equations
  Hspice ???
Simulation “time” as variable
Use of previously computed value (prev(x)) in equation
  Hspice can not
Calculation of 1st derivative of voltage or current
  Hspice can not