## Slide 1: Algorithmic Modeling (AMI) Parameter Syntax Discussion
August 14, 2007

## Slide 2: Where we are wrt Parameters
Previous Draft BIRD had defined new parameter structure and syntax for use in the Algorithmic Modeling Section
  Instance specific parameters are to be chosen by the user through the EDA platform, which are then passed to the DLL
EDA platform will pass parameters to DLLs in tree format (different than specified in Draft BIRD)

## Slide 3: Problems
Parameter declarations are flat
Parameter declarations in IBIS file and instance specific parameters passed to DLL are in different format
Advanced SERDES models will require hierarchy

## Slide 4: Proposed Solution
Make Parameter syntax in IBIS consistent with the tree format that is used by EDA platform and DLLs (syntax changes)
  Original Parameter declaration structure remains unchanged (as defined in the Draft BIRD) with Reserved Keywords and “standard” set of parameters
    Ignore_bits, GetWave_exists etc
    “Standard” set of parameters are interpreted and used by EDA platforms
  Two choices for storing Parameter Declarations
    Put parameters in AMI file, IBIS file points to the AMI file
      This will also include the DLL model file name per platform
    Put parameters declarations in tree format into the IBIS file
Parameter structure and syntax can be reused regardless where it is stored for use by Algorithmic Models

## Slide 5: Separate AMI file
IBIS Check can parse, check ami file
    EDA Vendors willing to provide starter parser & checker
AMI file will be parsed by EDA platform and the parameters will be passed to model dll as defined in the draft BIRD
Pros
  IBIS file has analog front end and all associated data, AMI file has data for Algorithmic Models – clean and clear distinction
  Using an external AMI file reduces the IBIS file changes to ONE new keyword in IBIS
    [Algorithmic Model <modelName>]
    Where
      <modelName>.ami file contains
      Executable names for supported platforms
      Parameter Declarations
      Comments
Cons
  Two files instead of ONE

## Slide 6: Example ami file
(sampleAMI
|
| AMI field contains the name of the dll also
|
(Dll |Reserved Keyword
(linux sampleami_lnx.so)
(solaris sampleami_sun4.so)
(windows sampleami.dll)
(mac sampleami_mac.so)
)
(Reserved_Parameters |Reserved Keyword
| all the paremeters under this section are "standard". ie they have unique interpretatiosn
(Ignore_Bits (Type Integer) (Default 21))
(Max_Init_Aggressors (Type Integer)(Default 25))
(Init_Returns_Impulse (Type Bool)(Default True))
(GetWave_Exists (Type Bool) (Default True))
) | End Reserved
(Model_specific |Reserved Keyword
| txtaps is a structure
(txtaps
(tapid (Range -1 3) (type int) )
(txtapcoeff
(-1 (Range -0.1 0.1 0.1) (Type float) (Default 0))
(0 (Range 1 1 0) (Type float) (Default 1))
(1 (List -0.1 0.1) (Type float)(Default 0))
(2 (Range -0.01 0.02 0.005) (Type float) (Default 0))
(3 (Range -0.01 0.02 0.005) (Type float) (Default 0))
) | tapcoeff
) | txtaps
(tx_freq_offset (Range 0 150 1) (Type ppm) (Default 0))
) | End User_Defined
| here is an example of txtaps instance
| (txtapcoeff (-1 -0.05) (0 1) (1 0) (2 0) (3 0))
) | End SampleAMI

## Slide 7: Parameter Declarations in IBIS file
Pros
  All model developer published parameters contained in one file
Cons
  Syntax for the parameters in Algorithmic Modeling Section very different than syntax for other parameters in the IBIS file