## Slide 1: IBIS & ICM Interfacing: Three Options
Michael Mirmak
Intel Corporation
December 4, 2007

## Slide 2: IBIS & ICM Today
High demand for improvements to IBIS package technology
ICM can describe almost any interconnect
  ICM today includes
    Interconnect RLGC or S-parameter characteristics
    Coupling, if present, between interconnect segments
    Pin end-points and names
  ICM and IBIS are completely separate
    ICM does not make reference to any IBIS structure
ICM support for IBIS packages needs to cover…
  Expanding [Package Model] to reference ICM files
  [Model], [External Model] and [External Circuit] cases
IBIS has a number of limits that make complex package models tricky
  1-to-1 connections from package to pin are assumed
  [Pin] implicitly defines both pin AND buffer instance

## Slide 3: Package Modeling Today
IBIS 3.2 & 4.0 Approach
If [Pin] and [Pin Numbers] ([Package Model]) use the same values…
  Tools assume connections corresponding to values
  Tools infer connections between [Model], [Pin] and package
  [Pin Mapping] can map supplies to package pins
A1 name iobuf
B1 name iobuff
[Pin]
[Package Model]
[Model] iobuf
[Model] iobuf
implied!
implied!
[Pin Numbers]
A2 name GND
[Pin] & [Pin Mapping]
implied!
Notes: ICM can do pin-to-pin coupling easily under this structure, if [Package Model] expands to support ICM files.

## Slide 4: What about this?
Forked t-line assignment
  This structure cannot be described using IBIS 3.2/4.0
    A fork can only end as an unterminated stub
A1
C1
[Pin]
[Package Model]
[Model]
[Model]
[Model]
implied!
implied!
[Pin Numbers]
?

## Slide 5: IBIS & ICM
What interfacing options require new syntax?
IBIS 3.2/4.0 + ICM
  Key decision: expand IBIS beyond 1-to-1 [Pin] connections OR limit ICM to only 1-to-1 paths here
IBIS 4.1/4.2 + [External Model]
  Should be nearly identical to IBIS 3.2/4.0 treatment
  Decision above dictates [External Model] treatment
IBIS 4.1/4.2 + [External Circuit]
  Fairly easy, using [Node Declarations]
Algorithmic models unaffected
Notes: 1-to-1 is very easy to adapt to support ICM; non-1-to-1 was requested by some EDA vendors and is much harder….

## Slide 6: Summary of Options
Today’s Choices
Easy
Hardest
Harder
Minimal changes to
IBIS; keep 1-to-1
connections
Redefine [Pin] &
add nodal syntax
to IBIS
Defer ICM links
until new IBIS
architecture defined
Notes: “new IBIS architecture” essentially Walter Katz’s 3-part-IBIS proposal

## Slide 7: The Easy Solution

## Slide 8: The Easiest Option Follows IBIS Assumptions
Maintain the 1-to-1 [Pin]-[Model] approach for “classic IBIS” models
No support of multiple package paths under “classic IBIS”
Multiple package paths would be available under [External Circuit]
ICM can only be used with…
[External Circuit] through [Node Declarations]
[Model]/[E. Model] through 1-to-1 package descriptions
Assumptions
IBIS [Pin]/[Model] names must match one node/pin map in ICM
    Other end of ICM path is assumed connected to the [Model] pad
    More than two ICM endpoint nodes are unterminated/unconnected
[Pin Mapping] connects packages to buffers
    “Rail” names match ICM node on one side and [Pin] name on the other
Notes: Easy to create, easy to parse but limited

## Slide 9: [External Circuit]
Linking ICM to IBIS [E. Circuit]
  Use [Node Declarations] to list internal ICM map pin names
|****************************************
  [Node Declarations]
  |Die pads OR PIN NAMES
  A1, A2, A3, A4
  buff1, buff2, buff3, buff4
  [End Node Declarations]
  |****************************************
  [ICM Pin Map] Example1_external
  Pin_order Row_ordered
  Num_of_columns = 4
  Num_of_rows = 1
  Pin_list
  |Pin Name
  A1 AD2
  A2 AD5
  A3 AD7
  A4 GND
Easy!
Just change [Package Model]
Only downsides:
Names must be matched;
arbitrary packages not reusable
Both sides of ICM
interconnect are mapped
  [ICM Pin Map] Example1_internal
  Pin_order Row_ordered
  Num_of_columns = 4
  Num_of_rows = 1
  Pin_list
  |Pin Name
  buff1 AD2
  buff2 AD5
  buff3 AD7
  buff4 GND
IBIS
ICM
(IIRD8)

## Slide 10: The Harder Solution

## Slide 11: Key Concept: Expand [Pin] Syntax
Developed from an idea by A. Muranyi
Expand [Pin] to:
  Allow reuse of [Pin] name in first column in more than one line
  Add a column which names [Model] instance not just [Model]
    A specific [Model] instance is a pad identifier
  Use a “dot notation” in ICM to point to specific nodes
    component.pin.instance at one end
    [Pin] name at the other
    [External Model]: component.pin.instance.analog_port
  Same system works for traditional IBIS package models!
Concept:
  Naming a [Pin] twice links the same pin to multiple buffers
  “instance_name” column is a buffer instance identifier
  Unique pin/model pairs still assume 1-1 association
  This syntax enables tools to track electrical association easily
Notes: Why do this? Simple: some customers and EDA vendors may want better packages with traditional IBIS table-driven models.

## Slide 12: Expansion of [Pin]
New [Pin] syntax examples
[Pin] signal_name model_name R_pin L_pin C_pin instance_name
A1 Power POWER
A2 Ground GND
A3 AD1 IO
A4 CLK Input NA NA NA Input1
A4 CLK Input NA NA NA Input2
|
| Pin A4 above is named CLK and is tied to TWO die pads/buffers.
| One is called Input1 and the other is called Input2.
| Both refer to the same [Model] in the IBIS file.
|
| The version below is also legal:
[Pin] signal_name model_name R_pin L_pin C_pin instance_name
A1 Power POWER
A2 Ground GND
A3 AD1 IO
A4 CONTROL Input NA NA NA InputControl
A4 CONTROL Output NA NA NA OutputControl
|
| Pin A4 above is named CONTROL and is intended for use as a feedback buffer
| control. This pin is tied to TWO die pads/buffers. The buffers use different
| [Model]s in the IBIS file and are named InputControl and OutputControl.
Notes: Does this also cure our differential problems?
Just like C functions or SPICE subcircuits

## Slide 13: Expansion of [Pin]
Multiple pins, same buffer
[Pin] signal_name model_name R_pin L_pin C_pin instance_name
A1 Power POWER
A2 Ground GND
A3 AD1 IO
A4 CLK1 Output NA NA NA DRIVERA
A5 CLK2 Output NA NA NA DRIVERA
|
|
| Pins A4 and A5 are physically separate pins, with distinct names. However,
| they are intended to be driven by the same buffer (a ganged output)
| In this case, the same model_name is used (same buffer design is used for both
| pins AND the same instance_name is used for each. This shows that the same
| buffer instance is used for both pins, and not two instances of the same
| buffer design.

## Slide 14: Traditional Packages… Expanded!
This new syntax supports ICM and non-ICM packages
We add a package parameter “Pad” that points to instances from the new [Pin] column
Recall that IBIS [Package Model] starts from the die and moves out
Old syntax is still supported!
|* Here is an example where a two Buffers are explicitly linked to the
|* same named pin.
|*
|* 14 Pad=InControl Len=0 L=2.3n / | Buffer and bondwire
|* Fork | indicates the starting of a branch
|* Len=0 L=2.3n / | a different bondwire
|* Pad=OutControl | Buffer pad
|* Endfork | ending of the branch
|* Len=1.2 L=1.0n C=2.5p / | first section
|* Len=0.5 L=1.0 C=2.5/ | second section, pin connects here
|* Fork | indicates the starting of a branch
|* Len=1.0 L=2.0n C=1.5p / | section
|* Endfork | ending of the branch
|* The connection to the named pin follows the final Endfork

## Slide 15: Harder Approach Alters IBIS Assumptions
Summary of Changes
  Update [Pin] with instance_name column
    Include new usage rules for multiple pins/multiple buffers
  Update [Pin Numbers] (IBIS PKG) for Buffers
  Update [Package Model]
    Must accept .icm files
    Must support new dot notation names
  No changes required to ICM
This does not replace Circuit Call
  New [Pin] only supports “native” IBIS and [External Model]
  [Node Declarations] used for ICM and [External Circuit]
Issues to consider
  Parsing: How to check dot notation between ICM and IBIS?
  [Pin Mapping] prohibited with [E. Model], [E. Circuit]
  [Series Pin Mapping], [Diff Pin] still tricky

## Slide 16: Draft Interfacing BIRD

## Slide 17: The Hardest Solution

## Slide 18: Hardest Approach Rewrites IBIS Assumptions
Start “fresh” with IBIS architecture that
supports ICM natively without 1-to-1 assumption
Easy to state but hard to write…

## Slide 19: What do we want to do?
Notes: Personal recommendations are (hardest) then (easy) then (harder)

## Slide 20: BACKUP

## Slide 21: Package Modeling Today
  |**************************************************************************
  [IBIS Ver] 3.2
  [File name] example.ibs
  {...}
  [Component] Example_chip
  {...}
  [Package Model] simple_package
  |**************************************************************************
  [Pin] signal_name model_name R_pin L_pin C_pin
  1 IO1 io_buffer
  2 IO2 io_buffer
  3 IO3 io_buffer
  |**************************************************************************
  [Model] io_buffer
  Model_type I/O
  {...}
  |**************************************************************************
  |
  [Define Package Model] simple_package
  [Number of Pins] 3
  |
  [Pin Numbers]
  A1 Len=1.2 L=2.0n C=0.5p R=0.05/
  B1 Len=1.2 L=2.0n C=0.5p R=0.05/
  C1 Len=1.2 L=2.0n C=0.5p R=0.05/
  |
  [End Package Model]
  [End]
  |**************************************************************************
Package Model
definition/assignment
(overrides [Pin] and
[Package])
Header
([Package] not shown)
Pin/Model
assignment
Model definition

## Slide 22: Four Cases
We must handle four cases to have a comprehensive package approach
Case 1: ICM expresses coupling – DONE with [Package Model]
[Model]
[Model]
[Model]
ICM
Pin A1
Pin B1
Pin C1

## Slide 23: Four Cases
Case 2 – Wired-or or “mux” connections
  Multiple pins, single [Model] - DONE with [Package Model]
[Model]
ICM
Pin A1
Pin B1
Pin C1

## Slide 24: Four Cases
Case 3 – Coupling & power distribution
  Single model, single signal pin –
    DONE with [Package Model] and [Pin Mapping]
  No different than Case 2, from [Pin] perspective
[Model]
ICM
POWER
Pin A1
GND

## Slide 25: Four Cases
Case 4 – Wired-or or “mux” connection
  Single pin, multiple [Model]s
[Model]
[Model]
[Model]
ICM
Pin A1

## Slide 26: [Pin] Rulesfor “Harder” Solution
New syntax language rules for specification
Rules: Each shared or repeated entry under column 1 of [Pin] must have the same signal_name as all other pins using the same column 1 entry. Example (1) shows such a case.
Any [Pin] which uses the same column 1 entry as another pin MUST have instance_name filled out, even if the model_name is different. Otherwise, an error is flagged, as in IBIS version 1.1 through 4.1.
R_pin, L_pin and C_pin entries for duplicated pins may be filled out numerically or may be NA. If instance_name is used, the R_pin, L_pin and C_pin columns MUST contain entries. Rules regarding precedence of [Package Model] and [Package] over [Pin] parasitic entries still apply even when instance_name is present.
No entry in the instance_name field is permitted for [Pin]s of type POWER, GND, NA or CIRCUITCALL.
Identical instance_name entries for different [Pin]s (different column 1 entries) with identical model_name entries are permitted. This signifies multiple pins connected to the same buffer instance. Example (3) shows such a case.

## Slide 27: Package Modeling Today
A Few Oddities
  Package Pin attachment
“A package stub description starts at the connection to the die and ends at the point at which the package pin interfaces with the board or substrate the IC package is mounted on.”
A1 Len=0 L=1.2n/ Len=1.2 L=2.0n C=0.5p/ Len=0 L=2.0n C=1.0p/
  Package Pins vs. Fork/Endfork
“The package pin is connected to the last section of a package stub description not surrounded by a Fork/Endfork statements.”
Pin is here!

## Slide 28: Assuming [Pin Mapping] as On-die
Package model associated with pins
[Pin Mapping] is between packages and buffers
Digital Port
[Package], [Pin]
A2 (POWER)
A1
A3 (GND)
[Pin
Mapping]
[Package Model]
pullup_ref
pulldown_ref