## Slide 1: The Presentation That Arpad Forgot
Michael Mirmak
Intel Corp.
September 30, 2008

## Slide 2: Proposal for New Keywords to Improve Buffer Impedance Modeling
Michael Mirmak
Intel Corp.
September 30, 2008

## Slide 3: A Simple Proposal
Add two “traditional” IBIS keywords to IBIS 5.1
  [C_comp Series R]
  [C_comp Series C]
Examples
[C_comp Series R]
Branch 1
| units below are volts, ohms
|Voltage typ min max
0.0 20 NA NA
0.75 20 NA NA
1.5 800 NA NA
[C_comp Series C]
Branch 1
| units below are volts, farads
|Voltage typ min max
0.0 4p NA NA
0.75 2.33p NA NA
1.5 1.63p NA NA

## Slide 4: Concept
This approach captures both buffer Z(f) and Z(V) variations, improving time- and frequency-domain modeling.
It supports the “Rdie” DDR approach currently documented by JEDEC.
It avoids direct frequency-based tables, difficult extraction methods or extensive model pre-processing.
Supporting these in today's tools should not represent any more of a burden than classic C_comp does.
The tables here cover an I-V-like voltage range, but need not match I-V ranges for any particular table. In many cases a pair of voltage rows for a particular [... R] and [... C] with different voltages but identical R and C values per corner would be perfectly adequate.
CComp
Branch 1
Branch 2
Branch 3
…

## Slide 5: Keyword Syntax Rules
[C_comp Series R] and [C_comp Series C]
  are optional
  are hierarchically located within [Model]
  may appear multiple times within any [Model]
  contain only one subparameter, "Branch"
  contain four columns of data after the required subparameter
  columns are voltage, and typ/min/max ohms (for [... Series R])
  columns are voltage, and typ/min/max farads (for [... Series C])
  do not affect, override or interfere with existing C_comp values
  if one is present, the other is required for any given Branch value
  voltage corresponds to pad vs. pulldown/ground clamp rail (really, the bias voltage for AC sweeps)
  voltage sweep should correspond to pulldown range (-Vcc to 2*Vcc)
  must not contain negative values (voltage, capacitance or resistance)
Branch subparameter
  is required for any usage of [C_comp Series R] and/or [C_comp Series C]
  contains an integer argument, positive and non-zero
  no two [... Series C] tables may have the same Branch value in the same [Model]
  no two [... Series R] tables may have the same Branch value in the same [Model]
  If multiple tables are present, one must use the value 1 and others must use sequential increasing Branch values

## Slide 6: Issues
These keywords are generally subject to the same usage rules and restrictions as C_comp (e.g., not in series devices or [Driver Schedule] scheduled models).
No special treatment or procedure is defined here for differential buffers. A differential RC could be defined in a separate keyword structure, along with a differential C_comp.
These keywords are not expected to be used with multi-lingual (IBIS 4.1/4.2) buffers.
IBIS AMI should be unaffected, though the use of heavily voltage-dependent RC circuits may violate the LTI assumption in some cases.
Additional keywords or subparameters may be required should separate RC circuits connected to the pullup rail, power clamp rail, etc. be needed.
Impact to and usage in ECL designs is unknown.

## Slide 7: From April & October 2004 IBIS Summits…

## Slide 8: How is C_comp data collected?
Common method for single-ended buffer C_comp
  Use Vsource with known edge rate, dV/dt
  Measure the input current
  Calculate capacitance (may have to take an average)
Driver
I
Vsource
dV/dt
What about for the differential case?
How about pre-emphasis (wired-or structures)?

## Slide 9: IBIS for SerDes Pre-Emphasis
A
B
C
D
TX+
TX-
Pre-Emphasis
A = P C = P
B = P D = P
De-Emphasis
A = P C = P
B = P D = P
Main
Boost
Pullup – Main (+ & -)
Pullup – Boost (+ & -)
Ground Clamps
Main + & -
1) Extract C_comp
for entire buffer
2) Split C_comp
across Main, Boost

## Slide 10: Results of Crude C_comp Accounting
Transistor vs. Combination IBIS into Rload
C_comp = 8pF

## Slide 11: Proposed Fix
Method 2: Adjust all V-t curves for the total C_comp value before using the models for simulation
  Each V-t curve reflects total C_comp load
  Adjust each curve (Main, Boost) for total C_comp
  Set IBIS C_comp for Main, Boost to 0 pF
  Add external cap equal to original total C_comp
images and equations from A. Muranyi
Vwfm_pu (V-t)
Vfx_pu
fixture
Current through fixture
is function of current
through pullup AND
through die cap

## Slide 12: Another New Approach
First C_comp adjustment attempt made two assumptions
  Differential buffers can be “split” in two
  Each can be modeled adequately with a single C_comp
Additional data calls at least one assumption into question
  Single C_comp does not permit frequency dependence
  A differential component appears at some frequencies
Proposal: Stay in AC Domain for C_comp Measurement
  Attempt to match AC behavior of simulation model
  Once model correlates in frequency of interest, add data into IBIS model
    This may stretch IBIS 3.2/4.0 beyond available keywords

## Slide 13: Our Target Behavior
V
Hz
F
~ 14-15 pF
~ 5-7 pF
A Low
Pass
Filter!

## Slide 14: Recall L. Giacotto’s Slides…
2002: Luca Giacotto presented twice on buffer impedance starting with observations by A. Muranyi
Two caps,
two resistors

## Slide 15: Original Giacotto-Muranyi C_comp Model
Pad
CComp = 7pF
C1 = 8.3pF
45 Ω
R1
Linearized
I-V Curve
One side of our differential
buffer (built-in pulldown,
current source is AC high-Z)
Near DC, only 45 Ω;
At low AC, caps look more
like ~ 14 pF
Value of R1 depends on
frequency of drop in
capacitance to ~ 7 pF

## Slide 16: Model vs. AC Analysis of Buffer
transistor model
Ignoring voltage…

## Slide 17: Modified G-M Model
Pad
CComp = 3p
C2 = 8.3p
45 Ω
R1
R2
C3 = 4p
Linearized
I-V Curves
Near DC, only 45 Ω;
At low AC, caps still add to ~ 14 pF
Adding new elements
to cause new “break”
in frequency

## Slide 18: Modified Model AC Analysis
transistor model
Ignoring voltage…

## Slide 19: Model Assessment
Model is a fair match up to ~ 2 GHz
Problems arise
  A single C_comp value is no longer adequate
  No IBIS keywords support this structure
  Still need to “back out” these elements from V-t curves
Pad
CComp = 3p
C2 = 8.3p
45 Ω
R1= 5 kΩ
R2
= 20 Ω
C3 = 4p
Linearized
I-V Curves

## Slide 20: Original C_comp Adjustment
Pad
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
Idriver(t) = Icap(t) + Ifixture(t)
Icap = C_comp * dV/dt where dV/dt is instantaneous V-t slope
Ifixture = V-t/Rfixture, taken at every time point
“Cap-less” V-t curve = Idriver(t) * Rfixture
  Driver is pullup curve set with internal pulldowns
  Vfixture = 0, since there is no active, driving pulldown

## Slide 21: Modified Approach
Pad (V-t curves)
CComp
Rfixture
Diff.
Driver
Idriver
Icap
Ifixture
Very tricky differential equation…
Easier solution – use EDA tool to generate data!
  Create netlist as shown
  Drive PWL source with original V-t data set(s), at pad
  CCCS into load = Rfixture provides “adjusted” V-t curves
C1
C2
R1
R2
I1
I2
V1
V2

## Slide 22: Assessment
We can now adjust V-t curves for AC C_comp
  Enabling each portion of differential buffer…
  Take a separate V-t curve (Main Only, Boost only)
  Take AC domain frequency response for entire buffer
    Single-ended response only analyzed so far
  Match AC domain with model & extract adjusted V-t curve
Can we repeat the process for differential behavior?
V
Hz
F
A High
Pass
Filter!

## Slide 23: What About Differential C_comp?
Pad
CCompP = 3p
C2P = 8.3p
45 Ω
R1P
= 5k
R2P
= 20
C3P = 4p
CCompN = 3p
45 Ω
R1N
= 5k
R2N
= 20
C2N = 8.3p
Pad
C3N = 4p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 0V
We need Rdiff, not Cdiff!

## Slide 24: Differential C_comp (Bias = 0 V)
Diff. C_comp resembles a pass-band
filter (BW ~ 1/Rd)

## Slide 25: What About Differential C_comp?
Pad
CCompP = 3p
C2P = 8.3 p
45 Ω
R1P
= 5k
R2P
= 20
C3P
= 2.33 p
CCompN = 3p
45 Ω
R1N
= 5k
R2N
= 20
C2N = 8.3 p
Pad
C3N
= 2.33 p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 0.75 V

## Slide 26: Diff. C_comp (Bias = 0.75 V)

## Slide 27: What About Differential C_comp?
Pad
CCompP = 2.6 p
C2P = 4.86 p
45 Ω
R1P
= 5k
R2P
= 800
C3P
= 1.63 p
CCompN = 2.6 p
45 Ω
R1N
= 5k
R2N
= 800
C2N = 4.86 p
Pad
C3N
= 1.63 p
To match our
target…
RD ~ 2 Ω
At high Hz,
C2P and
C2N add
up, acting
differentially
Bias = 1.5 V

## Slide 28: Diff. C_comp (Bias = 1.5 V)