## Slide 1: Package Model Format Needs Revised with additional material Part 1…
Presented by Michael Mirmak
Updated Sept. 11, 2012

## Slide 2: Legal Disclaimers
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL® PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL’S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER, AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT. Intel products are not intended for use in medical, life saving, or life sustaining applications.
Intel may make changes to specifications and product descriptions at any time, without notice.
The Intel products in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Contact your local Intel sales office or your distributor to obtain the latest specifications and before placing your product order.
All dates specified are target dates, are provided for planning purposes only and are subject to change.
Code names in this document are used internally within Intel to identify products that are in development and not yet publicly announced for release. Customers, licensees and other third parties are not authorized by Intel to use code names in advertising, promotion or marketing of any product or services and any such use of Intel's internal code names is at the sole risk of the user.
Intel, Intel Core, Intel SpeedStep and the Intel logo are trademarks or registered trademarks of Intel Corporation or its subsidiaries in the United States and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2012, Intel Corporation. All rights reserved.

## Slide 3: Additional Material
Consulted with experts in new areas:
  PCB post-layout analysis
  Device and platform power delivery (two different product lines)
Now addressing all three segments of the IBIS community
  EDA vendors (both for extraction and system simulation)
  model makers
  end users (system designers)
Do the current proposals address both PCB pre- and
post-layout needs without overburdening one IBIS segment?

## Slide 4: Usage Models
What usage models should we support?
  Pre-PCB layout
    User doesn't care about specific package or board nets
    User just wants general trends on an interface
    A subset of signals will be modeled & simulated
  Post-PCB layout
    May have specific nets to examine
    Interested in other nets that may not yet be identified but become significant based on electrical behavior
    For example: I want to analyze Data Pin 5, Clock Pin 2… … and all others with < 30 dB of noise reduction impact due to crosstalk
Can the same modeling format support both approaches
efficiently and accurately?
Can the same modeling data…?
Notes: In many cases, the end user *doesn't know* how big or complicated a model is needed or desirable for the package. Our immediate difficulty is in ensuring that simulation is efficient but also accurate.

## Slide 5: Modeling Choices
Package/On-die Model | EDA Vendor | Model Maker | End User
Large, complicated model |  |  | 
Small model that can be shifted/swathed |  |  | 
Many small models that overlap |  |  | 





/

/

Big models are hard to extract but may not be algorithmically challenging to analyze
  Big models are easy to use… if the tool handles connections & terminations of unused nodes
  Big models tend to be slow
Swathing and overlap algorithms may be hard to create and implement
Notes: If I have a massive, 1000 port model…
the end user is guaranteed to be able to analyze the crosstalk on a 1000 pin device
the model maker has a huge burden to extract this correctly
further, if the end user is only interested in a few pins, either the end user or the EDA tool has to intelligently reduce, terminate, etc. this massive model for the end user's purposes, or else you end up with 2 days of simulation to analyze 3 pins.
Similar analyses apply to the other scenarios

## Slide 6: Key Issue
In the current proposals, the model maker controls the “destiny” of the other two segments
  Can I analyze crosstalk accurately for 1000-pin device using only a two-port model?
  Can I quickly generate, instantiate and use a 1000-port model if I may only be interested in two or three connections?
  Ideally, the end user would determine what model is extracted
To be continued…
Notes: If the model maker chooses only to provide a two port model, there's nothing the EDA tool or end user can do to make it cover more or something different than what is supported.
In other words, without swathing or more exotic algorithmic treatments (a burden to the EDA vendor), a two port model can only be used to accurately simulate crosstalk between two ports at a time.

## Slide 7: PREVIOUS MATERIAL (in support of PCB pre-layout needs)

## Slide 8: Intent
Present summary principles behind package model formats in-use today
  To illustrate what a generic, standard format should support
“Format” here refers to both model content and connectivity
Models described are for customer usage, not necessarily internal design or analyses
These assume that the user will create the connections between the PCB, package and buffers
  Scripts/tools may be supplied to assist with connections, using the assumptions documented here
This is not an exhaustive description of formats currently in-use across groups

## Slide 9: Package Model Format Summary (SerDes)
Behavioral/electrical – structural data is not provided
Separate models usually provided per interface
  Further separated by TX vs. RX usage
Six-line, three-differential-pair structure, as crosstalk is critical
SPICE subcircuit of subcircuits
  May includes via, routing, ball, etc. as separate subcircuits
  Mix of tabular W-elements and coupled SPICE circuits
  One reference (no power rails)
W-element lengths passed in through parameters
Separate “corner” subcircuits provided, primarily for impedance and propagation delay variations
  May be more than three corners depending on package structure
Separate information provided on lengths
  Documentation provides length ranges and per-signal lengths
Oriented toward time-domain analysis

## Slide 10: Package Model Format Summary (Memory)
Behavioral/electrical – structural data is not provided
Ten-line structure, as crosstalk is critical (spacing may not be regular)
SPICE subcircuit of subcircuits
  May include via, routing, ball, etc. as separate subcircuits
  Mix of tabular W-elements and coupled SPICE circuits
  One reference (no power rails)
W-element lengths passed in through parameters
Separate “corner” subcircuits provided, primarily for impedance and propagation delay variations
  May be more than three corners depending on package structure
Separate information provided on lengths
  Documentation provides length ranges and per-signal lengths
Oriented toward time-domain analysis

## Slide 11: Thoughts on a Generic Format
Information on the physical structure (e.g., x & y coordinates) should not be required
  This may not be available when models are created
Minimally, a generic format should support
Multiple coupled lines, for crosstalk (not just single-line)
Internal probing points or access
Time-domain analysis
Parameter-passed length information
“Drop-in” for users, “free-form” for makers
  Internal structure can be almost anything
  Buffers and packages may be independent
… and any format must be more compelling to create and use than a SPICE subcircuit!