## Slide 1
Mid-Channel Redriver AMI Model and Simulation
Mahbubul Bari, Maxim Integrated
Fangyi Rao, Agilent Technologies Inc

## Slide 2: Redriver Background
Tx
Rx
channel
Redriver
Tx
Rx
upstream
channel
downstream
channel
Redriver is placed in the middle of the channel to compensate channel loss to support high data rate
It equalizes signals from the upstream channel and retransmits them into the downstream channel
Redriver output is continuously driven by input. No retiming is performed when it retransmits signal
The device can be nonlinear and noisy, thus breaks the linear channel assumption in AMI
Need to extend current standard to include redriver in AMI simulations
Regular channel
Channel with redriver
Notes: Describe the high-level user need.
Summarize in a paragraph or two the key elements of the problem and why this is important to the user. Include some general background information including the user profile. Don’t speculate on the solution just yet.
Why are we doing this development?
Example User Profile (Summarize in the Design Review)
Job
Design Engineer
Large Corporation (Motorola, Ericsson, Nokia…)
Products
Cell Phones, pagers & other communication systems (wired & wireless)
Work Profile
Frequency range: < 3 GHz
General application: Mixed-mode (RF & digital), passive/linear filters and subsystems
Manufacturing technologies: Surface-mount PCB, silicon RFIC and system integration.
Computer Tool Profile
Moderate level of computer literacy
Novice digital filter designer
Uses either Mentor, Cadence, or Synopsys
Wants, Needs, & Expectations
No time for classes – wants easy-to-learn tools
Increasing pressures at work to get designs finished sooner and at/under budget
Wants to eliminate bottlenecks and design process through simpler design process
Wants good online support (examples, tutorials, and help tools)

## Slide 3: Redriver AMI Model
Rx analog
model (IBIS)
Redriver AMI model consists of two back-to-back regular AMI models that represent receiving and transmitting parts of the device.
Each half model has its own .ami and .dll (or .so) files.
Both file pairs are reference in the same .ibs file. The .ami and .dll files of the Rx part are specified under the [Algorithmic Model] keyword in the Rx model section of the .ibs file. The .ami and .dll files of the Tx part are specified under the [Algorithmic Model] keyword in the Tx model section.
Signal flow is from Rx analog to Rx algorithmic to Tx algorithmic to Tx analog
Rx analog model represents input termination.
Looking from Rx analog, the Rx algorithmic block has infinite impedance.
Tx analog represents output impedance.
Looking from Tx analog, Tx algorithmic block is an ideal voltage source.
Rx algorithmic
model (AMI dll)
Tx analog
model (IBIS)
Tx algorithmic
model (AMI dll)
Rx input
Rx output/Tx input
Tx output
electrical isolation
Rx AMI model
Tx AMI model
Redriver AMI model
upstream
channel
downstream
channel
electrical isolation
Notes: Describe the high-level user need.
Summarize in a paragraph or two the key elements of the problem and why this is important to the user. Include some general background information including the user profile. Don’t speculate on the solution just yet.
Why are we doing this development?
Example User Profile (Summarize in the Design Review)
Job
Design Engineer
Large Corporation (Motorola, Ericsson, Nokia…)
Products
Cell Phones, pagers & other communication systems (wired & wireless)
Work Profile
Frequency range: < 3 GHz
General application: Mixed-mode (RF & digital), passive/linear filters and subsystems
Manufacturing technologies: Surface-mount PCB, silicon RFIC and system integration.
Computer Tool Profile
Moderate level of computer literacy
Novice digital filter designer
Uses either Mentor, Cadence, or Synopsys
Wants, Needs, & Expectations
No time for classes – wants easy-to-learn tools
Increasing pressures at work to get designs finished sooner and at/under budget
Wants to eliminate bottlenecks and design process through simpler design process
Wants good online support (examples, tutorials, and help tools)

## Slide 4: Redriver AMI Model (Cont’d)
Rx AMI_Init takes upstream channel impulse matrix as input. Tx AMI_Init takes downstream channel impulse matrix as input.
Rx algorithmic model’s output waveform is the input signal to the Tx algorithmic model.
Tx analog is continuously driven by Tx algorithmic output waveform instead of digital trigger events as in a regular IBIS output model.
Tx analog is expected to describe an analog circuit as oppose to the conventional D/A converter.
If Rx DLL generates clock times, they will be ignored by simulator.
Jitter parameters in a redriver model are ignored. Device noise can be modeled in AMI_GetWave.
Redriver can be cascaded in a channel.
Notes: Describe the high-level user need.
Summarize in a paragraph or two the key elements of the problem and why this is important to the user. Include some general background information including the user profile. Don’t speculate on the solution just yet.
Why are we doing this development?
Example User Profile (Summarize in the Design Review)
Job
Design Engineer
Large Corporation (Motorola, Ericsson, Nokia…)
Products
Cell Phones, pagers & other communication systems (wired & wireless)
Work Profile
Frequency range: < 3 GHz
General application: Mixed-mode (RF & digital), passive/linear filters and subsystems
Manufacturing technologies: Surface-mount PCB, silicon RFIC and system integration.
Computer Tool Profile
Moderate level of computer literacy
Novice digital filter designer
Uses either Mentor, Cadence, or Synopsys
Wants, Needs, & Expectations
No time for classes – wants easy-to-learn tools
Increasing pressures at work to get designs finished sooner and at/under budget
Wants to eliminate bottlenecks and design process through simpler design process
Wants good online support (examples, tutorials, and help tools)

## Slide 5: Example of Redriver IBIS File
…
|**************************************
| Rx Model
|**************************************
[Model] max3997_rx
Model_type Terminator
…
[Algorithmic Model]
Executable Windows_VisualStudio_32 max3997_rx.dll max3997_rx.ami
Executable linux_gcc_32 max3997_rx.so max3997_rx.ami
[End Algorithmic Model]
…
[END]
|**************************************
| Tx Model
|**************************************
[Model] max3997_tx
Model_type Output
…
[Algorithmic Model]
Executable Windows_VisualStudio_32 max3997_tx.dll max3997_tx.ami
Executable linux_gcc_32 max3997_tx.so max3997_tx.ami
[End Algorithmic Model]
…
[END]
Notes: Describe the high-level user need.
Summarize in a paragraph or two the key elements of the problem and why this is important to the user. Include some general background information including the user profile. Don’t speculate on the solution just yet.
Why are we doing this development?
Example User Profile (Summarize in the Design Review)
Job
Design Engineer
Large Corporation (Motorola, Ericsson, Nokia…)
Products
Cell Phones, pagers & other communication systems (wired & wireless)
Work Profile
Frequency range: < 3 GHz
General application: Mixed-mode (RF & digital), passive/linear filters and subsystems
Manufacturing technologies: Surface-mount PCB, silicon RFIC and system integration.
Computer Tool Profile
Moderate level of computer literacy
Novice digital filter designer
Uses either Mentor, Cadence, or Synopsys
Wants, Needs, & Expectations
No time for classes – wants easy-to-learn tools
Increasing pressures at work to get designs finished sooner and at/under budget
Wants to eliminate bottlenecks and design process through simpler design process
Wants good online support (examples, tutorials, and help tools)

## Slide 6: Redriver Simulation Flow
v_rx_in = input_to_upstream_channel * Imp_upstream
Rx algorithmic model processes v_rx_in and returns v_rx_out
Tx algorithmic model processes v_rx_out and returns v_tx_out
output_of_downstream_channel = v_tx_out * Imp_downstream
Redriver
Rx analog
model
Rx algorithmic
model (AMI dll)
Redriver
Tx analog
model
Tx algorithmic
model (AMI dll)
v_rx_in
v_rx_out
v_tx_out
upstream
channel
downstream
channel
Imp_downstream
Rx analog
model
Tx analog
model
Imp_upstream
Notes: Describe the high-level user need.
Summarize in a paragraph or two the key elements of the problem and why this is important to the user. Include some general background information including the user profile. Don’t speculate on the solution just yet.
Why are we doing this development?
Example User Profile (Summarize in the Design Review)
Job
Design Engineer
Large Corporation (Motorola, Ericsson, Nokia…)
Products
Cell Phones, pagers & other communication systems (wired & wireless)
Work Profile
Frequency range: < 3 GHz
General application: Mixed-mode (RF & digital), passive/linear filters and subsystems
Manufacturing technologies: Surface-mount PCB, silicon RFIC and system integration.
Computer Tool Profile
Moderate level of computer literacy
Novice digital filter designer
Uses either Mentor, Cadence, or Synopsys
Wants, Needs, & Expectations
No time for classes – wants easy-to-learn tools
Increasing pressures at work to get designs finished sooner and at/under budget
Wants to eliminate bottlenecks and design process through simpler design process
Wants good online support (examples, tutorials, and help tools)