## Slide 1: Tx_Init_Optimizes
Walter Katz
Signal Integrity Software, Inc.
IBIS-ATM
April 1, 2014

## Slide 2: Overview
How Things Work Today
Why Tx Optimizing Itself is Wrong
How to Fix It
Could Make Tx_Init_Optimizes Usage Info or Usage In
Current Flows Do Not Need to Change
How Current Flows can be Simplified
Does not Solve Tx GetWave Only, Rx Init Only

## Slide 3: How Things Work Today
The Tx AMI_Init function may or may not change its filter setting based on the channels Impulse Response
The EDA tool has no information from the .ami file if the Tx AMI_Init function will or will not change its equalization based on the channels Impulse Response
The Redriver statistical flow in the current IBIS 6.0 standard is incorrect.

## Slide 4: Why Tx Optimizing Itself is Wrong
No silicon does this (How can it?)
Very few Tx AMI models do it.
The Tx and Rx equalization should be optimized together
It only makes sense if the Rx model has no equalization
Optimizing the Tx to open the eye at the input to the Rx caused the Rx DFE to undo what the Tx did – causing reduced signal to noise at the Rx latch.

## Slide 5: How to Fix It
To maintain backward compatibility with existing flows, IBIS 7 should add a new required AMI Reserved Parameter “Tx_Init_Optimizes”
(Type Boolean) (Usage Info)
If True then Tx AMI_Init does change its filter equalization based on the impulse response of the channel.
If False then Tx AMI_Init does not change its filter equalization based on the impulse response of the channel.

## Slide 6: Could Make Tx_Init_Optimizes Usage Info or Usage In
(Usage Info) (Value True)
  Tx Init does alter equalization based on IR input
(Usage Info) (Value False)
  Tx Init does not alter equalization based on IR input
(Usage In) (List False True)
  EDA tool (User) choose True or False which is input to Tx Init.
  Tx Init does what it is told.
    If True, then Tx Init does alter equalization based on IR input
    If False, then Tx Init does not alter equalization based on IR input

## Slide 7: Current Flows Do Not Need to Change
The current flows are agnostic to whether the Tx AMI_Init function changes its filter equalization based on the impulse response of the channel.
The current flows can be significantly simplified if Tx_Init_Optimizes is False.
Also note that if Tx_Init_Optimizes is False the Init flow and GetWave flow are the same.

## Slide 8: How Current Flows can be Simplified
Input to Tx Init
  Unit Impulse Response
Input to Rx Init
  Output of Tx Init convolved with Impulse Response of Channel
Input to Tx GetWave
  Digital Stimulus
Input to Rx GetWave
    Output of Tx GetWave convolved with Impulse Response of Channel

## Slide 9: Does not Solve Tx GetWave Only, Rx Init Only
Rx Init Only Requires an Impulse Response with the Tx equalization and Channel Impulse Response combined.
Tx_Init_Optimizes only tells how the Tx Init equalization is determined, totally academic if the Tx Init_Returns_Impulse is False.