## Slide 1: Backchannel Issues
Walter Katz
Signal Integrity Software, Inc.
IBIS-ATM
April 8, 2014

## Slide 2: Overview
Functionality that “Backchannel” Should Support
What Standards say About Trainable Tx
Tx Buffer Configuration
The System Integrator Problem
Recommendations

## Slide 3: Functionality that “Backchannel” Should Support
Will this Rx training algorithm, with this Tx, with this channel find a solution, and how good will time domain training solution be?
What is the optimal solution with this Rx, with this Tx, with this channel?
What presets should the BIOS set when starting training?
An Rx DLL and AMI ASCII files should work with multiple Tx DLL and AMI ASCII files from different vendors.
An Tx DLL and AMI ASCII files should work with multiple Rx DLL and AMI ASCII files from different vendors.

## Slide 4: What Standards say About Trainable Tx
Standards require at least one pre-cursor tap
  They allow two or more pre-cursor taps.
Standards require at least one post-cursor tap
  They allow two or more post-cursor taps.
Standards specify min and max coefficients for each pre and post cursor tap.
  Standards allow Tx to be capable of a wider range of coefficients for each pre and post cursor tap.
Standards specify a min and max coefficient step size for each pre and post cursor tap.
Standards specify a min and max peak to peak voltage output at Tx into a “standard load”.

## Slide 5: Tx Buffer Configuration
A Tx buffer is configured by setting a register with bits that control impedance, peak to peak voltage swing, and index values for each tap.
There is a mapping from these register bits to an actual impedance, peak to peak voltage swing, a tap index and coefficient for each tap.
This mapping can be complex, non-linear, and can have combinations of settings that are not valid.

## Slide 6: The System Integrator Problem
Consider a Controller with a PCIe-Gen3 interface. At startup, the Controller BIOS determines that a specific Device is plugged in (which in general is a different IC Vendor then the Controller).
The Controller BIOS must choose a preset for all of the Device Tx buffers and a preset for all of the Controller Tx buffers.
How is this information determined?

## Slide 7: Recommendations
New Tx Reserved Parameters
  Tx Peak to Peak Voltage, Tap Indexes, Tap Increment and Tap Coefficients
  Describe Tx ability to support GetWave input of Tap Indexes, Tap Increment and Coefficients
  Tell Tx Init and GetWave to map Tap Index to Tap Coefficients or Tap Coefficients to Tap Index
  Clearly identify to EDA tool when Tx Init optimizes or does not optimize its own taps
  Note, the IC Vendors needs to independently supply a utility to the User to convert Tap Indexes to Register values. This is outside the scope of IBIS AMI.
Add method to define presets
Allow Rx Init to Train Tx Tap Coefficients
Make .bci file a Property of just Rx
  Tx become training protocol agnostic
  Eliminate .bci file, and just include in Rx .ami file