## Slide 1: Backchannel, Training and Co-Optimization BIRD Introduction and Flows
Walter Katz
Signal Integrity Software, Inc.
IBIS-ATM
May 13, 2014

## Slide 2: Overview
Purpose of this Presentation
Backchannel Definitions
Training Makes Assumptions About Tx Silicon
Tx Silicon Never Optimizes Itself
How Training Really Happens
Tx .ami File Enhancements
Rx .ami File Enhancements
Training Flow

## Slide 3: Purpose of this Presentation
In order to operate optimally a SerDes channel must be configured with a Tx and Rx configuration consisting of Tx transmit taps and Rx CTLE and Rx DFE taps. The Rx silicon can automatically optimize its DFE taps and may sometime be able to optimize its CTLE. (Note the term DFE here is used generically to encompass any Rx equalization technique.)
The optimal configuration can either be determined by EDA tools varying the Tx tap coefficients blindly, intelligently, or using the Rx AMI model to vary the Tx tap coefficients. The later is called Training or Backchannel. The former is called Co-Optimization.
These IBIS AMI enhancements support Rx training, Rx controlled optimization and EDA tool controlled optimization.

## Slide 4: Backchannel Definitions
Reading 802.3 and PCIe-3 training specification will make your head spin
In PCIe-3
  A channel consist of a Tx/Rx
  A Lane is a pair of Tx/Rx and Rx/Tx channels, one for transmission and one pair for reception. A by-N Link is composed of N Lanes.
Training may be controlled by component software or can be done autonomously by a Lane or Link.
An Rx on component A communicates to its Tx on component B using its lanes paired channel.

## Slide 5: Training Makes Assumptions About Tx Silicon
Tx is has FFE equalization
One pre cursor tap required (more optional)
One post cursor tap required (more optional)
Standard specifies presets
Rx recommends changes to pre and post tap Coefficients (Tx silicon never optimizes itself)
Protocol must convert Coefficient to Index changes (and must know how)
Protocol may initialize channel to preset or optimized tap coefficients from simulation

## Slide 6: Three Representations of Tx Taps
Hardware Registers
  Hardware specific, often no simple relationship between hardware register contents and either Tap Indexes or Coefficients
Tap Indexes
  Integer range for each tap
  Ranges typically go from 0 to 7, 15, 31 or 63
  Often different ranges for each tap
Tap Coefficients
  Floating point number for each tap
  Sum of absolute values either 1 or Peak to Peak Voltage
Training/Co-optimization deal with Indexes and Coefficients

## Slide 7: Tx Silicon Never Optimizes Itself
How could it?
Ability of Tx AMI_Init was designed to optimize itself based on knowing impulse response of channel.
Optimizing a Tx based on IR of channel was OK at 3Gpbs, but has been proven invalid >=6Gbps
The feature of Tx Init optimizing Tx taps based on the channel impulse response has complicated AMI flows considerably and unecessarily.

## Slide 8: How Training Really Happens
Controller sets Tx and Rx presets Based on Channel Loss, Simulation, …
  Tx Tap Indexes (or coefficients)
  Rx CTLE Index (some Rx optimize their own CTLE)
Controller sends PRBS pattern on Tx
After ~thousand(s?) of UI, Rx tells controller to change Tx taps
  PCIe – new pre and post tap coefficients
  KR – increment or decrement pre and post indexes
  Tap changes maintain peak to peak voltage
Controller converts Rx request to new Tx tap Indexes (or coefficients) and Rx CTLE Index
Controller updates Tx Taps and Rx CTLE
Go To 2.

## Slide 9: Can We Use Existing Tx Models?
It would be helpful if only the Rx DLL needs to be changed to support training/co-optimization
Idea is to add Reserved Parameters to describe the Tx to the Rx, without changing how Tx DLL operates
  E.G. Do not need reserved tap names, just need a reserved parameter that points to the existing tap parameter
Advanced Tx can enable optimization during time domain simulations
Rx Init can do time domain training without Tx having time domain training capability

## Slide 10: Tx .ami Reserved Parameters
Tx_Peak_to_Peak_Voltage_Parameter
  (Type String) (Usage Info)
  Model Specific Tx_Peak_to_Peak_Voltage Parameter
Tx_Tap_Coefficient_Parameter
  (Type String) (Usage Info)(Value “My_Tap_Coefficient”)
  Model Specific Coefficient values Parameter
Tx_Tap_Index_Parameter
  (Type String) (Usage Info)
  Model Specific Index values Parameter
Tx_Tap_Increment_Parameter
  (Type Tap)(Usage InOut)
  Taps with Increment values
Tap_Conversion
  (Usage In) (Type Boolean) (List True False)
  True converts Tx_Tap_Coefficients to Tx_Tap_Index
  False converts Tx_Tap_Index to Tx_Tap_Coefficients

## Slide 11: Tx .ami Reserved Parameters(cont)
Tx_Tap_Coefficient_Ranges
  (Type Integer Float Float) (Usage Info)
  Table with coefficient ranges for each tap
Tx_Tap_Index_Ranges
  (Type Integer Integer Integer ) (Usage Info)
  Table with index ranges for each tap
Tx_Optimization_Mode
(Tx_Optimization_Mode (List “Manual” “Auto” “Co-Optimize”)
(Usage In) (Type String) (Description “
  Manual: Tx Equalization will be based on Tx parameter inputs
  AMI_Init will not alter the Tx equalization
  AMI_GetWave will not alter the Tx equalization
  Auto: Tx Equalization will be based on input impulse response
  AMI_GetWave will not alter the Tx equalization
  Co-Optimize Initial Tx equalization will be based on Tx parameter inputs
  AMI_Init will not alter the Tx equalization
  AMI_GetWave will alter the Tx equalization based on inputs”))

## Slide 12: Tx .ami Model Specific Parameters
My_Peak_to_Peak_Voltage
  (Type Tap) (Usage InOut)
  Tx Peak to Peak Voltage
My_Tap_Coefficient
  (Type Tap) (Usage InOut)
  Taps with Coefficient values
  Sum of absolute values of taps = 1.
My_Tap_Index
  (Type Tap)(Usage InOut)
  Taps with Index values
My_Tap_Increment
  (Type Tap)(Usage InOut)
  Taps with Increment values

## Slide 13: Rx .ami Info Reserved Parameters
Rx_Init_Optimizes_Tx
Rx_GetWave_Optimizes_Tx
Max_Training_Bits
Pre_Amble (This is really a Link function)
Training_Pattern (Just need PRBS<n>)
Post_Amble (This is really a Link function)
Rx_Tap_Coefficient_Parameter
Rx_Tap_Index_Parameter
Rx_Tap_Increment_Parameter
Training True|False

## Slide 14: Rx .ami In and InOut Reserved Parameters
InOut
  Training True|False
In
  Tx_Tap_Coefficient_Ranges
    (Type Integer Float Float) (Usage Info)
    Table with coefficient ranges for each tap
    EDA tool puts Tx data here
  Tx_Tap_Index_Ranges
    (Type Integer Integer Integer ) (Usage Info)
    Table with index ranges for each tap
    EDA tool puts Tx data here

## Slide 15: Rx .ami Model Specific Parameters
InOut
  This_Tx_Tap_Coefficient
  This_Tx_Tap_Index
  This_Tx_Tap_Increment

## Slide 16: Rx Can Support Multiple Protocols
Rx_Init_Optimizes_Tx
Rx_GetWave_Optimizes_Tx
Max_Training_Bits
Training True|False
Training_Protocol (List “PCIe-G3” “802.3KR”)
(PCIe-G3
  (Training_PRBS (Value 11))
(802.3KR
  (Training_Pattern (Value “PRBS21”))

## Slide 17: PCIe-3 Presets Not clear where this should be defined
Table 4-3: Transmitter Preset Encoding
  Encoding De-emphasis (dB) Preshoot (dB)
  0000b -6 0
  0001b -3.5 0
  0010b -4.5 0
  0011b -2.5 0
  0100b 0 0 (note this is no equalization!)
  0101b 0 2
  0110b 0 2.5
  0111b -6 3.5
  1000b -3.5 3.5
  1001b 0 3.5
  1010b See description above. See description above.
  1011b through 1111b Reserved
Table 4-4: Receiver Preset Hint Encoding
  Encoding Receiver Preset Value
  000b -6 dB
  001b -7 dB
  010b -8 dB
  011b -9 dB
  100b -10 dB
  101b -11 dB
  110b -12 dB
  111b Reserved

## Slide 18: Training Flow - Verify presets
EDA tool picks presets
EDA tool runs normal flow with no training to verify that channel has BER < 1.0E-5
  If not, repeat these steps to find preset with best BER
802.3bj COM (Channel Operating Margin) uses brute force technique to evaluate channel with every possible Tx tap configuration, and an ideal 14 UI Rx equalization.

## Slide 19: Init Training Flow – Tx Init
Tx_Init Input
  Tx_Tap_Coefficient or Tx_Tap_Index set to preset
  Tap_Conversion
    True if Tx_Tap_Coefficient is preset
    False if Tx_Tap_Index is preset
  Impulse Response Input is Channel Impulse Response
Tx_Init Output
  Tap_Conversion True
    Tx_Tap_Index (from input Tx_Tap_Coefficient)
    Tx_Tap_Coefficient (corrected from actual Index)
  Tap_Conversion False
    Tx_Tap_Coefficient (Tx_Tap_Index is unchanged)
  Channel with Preset Tx Equalization

## Slide 20: Init Training Flow – Rx Init
Rx_Init Input
  Tx_Tap_Coefficient
  Tx_Tap_Index
  Tx_Tap_Coefficient_Ranges
  Tx_Tap_Index_Ranges
  CTLE preset
  Training True
  Channel Impulse Response with Tx_Tap_Coefficient Equalization
Rx_Init Output
  Either
    Tx_Tap_Index
    Tx_Tap_Coefficient
  CTLE
  Equalized Impulse Response, including
    Channel Impulse Response
    Tx Equalization
    Rx Equalization

## Slide 21: Init Training Flow – Tx Init Again?
After Rx Init determines optimum Tx tap coefficients, Tx Init can be called again
  Tx Init can verify/correct Tx tap coefficients
  Tx Init can convert Tx tap coefficients to Tx tap indexes
  Tx Init can create a new Impulse Response of Channel modified by Tx equalization
Rx Init can be called again with refined equalized channel, and Rx Init can then be called upon to do normal channel analysis.
EDA tool may choose to continue with training or no training GetWave time domain flow.

## Slide 22: Time Domain Training Flow – Tx GetWave Input
Tx_GetWave Input
  Tx_Tap_Coefficient or Tx_Tap_Index from Rx Init statistical optimization or from User/EDA tool selected Preset
    If Tx_Tap_Coefficient
      EDA tool corrects based on Tx_Tap_Ranges
      Tap_Conversion set to True
    If Tx_Tap_Index
      EDA tool corrects based on Tx_Tap_Ranges
      Tap_Conversion set to False
  Stimulus
    Pre-amble followed by Training_Pattern

## Slide 23: Time Domain Training Flow – Tx GetWave
Note that Tx_GetWave may not accept all Tap coefficients/indexes/increments, and may alter them
Tx_GetWave Output
  Tap_Conversion True
    Tx_Tap_Index
    Tx_Tap_Coefficient
  Tap_Conversion False
    Tx_Tap_Coefficient
  Waveform: Stimulus including Tx Equalization
EDA tool convolves Waveform with Channel to form waveform input to Rx_GetWave

## Slide 24: Time Domain Training Flow – Rx GetWave
Rx_GetWave Input
  One or more of following
    Tx_Tap_Coefficient
    Tx_Tap_Index
    Tx_Tap_Increment
    CTLE
  Training True
  Waveform from previous step
Rx_GetWave Output
  One or more of following
    Tx_Tap_Index
    Tx_Tap_Coefficient
    Tx_Tap_Increment
    CTLE
  Waveform including Rx Equalization
  Training True|False
    True, go to Training Flow – Tx GetWave Input
    False, go to Training Flow - Ended

## Slide 25: Time Domain Training Flow - Ended
Tx_GetWave Input
  Tx Tap Coefficient , Index, or Increment from Rx
    If Tx_Tap_Coefficient
      EDA tool corrects based on Coefficient Ranges
      Tap_Conversion set to True
    If Tx_Tap_Index (or Incremented Index)
      EDA tool corrects based on Index Ranges
      Tap_Conversion set to False
  Stimulus
    Post-amble followed by simulation stimulus

## Slide 26: Time Domain Training Flow – Ended (cont)
Tx_GetWave Output
  Tap_Conversion True
    Tx_Tap_Index
    Tx_Tap_Coefficient
  Tap_Conversion False
    Tx_Tap_Coefficient
  Waveform: Stimulus including Tx Equalization
EDA tool convolves Waveform with Channel to form waveform input to Rx_GetWave

## Slide 27: Time Domain Training Flow Ended –Statistical Channel Analysis
From the last call to Tx GetWave we have either:
  Tx_Tap_Index(s)
  Tx_Tap_Coefficient(s)
Remember the trained configuration of Tx and Rx models.
Close Tx and Rx DLLs
Run Tx Init then Rx Init in the normal way, but using the remembered Tx and Rx configuration.

## Slide 28: Time Domain Training Flow Ended – Time Domain Channel Analysis
Rx_GetWave Input
  Training False
  Waveform from previous step
Rx_GetWave Output
  Waveform including Rx Equalization
Tx_GetWave Input
  Stimulus
Tx_GetWave Output
  Waveform including Tx Equalization
  EDA tool convolves Waveform with Channel to form waveform input to Rx_GetWave
Go to Rx_GetWave Input above