## Slide 1: IBIS-AMI and Direction Indication
February 17, 2015
Michael Mirmak

## Slide 2: Disclaimers
INFORMATION IN THIS DOCUMENT IS PROVIDED IN CONNECTION WITH INTEL PRODUCTS. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. EXCEPT AS PROVIDED IN INTEL'S TERMS AND CONDITIONS OF SALE FOR SUCH PRODUCTS, INTEL ASSUMES NO LIABILITY WHATSOEVER AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO SALE AND/OR USE OF INTEL PRODUCTS INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
UNLESS OTHERWISE AGREED IN WRITING BY INTEL, THE INTEL PRODUCTS ARE NOT DESIGNED NOR INTENDED FOR ANY APPLICATION IN WHICH THE FAILURE OF THE INTEL PRODUCT COULD CREATE A SITUATION WHERE PERSONAL INJURY OR DEATH MAY OCCUR. Intel may make changes to specifications and product descriptions at any time, without notice. Designers must not rely on the absence or characteristics of any features or instructions marked "reserved" or "undefined." Intel reserves these for future definition and shall have no responsibility whatsoever for conflicts or incompatibilities arising from future changes to them. The information here is subject to change without notice. Do not finalize a design with this information.
The products described in this document may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.
Contact your local Intel sales office or your distributor to obtain the latest specifications and before placing your product order.
Copies of documents which have an order number and are referenced in this document, or other Intel literature, may be obtained by calling 1-800-548-4725, or go to: http://www.intel.com/design/literature.htm%20
Intel, Xeon, and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
Copyright © 2015, Intel Corporation. All Rights Reserved.
* Other names and brands may be claimed as the property of others.

## Slide 3: Disclaimers
This presentation is the opinion of only one individual and does not represent the policies or opinions of Intel Corporation, its partners or subsidiaries

## Slide 4: The Problem
Analog IBIS I/O
[Model]
I/O Pad*
POWER Clamp Ref.
GND Clamp Ref.
* Differential version not shown
Pullup Ref
Pulldown Ref
"Digital” I/O
Enable
How do we ensure the state of the enable on the analog side is shared and consistent with
the algorithmic side?
Algorithmic
Model
(DLL + .ami)

## Slide 5: Original Proposal to Address the Problem
Add two Reserved_Parameters to post-6.0 IBIS, for .ami file
  AMI_Model_Type
    String literal, of type Info
    I/O, 3-state, Tx, Rx
    Defines whether the buffer supports bi-directional or uni-directional operation
    “What the model can do”
  AMI_Model_Direction
    String literal list, of type Info or In
    Available options are Ignore, Tx, and Rx
    Only two of these permitted for any one model
    Related to AMI_Model_Type
    State is assumed to change for I/O or 3-state models based on situation, as defined by user
    “What the model is doing, right now”

## Slide 6: Three Options for IBIS-AMI Direction Support
These two parameters are not enough
  For example, do we need I/O DLLs? What would it look like?
Need consensus on one of three potential approaches
1
2
3
Require a single DLL for I/O buffers that supports both TX and RX operations
Add [Algorithmic Model Selector] to [Model]
Selector parameter identifies direction for each model
User selects, through EDA tool, the Algorithmic Model to use for any given simulation
Change [Model] to allow multiple instances of [Algorithmic Model]
Add sub-parameter to [Algorithmic Model] for direction

## Slide 7: Option 1: Require Unified DLL (“Do Nothing”)
New directional AMI models must be able to change behavior based on state of AMI_Model_Direction
  DLLs and .ami files must contain everything needed to operate in states allowed by AMI_Model_Direction
Advantages
No changes to tools or existing models
No new functions
No syntax changes outside of AMI_Model_Type and AMI_Model_Direction
Disadvantages
No way to check DLL compatibility with new direction features
May be hard to program
Extra parsing needed to check .ami compatibility

## Slide 8: Option 2: Updated [Model], [Alg. Model]
Remove restriction that [Algorithmic Model] appear only once under [Model]
  “… and it may appear only once for each [Model] keyword in a .ibs file”
Add subparameter “Direction” under [Algorithmic Model]
EDA tools use [Algorithmic Model] with appropriate direction depending on state of enable node
Parser must check that Model_type, [Algorithmic Model] direction(s), and .ami file AMI_Model_Type are consistent
No changes required to existing models and associated tool support

## Slide 9: Option 2 Example
[Model] My_Bidirectional_Model
Model_type I/O
… [Algorithmic Model] | Direction TX | new with post-6.0 IBIS; must be consistent with [Model_Type]
Executable Windows_VisualStudio_32 tx_getwave.dll tx_getwave_params.ami Executable Solaris_cc_32 libtx_getwave.so tx_getwave_params.ami | [End Algorithmic Model]
[Algorithmic Model] | Direction RX | new with post-6.0 IBIS; must be consistent with [Model_Type]
Executable Windows_VisualStudio_32 rx_getwave.dll rx_getwave_params.ami Executable Solaris_cc_32 libtx_getwave.so rx_getwave_params.ami | [End Algorithmic Model] Model_type and Direction must be consistent
Direction and AMI_Model_Type must be consistent
Must have one [Algorithmic Model] of each Direction permitted by the Model_Type/AMI_Model_Type
How many should we allow? How to indicate which one to use?

## Slide 10: Option 3: [Algorithmic Model Selector]
Add [Algorithmic Model Selector] keyword
  Hierarchically between [Model] and [Algorithmic Model]
  If not present, then one and only one [Algorithmic Model] must appear
  Allows automatic selection by tool/user between Tx and Rx subsets as appropriate
Remove restriction that [Algorithmic Model] appear only once under [Model]
  “… and it may appear only once for each [Model] keyword in a .ibs file”
Selector control is based on new, optional argument for [Algorithmic Model] keyword
Requires re-coding of [Algorithmic Model] keyword in tools

## Slide 11: Option 3 Example
[Model] My_Bidirectional_Model
Model_type I/O
… [Algorithmic Model Selector]
| Fields include Model_name, Model_direction, comment; are others needed?
TX_1 Tx Transmitter algorithmic Model
RX_1 Rx Receiver algorithmic Model #1
RX_2 Rx Receiver algorithmic Model #2
[End Algorithmic Model Selector]
[Algorithmic Model] TX_1 | Executable Windows_VisualStudio_32 tx_getwave.dll tx_getwave_params.ami Executable Solaris_cc_32 libtx_getwave.so tx_getwave_params.ami | [End Algorithmic Model]
[Algorithmic Model] RX_1 | Executable Windows_VisualStudio_32 rx_getwave.dll rx_getwave_params.ami Executable Solaris_cc_32 libtx_getwave.so rx_getwave_params.ami | [End Algorithmic Model]
[Algorithmic Model] RX_2 …

## Slide 12: Option 3 Rules
Model_type and Selector Model_direction field must be consistent
Model_direction field and AMI_Model_Type must be consistent
Must have at least one [Algorithmic Model] of each Direction permitted by the Model_Type/AMI_Model_Type
If [Algorithmic Model Selector] is not present, no [Algorithmic Model] argument is needed or permitted

## Slide 13
Which one shall we adopt?

## Slide 14: New Table
In the Feb. 10 IBIS-ATM meeting, Radek Biernacki suggested adding a “Table 2” to the directionality BIRD proposal
This would cover how Reserved_Parameters would interact with the new ATM directionality parameters
This table is shown on the next two pages

## Slide 15: New Table for TX and RX Parameter Interactions
Reserved Parameter | AMI_Model_Types Permitted
Rx_Clock_PDF | Rx, I/O
Rx_Clock_Recovery_DCD | Rx, I/O
Rx_Clock_Recovery_Dj | Rx, I/O
Rx_Clock_Recovery_Mean | Rx, I/O
Rx_Clock_Recovery_Rj | Rx, I/O
Rx_Clock_Recovery_Sj | Rx, I/O
Rx_DCD | Rx, I/O
Rx_Dj | Rx, I/O
Rx_Noise | Rx, I/O
Rx_Receiver_Sensitivity | Rx, I/O
Rx_Rj | Rx, I/O
Rx_Sj | Rx, I/O
Tx_DCD | Tx, I/O, 3-state
Tx_Dj | Tx, I/O, 3-state
Tx_Jitter | Tx, I/O, 3-state
Tx_Rj | Tx, I/O, 3-state
Tx_Sj | Tx, I/O, 3-state
Tx_Sj_Frequency | Tx, I/O, 3-state

## Slide 16: New Table for TX and RX Parameter Interactions (2)
Reserved Parameter | AMI_Model_Types Permitted
DLL_ID | All
DLL_Path | All
Supporting_Files | All
AMI_Version | All
GetWave_Exists | All
Ignore_Bits | All
Init_Returns_Impulse | All
Max_Init_Aggressors | All
Use_Init_Output | n/a (will not be combined legally)