## Slide 1: IBIS Interconnect BIRD Draft 2
Walter Katz
Signal Integrity Software, Inc.
IBIS Summit, DesignCon
Santa Clara, CA
January 30, 2015

## Slide 2: Overview
IBIS Interconnect Task Group
Models Represent Package and On-Die Interconnect
On Die, Package, Supply and Signal Interconnect can be Combines or Kept Separate
Similar Approach for Both IBIS and EBD
Pre and Post Layout IBIS Files
IBIS Interconnect Model Terminals
Differential Signal (I/O) Model Terminals
Supply Model Terminals
Graphics Showing Model Terminals
Corners
Reconciling Legacy IBIS Models and [External Model][Interconnect Model]
Next Steps

## Slide 3: IBIS Interconnect Task Group
Meets Wednesdays 8AM PDT
http://www.eda.org/ibis/interconnect_wip/
Major Contributors
  Altera David Banas
  Cadence Design Systems Bradley Brim
  Intel Corp Michael Mirmak
  Keysight Technologies Radek Biernacki
  Mentor Graphics Arpad Muranyi
  Micron Technology Justin Butterfield, Randy Wolff
  Signal Integrity Software Walter Katz
  Synopsys Rita Horner
  Teraspeed Labs Bob Ross

## Slide 4: Models Represent Package and On-Die Interconnect
Languages Supported
  IBIS-ISS
  Touchstone
Model Terminals
  Pins
  Die Pads
  Buffer Signals
  Buffer Supplies

## Slide 5: On Die, Package, Supply and Signal Interconnect can be Combines or Kept Separate
Supports separate on-die and package interconnect models and combined on-die and package interconnect models
Independent Supply and Signal Interconnect Models
Coupled Supply and Signal Interconnect Models
Singled Ended and Differential Interconnect Models

## Slide 6: Similar Approach for Both IBIS and EBD
IBIS (.ibs) Interconnect Model Terminals
  Pins ([Pins])
  Die Pads
  Buffers
EBD (.ebd) Interconnect Model Terminals
  Pins ([Pin List])
  reference_designator.pin
  EBD will be a separate BIRD based on the IBIS package BIRD when completed
EBD will be updated as soon as .ibs package BIRD is Finished

## Slide 7: IBIS Interconnect Model Terminals
Pins
Die Pads
  Signal (I/O)
  Supply (POWER and GND)
Buffers
  Signal (I/O)
  Supply
    Pullup Reference
    Pulldown Reference
    Power Clamp Reference
    Ground Clamp Reference
    External Reference

## Slide 8: Pre and Post Layout IBIS Files
Post Layout
  Signal (I/O) Terminals
    Pin, Die Pad and Buffer terminals referenced by Pin_name
  Supply Terminals
    Pin terminals referenced by Pin_name or Signal_name
    Die Pad terminals referenced by Die_Pad_name or Signal_name
    Buffer terminals referenced by Pin_name or Signal_name
Pre Layout
  Signal (I/O) Terminals
    Referenced by Model_name
  Supply Terminals
    Referenced by Signal_name

## Slide 9: Interconnect Model Terminals
Terminal <terminal number> <At Pin|DiePad|Buffer> <ID> <What ID is>
One line per terminal
Supports both Pre and Post Layout
Example Signal (I/O) Terminal records
  Post Layout
    Terminal 1 Pin_A_signal M8
    Terminal 2 Pad_A_signal M8
    Terminal 3 A_signal M8
  Pre Layout
    Terminal 1 Pin_A_signal DQ Model_name
    Terminal 2 Pad_A_signal DQ Model_name
    Terminal 3 A_signal DQ Model_name

## Slide 10: Differential Signal (I/O) Model Terminals
  Post Layout
    Terminal 1 Pin_A_signal M8
    Terminal 2 Pin_A_signal M7
    Terminal 3 Pad_A_signal M8
    Terminal 4 Pad_A_signal M7
    Terminal 5 A_signal M8
    Terminal 6 A_signal M7
  Pre Layout
    Terminal 1 Pin_A_signal_pos DQS Model_name
    Terminal 2 Pin_A_signal_neg DQS Model_name
    Terminal 3 Pad_A_signal_pos DQS Model_name
    Terminal 4 Pad_A_signal_neg DQS Model_name
    Terminal 5 A_signal_pos DQS Model_name
    Terminal 6 A_signal_neg DQS Model_name

## Slide 11: Supply Model Terminals
Post Layout
  Using Pins, Pads and Buffers
    Terminal 1 Pin_A_Signal B1
    Terminal 2 Pin_A_Signal B2
    Terminal 4 A_puref M3
  Using Signal_name and Buffers
    Terminal 1 Pin_A_Signal VDD Signal_name
    Terminal 3 A_puref M3
Pre and Post Layout
  Using Signal_name and “Pin mapping”
    Terminal 1 Pin_A_Signal VDD Signal_name
    Terminal 3 A_Signal VDD Signal_name
  Using Signal_name and “Model_name”
    Terminal 1 Pin_A_Signal VDD Signal_name
    Terminal 3 A_puref DQ Model_name

## Slide 12: Package Terminals Post Layout
A_puref A1
Pullup
Pulldown
Power Clamp
Ground Clamp
C_comp
Model
A_pcref A1
A_gcref A1
A_pdref A1
A_signal
A1
Combined Package and On-Die Model
Pin_A_Signal
A1
Pin_Signal_Name
VSSQ
Pin_Signal_Name
VSS
Pin_A_Signal
B3
Pin_A_Signal
B4

## Slide 13: Package Terminals Post Layout
A_puref A1
Pullup
Pulldown
Power Clamp
Ground Clamp
C_comp
Model
A_pcref A1
A_gcref A1
A_pdref A1
A_signal
A1
Combined Package and On-Die Model
Pin_A_Signal
A1
Pin_Signal_Name
VSSQ
Pin_Signal_Name
VSS
Pin_A_Signal
B3
Pin_A_Signal
B4

## Slide 14: Package Terminals Post Layout
A_puref A1
Pullup
Pulldown
Power Clamp
Ground Clamp
C_comp
Model
On-Die
Model
A_pcref A1
A_gcref A1
A_pdref A1
A_signal
A1
Package
Model
Pad_A_Signal
VDD_pad
Pad_A_Signal
VDDQ_pad
Pad_A_Signal
A1
Pad_Signal_Name
VSSQ
Pad_Signal_Name
VSS
Pin_A_Signal
A1
Pin_Signal_Name
VSSQ
Pin_Signal_Name
VSS
Pin_A_Signal
B3
Pin_A_Signal
B4

## Slide 15: Corners
Parameters can have either a single value or three corner values
It is not clear if we will have a clear definition of the three corners Typ, Min, Max
  If a parameter is a length then Typ, Fast, Slow
  If a parameter is a delay then Typ, Slow, Fast
  If a parameter is an impedance then Typ, Min, Max
Expect it will inherit the existing usage of Typ, Min and Max and will be up to EDA tool on how to apply these corners.
Some “Corner” conditions (e.g. crosstalk) will be handled by [Interconnect Model Selector].

## Slide 16: Reconciling Legacy IBIS Models and [External Model]
[External Model] supports an A_extref terminal which has no analog in “B element” models that use the IV and VT curves.
If new package models has a terminal to an [External Model] A_extref, how should the EDA tool terminate this terminal when using a “B element”?

## Slide 17: Next Steps
The goal is to complete the new package BIRD and formally submit it to the Open Forum by the end of Q1, 2015
Shortly thereafter with a BIRD to enhance EBD to support IBIS-ISS subckts.