## Slide 1: Pin Mapping Key Concepts
From IBIS 6.0…
“The [Pin Mapping] keyword names the connections between POWER and/or GND pins and buffer and/or terminator voltage supply references using unique bus labels. All buses with identical labels are assumed to be connected with an ideal short. Each label must be associated with at least one pin whose model_name is POWER or GND.”

## Slide 2: Key Concepts (cont’d)
“The second column, pulldown_ref, designates the ground bus connections for the buffer or termination associated with that pin. The bus named under pulldown_ref is associated with the [Pulldown] I-V table for non-ECL [Model]s.”
“The third column, pullup_ref, designates the power bus connection for the buffer or termination. The bus named under pullup_ref is associated with the [Pullup] table for non-ECL [Model]s…”

## Slide 3: Pin Mapping in Interconnect BIRD
In Draft 9...
“… all pins with Signal_name VDD [connect to] to all Buffer supply terminals that are connected to Signal_name VDD as described in Pin_mapping.”
“All Pins with Signal_name VDD are shorted together. “
“All Buffer supply terminals that are connected to Signal_name VDD are shorted together”

## Slide 4: Example from Draft 9, P. 13
VDD: Interconnect between VDD Pins and individual buffer Pullup Reference.
  Terminal 1 Pin P1
  Terminal 2 Pin P2
  Terminal 3 Pin P3
  Terminal 4 Pin P4
  Terminal 5 Pin P5
  Terminal 6 Buf_PURef A1
  Terminal 7 Buf_PURef A2
  Terminal 8 Buf_PURef A3
  Terminal 9 Buf_PURef D1

## Slide 5: Proposal
Draft 9 and IBIS [Pin Mapping] agree on shorting of pins associated with a named supply
  [Pin] model_name must be POWER or GND
[Pin Mapping] implies but does not state a direct connection (short) between the buffer supply rail and the pin
Suggestion:
  For traditional interconnects, assume buffer rail/pin short
  For Draft 9 Interconnects([Interconnect Model] present), state that interconnect “sits between” buffer rail and pin
  Pin Mapping rails still shorted to each other
  Pin Mapping pins on named supplies still shorted together

## Slide 6: Additional Issue
From IBIS 6.0…
“If the [Pin Mapping] keyword is present, then the bus connections for EVERY pin listed under the [Pin] keyword must be given.”
Does this prevent effective use of Draft 9 Interconnects?
  Partial interconnect descriptions become impossible