## Slide 1: IBIS Interconnect BIRD Draft 0
Walter Katz
Signal Integrity Software, Inc.
IBIS Summit, DesignCon
January 27, 2015

## Slide 2: Overview
IBIS Interconnect Task Group
Models Represent Package and On-Die Interconnect
On Die, Package, Supply and Signal Interconnect can be Combines or Kept Separate
Similar Approach for Both IBIS and EBD
IBIS Interconnect Model Terminals
Pre and Post Layout IBIS Files
Corners
[Interconnect Model Selector]
[Interconnect Model]
[Begin Model]
Terminal
Terminals
Next Steps

## Slide 3: IBIS Interconnect Task Group
Meets Wednesdays 8AM PDT
http://www.eda.org/ibis/interconnect_wip/
Major Contributors
  Altera David Banas
  Cadence Design Systems Bradley Brim
  Intel Corp Michael Mirmak
  Keysight Technologies Radek Biernacki
  Mentor Graphics Arpad Muranyi
  Micron Technology Justin Butterfield, Randy Wolff
  Signal Integrity Software Walter Katz
  Synopsys Rita Horner
  Teraspeed Labs Bob Ross

## Slide 4: Models Represent Package and On-Die Interconnect
Languages Supported
  IBIS-ISS
  Touchstone
Model Terminals
  Pins
  Die Pads
  Buffer Signals
  Buffer Supplies

## Slide 5: On Die, Package, Supply and Signal Interconnect can be Combines or Kept Separate
Supports separate on-die and package interconnect models and combined on-die and package interconnect models
Independent Supply and Signal Interconnect Models
Coupled Supply and Signal Interconnect Models
Singled Ended and Differential Interconnect Models

## Slide 6: Similar Approach for Both IBIS and EBD
IBIS (.ibs) Interconnect Model Terminals
  Pins ([Pins])
  Die Pads
  Buffers
EBD (.ebd) Interconnect Model Terminals
  Pins ([Pin List])
  reference_designator.pin
  EBD will be a separate BIRD based on the IBIS package BIRD when completed
EBD will be updated as soon as .ibs package BIRD is Finished

## Slide 7: IBIS Interconnect Model Terminals
Pins
Die Pads
  Signal (I/O)
  Supply (POWER and GND)
Buffers
  Signal (I/O)
  Supply
    Pullup Reference
    Pulldown Reference
    Power Clamp Reference
    Ground Clamp Reference
    External Reference

## Slide 8: Interconnect Model Terminals
Terminal <terminal number> Pin|DiePad|Buffer …
One line per terminal
Supports both Pre and Post Layout
Example Terminal records
Terminal 1 Pin Pin_name M8
Terminal 2 Pad Pin_name M8
Terminal 3 Buffer Pin_name M8
Terminal 4 Buffer Pin_name M8 Pullup_Reference
Terminal 5 Pin Model_name DQ
Terminal 6 Pin Model_name DQS Diff_pos
Terminal 8 Pin Model name DQ SE
Terminal 9 Buffer Pin_name M9 Aggressor
Terminal 10 Buffer Pin_name M10 Victim
Terminal 11 Buffer Signal_name VDDQ

## Slide 9: Pre and Post Layout IBIS Files
Post Layout
  Signal (I/O) Terminals
    Pin, Die Pad and Buffer terminals referenced by Pin_name
  Supply Terminals
    Pin terminals referenced by Pin_name or Signal_name
    Die Pad terminals referenced by Die_Pad_name or Signal_name
    Buffer terminals referenced by Pin_name or Signal_name
Pre Layout
  Signal (I/O) Terminals
    Referenced by Model_name
  Supply Terminals
    Referenced by Signal_name

## Slide 10: Corners
File, Subckt and Parameters can have either a single value or three corner values
It is not clear if we will have a clear definition of the three corners Typ, Min, Max
  Can be Typ, Slow, Fast
  Can be Typ, Small Crosstalk, Large Crosstalk
Expect it will inherit the existing usage of Typ, Min and Max and will be up to EDA tool on how to apply these corners.