## Slide 1: IBIS Interconnect BIRD Update
Walter Katz
Signal Integrity Software, Inc.
IBIS Summit, EPEPS
San Jose, CA
October 28, 2015

## Slide 2: Overview
IBIS Interconnect Task Group
Models Represent Package and On-Die Interconnect
On Die, Package, Supply and Signal Interconnect can be Combined or Kept Separate
IBIS Interconnect Model Terminals
Examples

## Slide 3: IBIS Interconnect Task Group
Meets Wednesdays 8AM PDT
http://www.eda.org/ibis/interconnect_wip/
Major Contributors
  Altera David Banas
  Cadence Design Systems Bradley Brim
  Intel Corp Michael Mirmak (Chair)
  Keysight Technologies Radek Biernacki
  Mentor Graphics Arpad Muranyi
  Micron Technology Justin Butterfield, Randy Wolff
  Signal Integrity Software Walter Katz, Mike LaBonte
  Synopsys Rita Horner
  Teraspeed Labs Bob Ross

## Slide 4: Models Represent Package and On-Die Interconnect
Currently IBIS supports lumped coupled RLC models, or lossless uncoupled distributed models.
New modeling will support broadband, coupled, signal interconnect and power distribution models.
Languages Supported
  IBIS-ISS
    IBIS Interconnect SPICE Subcircuit (IBIS-ISS) Specification, Version 1.0, October 7th 2011 http://www.ibis.org/ibis-iss_ver1.0/ibis-iss_ver1_0.pdf
  Touchstone ®
    http://www.ibis.org/touchstone_ver2.0/

## Slide 5: On Die, Package, Supply and Signal Interconnect can be Combined or Kept Separate
Supports separate on-die and package interconnect models and combined on-die and package interconnect models
Independent Supply and Signal Interconnect Models
Coupled Supply and Signal Interconnect Models
Singled Ended and Differential Interconnect Models

## Slide 6: Similar Approach for Both IBIS and EBD
IBIS (.ibs) Interconnect Model Terminals
  Pins ([Pins])
  Die Pads
  Buffers
EBD (.ebd) Interconnect Model Terminals
  A similar approach will be used to update EBD (Electrical Board Description) or EMD (Electrical Module Description) to support broadband, coupled interconnect models

## Slide 7: IBIS Interconnect Model Terminals
Pins
  Pin_name (aka Pin Number)
  Signal_name (assumes signal_name pins shorted)
  Bus_label (allows sub-groups of rail signal_name pins)
Pads (Die/Package Interface)
  Pin_name (aka Pin Number) for I/O connections
  Pad_name for rail connections
  Signal_name (assumes signal_name pads shorted)
  Bus_label (allows sub-groups of rail signal_name pads)
Buffers
  Signal (I/O)
  Rails
    Pin_name and (puref/pdref/pcref/gcref)
    Signal_name (assumes signal_name terminals shorted)
    Bus_label (allows sub-groups of rail buffer terminals)

## Slide 8: Interconnect Model Terminals
<Terminal Number> <Terminal Type> <Qualifier>
  X I/O pin_name
  Y Supply pin_name, signal_name or bus_label
  Z Supply pad_name
Terminal_Type | pin_name | signal_name | bus_label | pad_name
Buffer_I/O | X |  |  | 
Puref | X |  |  | 
Pdref | X |  |  | 
Pcref | X |  |  | 
Gcref | X |  |  | 
EXTref | X |  |  | 
Buffer_rail |  | Y | Y | 
Pad_I/O | X |  |  | 
Pad_rail |  | Y | Y | Z
Pin_I/O | X |  |  | 
Pin_rail | Y | Y | Y | 

## Slide 9: Interconnect Model Examples
[Interconnect Model] DQ1 | IBIS-ISS Model
File_IBIS-ISS DQ.iss DQ
Param Length Value .1
Number_of_Terminals = 2
1 Pin_I/O A1
2 Buffer_I/O A1
[End Interconnect Model]
[Interconnect Model] A1 | Touchstone File Shortcut
File_TS A1.s2p
Number_of_Terminals = 3
1 Pin_I/O A1
2 Buffer_I/O A1
3 Pin_rail signal_name VSS
[End Interconnect Model]

## Slide 10: Full Package, All Pins to All Buffers
A1
P1
P2
P3
P4
G1
G2
G3
G4
A2
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
[Begin Interconnect Model]
…
1 Pin_I/O pin_name A1
2 Pin_rail pin_name P1
3 Pin_rail pin_name P2
4 Pin_rail pin_name P3
5 Pin_rail pin_name P4
6 Pin_rail pin_name G1
7 Pin_rail pin_name G2
8 Pin_rail pin_name G3
9 Pin_rail pin_name G4
10 Pin_I/O pin_name A2
11 Puref pin_name A1
12 Buffer_I/O pin_name A1
13 Pdref pin_name A1
14 Puref pin_name A2
15 Buffer_I/O pin_name A2
16 Pdref pin_name A2
[End Interconnect Model]
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
.subckt AllPinsAllBuffers 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16
Pin
Buffer

## Slide 11: Full Package, All VDD and VSS Pins Shorted All Buffer Rail Connections Shorted on Die
A1
P1
P2
P3
P4
A2
G1
G2
G3
G4
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
1
2
3
4
6
5
7
8
[Begin Interconnect Model]
…
1 Pin_I/O pin_name A1
2 Pin_rail signal_name VDD
3 Pin_I/O pin_name A2
4 Pin_rail signal_name VSS
5 Buffer_I/O pin_name A1
6 Buffer_rail signal_name VDD
7 Buffer_rail signal_name VSS
8 Buffer_I/O pin_name A2
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
.subckt AllPinsRailsShorted 1 2 3 4 5 6 7 8
Pin
Buffer

## Slide 12: Crosstalk Model, Signal I/O Only
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
1
2
3
4
[Begin Interconnect Model]
…
1 Pin_I/O pin_name A1
2 Pin_I/O pin_name A2
3 Buffer_I/O pin_name A1
4 Buffer_I/O pin_name A2
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
.subckt XtalkNoRail 1 2 3 4
Pin
Buffer

## Slide 13: Crosstalk Model, Signal I/O Only, Touchstone Model
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
File_TS xyz.s4p
1 Pin_I/O pin_name A1
2 Pin_I/O pin_name A2
3 Buffer_I/O pin_name A1
4 Buffer_I/O pin_name A2
5 Pin_rail signal_name VSS
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
3
4
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
5
.subckt XtalkNoRail_s4p 1 2 3 4
Pin
Buffer

## Slide 14: DQ1 Pin to Buffer
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
…
1 Pin_I/O pin_name A1
2 Buffer_I/O pin_name A1
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
.subckt DQ1Pin2Buffer 1 2
Pin
Buffer

## Slide 15: DQ1 Pin to Pad, DQ1 Pad to Buffer
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
…
1 Pin_I/O pin_name A1
2 Pad_I/O pin_name A1
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
[Begin Interconnect Model]
…
1 Pad_I/O pin_name A1
2 Buffer_I/O pin_name A1
[End Interconnect Model]
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
1
2
.subckt DQ1Pin2Pad 1 2
.subckt DQ1Pad2Buffer 1 2
XPinPad PinA1 PadA1 DQ1Pin2Pad
XPadBuf PadA1 BufA1 DQ1Pad2Buffer
A1
Pin
Buffer
Pad

## Slide 16: VDD Pad by signal_name
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
…
1 Pin_rail signal_name VDD
2 Pad_rail signal_name VDD
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
[Begin Interconnect Model]
…
1 Buffer_rail signal_name VDD
2 Pad_rail signal_name VDD
[End Interconnect Model]
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
2
1
.subckt VDDPin2Pad_sn 1 2
.subckt VDDBuf2Pad_sn 1 2
XPinPad VDDPin VDDPad VDDPin2Pad_sn
XBufPad VDDPad VDDBuf VDDBuf2Pad_sn
Pin
Buffer
Pad
[Die Supply Pads] signal_name bus_label
VDD1 VDD VDDa
VDD2 VDD VDDa
VDD3 VDD VDDb
[End Die Supply Pads]
VDD1
VDD2
VDD3

## Slide 17: VDD Pad by pad_name
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
…
1 Pin_rail signal_name VDD
2 Pad_rail pad_name VDD1
3 Pad_rail pad_name VDD2
4 Pad_rail pad_name VDD3
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
[Begin Interconnect Model]
…
1 Buffer_rail signal_name VDD
2 Pad_rail pad_name VDD1
3 Pad_rail pad_name VDD2
4 Pad_rail pad_name VDD3
[End Interconnect Model]
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
2
1
.subckt VDDPin2Pad 1 2 3 4
.subckt VDDBuf2Pad 1 2 3 4
XPinPad VDDPin VDD1 VDD2 VDD3 VDDPin2Pad
XBufPad VDDBuf VDD1 VDD2 VDD3 VDDBuf2Pad
Pin
Buffer
Pad
[Die Supply Pads] signal_name bus_label
VDD1 VDD VDDa
VDD2 VDD VDDa
VDD3 VDD VDDb
[End Die Supply Pads]
VDD1
VDD2
VDD3
4
4
3
3

## Slide 18: VDD Pad by bus_label
[Pin] signal_name model_name
A1 DQ1 DQ
A2 DQ2 DQ
P1 VDD POWER
P2 VDD POWER
P3 VDD POWER
P4 VDD POWER
G1 VSS GND
G2 VSS GND
G3 VSS GND
G4 VSS GND
[Begin Interconnect Model]
…
1 Pin_rail signal_name VDD
2 Pad_rail bus_label VDDa
3 Pad_rail bus_label VDDb
[End Interconnect Model]
[Pin Mapping] pulldown_ref pullup_ref
Bus_label_signal_name
A1 VSS VDD
A2 VSS VDD
[Begin Interconnect Model]
…
1 Buffer_rail signal_name VDD
1 Pin_rail signal_name VDD
2 Pad_rail bus_label VDDa
3 Pad_rail bus_label VDDb
[End Interconnect Model]
P1
P2
P3
P4
A1
A2
G1
G2
G3
G4
1
2
PU(A1)
PD(A1)
A1
PU(A2)
PD(A2)
A2
2
1
.subckt VDDPin2Pad_bl 1 2 3
.subckt VDDBuf2Pad_bl 1 2 3
XPinPad VDDPin VDDa VDDb VDDPin2Pad_bl
XBufPad VDDBuf VDDa VDDb VDDBuf2Pad_bl
Pin
Buffer
Pad
[Die Supply Pads] signal_name bus_label
VDD1 VDD VDDa
VDD2 VDD VDDa
VDD3 VDD VDDb
[End Die Supply Pads]
VDD1
VDD2
VDD3
3
3