## Slide 1: Package EBD/EMD
Walter Katz
IBIS Interconnect
11/13/12

## Slide 2: Overview
Multi Chip Module (MCM) is a Package with Multiple Die
Example MCM as an EBD
  EBD Electronic Board Description
Example as an EMD
  EMD Electronic Module Description
  A Nose by Any Other Name Still Smells
Example.ipkg

## Slide 3: MCM is a Package with Multiple Die
Pins
Components
U3.7
U2.8
U2.7
U1.8
U1.7
A2
A1
U3.8

## Slide 4: Example EBD
[IBIS Ver] 6.0
[File name] Example.ebd
[Begin Board Description] Example
[Manufacturer] SiSoft
[Number Of Pins] 2
[Pin List] signal_name
A1 XYZ
A2 DEF
[Extended Nets]
XYZ A1 U1.7 U2.7 U3.7
DEF A2 U1.8 U2.8 U3.8
[End Extended Nets]
[IBIS-ISS Package] Example.ipkg
[Reference Designator Map]
| Ref Des File name Component name
U1 memory.ibs memory
U2 memory.ibs memory
U3 memory.ibs memory
[End Board Description]
[End]

## Slide 5: Example as an EMD A Nose by Any Other Name Still Smells
[IBIS Ver] 6.0
[File name] Example.emd
[Begin Module Description] Example
[Manufacturer] SiSoft
[Number Of Pins] 2
[Pin List] signal_name
A1 XYZ
A2 DEF
[Extended Nets]
XYZ A1 U1.7 U2.7 U3.7
DEF A2 U1.8 U2.8 U3.8
[End Extended Nets]
[IBIS-ISS Package] Example.ipkg
[Reference Designator Map]
| Ref Des File name Component name
U1 memory.ibs memory
U2 memory.ibs memory
U3 memory.ibs memory
[End Module Description]
[End]

## Slide 6: Example.ipkg
(XYZ
(File Example.iss) (Subckt XYZ)
(Model_Ports
(1 (Pin_name A1))
(2 (Pin_name 7) (Ref_des U1))
(3 (Pin_name 7) (Ref_des U2))
(4 (Pin_name 7) (Ref_des U3))
)
)
(DEF
(File Example.iss) (Subckt DEF)
(Model_Ports
(1 (Pin_name A2))
(2 (Pin_name 8) (Ref_des U1))
(3 (Pin_name 8) (Ref_des U2))
(4 (Pin_name 8) (Ref_des U3))
)
)

## Slide 7: EMD using Parameter Tree Format
(Example
(IBIS_Ver 6.0)
(File_name Example.emd)
(Module
(Name Example)
(Manufacturer SiSoft)
(Number_Of_Pins 2)
(Pins
(A1 XYZ)
(A2 DEF))
(Extended_Nets
(XYZ A1 U1.7 U2.7 U3.7)
(DEF A2 U1.8 U2.8 U3.8))
(IBIS-ISS_Package Example.ipkg)
(Reference_Designator_Map
(U1 memory.ibs memory)
(U2 memory.ibs memory)
(U3 memory.ibs memory))
))

## Slide 8: Connector is an EMD
Side A Pins
A.A2
A.A1
Side B Pins
B.A2
B.A1

## Slide 9: Connector EMD
[IBIS Ver] 6.0
[File name] Connector.ebd
[Begin Module Description] Connector
[Manufacturer] SiSoft
[Number Of Pins] 4
[Pin List] signal_name
A.A1 A1
A.A2 A2
B.A1 A1
B.A2 A2
[Extended Nets]
A1 A.A1 B.A1
A2 A.A2 B.A2
[End Extended Nets]
[IBIS-ISS Package] Connector.ipkg
[End]

## Slide 10: Connector.ipkg
(A1
(File Connector.iss) (Subckt Simple)
(Model_Ports
(1 (Pin_name A.A1))
(2 (Pin_name B.A1)) ))
(A2
(File Connector.iss) (Subckt Simple)
(Model_Ports
(1 (Pin_name A.A2))
(2 (Pin_name B.A2)) ))
(Full
(Tstonefile Connector.s4p)
(Model_Ports
(1 (Pin_name A.A1))
(2 (Pin_name B.A1))
(3 (Pin_name A.A2))
(4 (Pin_name B.A2)) ))

## Slide 11: Conclusions
EBD can be easily extended to support MCM
Can define new standard EMD if we get hung up by the word “Board” in EMD
EMD can either be Legacy IBIS format or Parameter Tree
EMD support Connector Models