## Slide 1: Terminal Draft 2
Walter Katz
Signal Integrity Software, Inc.
IBIS Interconnect
July 9, 2014

## Slide 2: Overview
Terminal record is restructured a bit to make Post-Layout terminals simple
Pre-Layout terminals associated with a specific Model_name (or a Default package model) use trailing Qualifier names to determine interconnect
  Connections
  Inverting and Non-Inverting pins on differential models
The explanation will seem overly complex but the examples show how simple it really is, so start off looking at the examples in slides 9:12,14:16 and 18:20

## Slide 3: Terminal Record
Terminal <#> <location> <ID> {Qualifiers}
  <#>
    >= 1
    <= Number of Terminals
    Unique
    Terminals of an interconnect model that do not have a Terminal record are considered unconnected, and the
  <location>
    Pin|Pin_Sig
    Pad|Pad_Sig
    Buf|Buf_PCR|Buf_GCR|Buf_PUR|Buf_PDR|Buf_Xref|Buf_Sig
  <ID>
    <Pin_name>|<Signal_name>|<Model_name>|Default
  Qualifiers
    Aggressor|Model_name|Default|Inverting|Non-Inverting|Connection(n)

## Slide 4: Pre-Layout and Post-Layout Rules
A Terminal is Post-Layout if it has no Qualifiers (other than Aggressor)
  ID can only be
    <Pin_name>|<Signal_name>
A Terminal is Pre-Layout if it has one or more Terminals with Qualifier Model_name or Default
  Pre-Layout Terminal Record ID can only be
    <Signal_name>|<Model_name>|Default
  Additional Pre-Layout Terminal Record optional Qualifiers:
    Aggressor
    Inverting|Non-Inverting
    Connection(n)
An Interconnect Model is Post-Layout if all of its Terminals are Post-Layout
An Interconnect Model is Pre-Layout if any of its Terminal are Pre-Layout

## Slide 5: Post-Layout <ID> Rules
Pin
  Pin_name
Pin_Sig
  Signal_name
    All pins of Signal_name are shorted to this one node
Pad
  Pin_name (or Die_pad_name)
Pad_Sig
  Signal_name
    All pads of Signal_name are shorted to this one node
Buf|Buf_PCR|Buf_GCR|Buf_PUR|Buf_PDR|Buf_Xref
    Pin_name
Buf_Sig
    Signal_name
      All buffer supply of Signal_name are shorted to this one node

## Slide 6: Post-Layout {Qualifiers}
Post-Layout Qualifiers are optional and limited to
  Aggressor
Limited to Interconnect Models that contain two or more I/O buffers.
If an I/O buffer is an Aggressor, its interconnect does not include all of the crosstalk from its aggressors.
Limited to only Terminal records that have Pin_name records.
Limited to only Pin_names that are buffer I/O pins.
If any buffer I/O Pin_name is Aggressor then that I/O buffer shall be considered a Aggressor.
At least one I/O buffer cannot be an Aggressor.

## Slide 7: Post-Layout Differential Rules
Differential buffers can be represented as two instances of a single ended buffer, or as “True Differentials” when using [External Models].
  Two single ended buffer instances can have independent supply voltages, or they can share the same supply voltages. When defining supply voltage nodes using Buf_PCR, Buf_GCR, Buf_PUR, Buf_PDR, Buf_Xref keywords the model may choose to have a single node using either the Inverting or Non-Inverting Pin_name, or have two nodes with both the Inverting and Non-Inverting Pin_names.
  A True Differential buffer can only have a single set of supply voltage nodes and can use either the Inverting or Non-Inverting Pin_name.

## Slide 8: Post-Layout Terminal Inferences
All I/O Connections are defined
Buffer instance supply nodes are either
  Generated by the IBIS B element
  Generated by the EDA tool
  Generated from interconnect model using the BUF_PUR, BUF_PDR, BUF_PCR nodes BUF_GCR
  Generated from a Buf_Sig node in conjunction with the Pin-Mapping record that associates Signal_name with buffer supply nodes

## Slide 9: Post-Layout Model Examples
Single DQ (A1)
  Terminal 1 Pin A1
  Terminal 2 Buf A1
Single DQS (D1,D2) (Differential)
  Terminal 1 Pin D1
  Terminal 2 Pin D2
  Terminal 3 Buf D1
  Terminal 4 Buf D2
  [Diff pin]
  D1 D2 ….
Single DQS (D1,D2) (Differential)
  Terminal 1 Pin D1
  Terminal 2 Pin D2
  Terminal 3 Pad D1
  Terminal 4 Pad D2

## Slide 10: Post-Layout Model Examples
Crosstalk (coupled)
One DQ (A2) victim, two DQ (A1 and A3) aggressors
  Terminal 1 Pin A1 Aggressor
  Terminal 2 Buf A1 Aggressor
  Terminal 3 Pin A2
  Terminal 4 Buf A2
  Terminal 5 Pin A3 Aggressor
  Terminal 6 Buf A3 Aggressor

## Slide 11: Post-Layout Model Examples
VDD: All Pins connected to VDD shorted, all buffers connected to VDD shorted
  Terminal 1 Pin_Signal_name VDD
  Terminal 2 Buf_Sig VDD
VDD: Pins connected to board “bed spring” model, all buffers connected to VDD shorted
  Terminal 1 Pin P1
  Terminal 2 Pin P2
  Terminal 3 Pin P3
  Terminal 4 Pin P4
  Terminal 5 Pin P5
  Terminal 6 Buf_Sig VDD

## Slide 12: Post-Layout Model Examples
VDD: Pin terminals connected to board “bed spring” model, buffer terminals connected to individual buffer Pullup Reference
  Terminal 1 Pin P1
  Terminal 2 Pin P2
  Terminal 3 Pin P3
  Terminal 4 Pin P4
  Terminal 5 Pin P5
  Terminal 6 Buf_PUR A1
  Terminal 7 Buf_PUR A2
  Terminal 8 Buf_PUR A3
  Terminal 9 Buf_PUR A4

## Slide 13: Pre-Layout Model_name Qualifier
ID is a Model_name or Model_selector name
If [Model] is differential, Inverting or Non-Inverting Qualifier is required
If more than one Connection, then Connection(n) is required
Aggressor is optional
Power supplied to buffer is either
  Generated by B-Element
  Generated by EDA tool
  From Buf_SIG
    This can be problematic if different instances of the same model have different Pin-Mapping supply Signal_names

## Slide 14: Pre-Layout Model Examples
One DQ
  Terminal 1 Pin DQ Model_name
  Terminal 2 Buf DQ Model_name
One DQS
  Terminal 1 Pin DQS Model_name Non-Inverting
  Terminal 2 Pin DQS Model_name Inverting
  Terminal 3 Buf DQS Model_name Non-Inverting
  Terminal 4 Buf DQS Model_name Inverting

## Slide 15: Pre-Layout Model Examples
Crosstalk (coupled)
One DQ victim, two DQ aggressors
  Terminal 1 Pin DQ Model_name Aggressor Connection(1)
  Terminal 2 Buf DQ Model_name Aggressor Connection(1)
  Terminal 3 Pin DQ Model_name Connection(2)
  Terminal 4 Buf DQ Model_name Connection(2)
  Terminal 5 Pin DQ Model_name Aggressor Connection(3)
  Terminal 6 Buf DQ Model_name Aggressor Connection(3)
  [Pin]
  A1 DQ1 DQ
  [Model] DQ

## Slide 16: Hybrid Pre-Layout and Post_Layout Model Example
Crosstalk (coupled)
One DQ victim, two DQ aggressors, one DQS aggressor
Terminal 1 Pin DQ Model_name Aggressor Connection(1)
Terminal 2 Buf DQ Model_name Aggressor Connection(1)
Terminal 3 Pin A2
Terminal 4 Buf A2
Terminal 5 Pin DQ Model_name Aggressor Connection(2)
Terminal 6 Buf DQ Model_name Aggressor Connection(2)
Terminal 7 Pin DQS Model_name Aggressor Connection(3) Non-Inverting
Terminal 8 Buf DQS Model_name Aggressor Connection(3) Inverting
Terminal 9 Pin DQS Model_name Aggressor Connection(3) Non-Inverting
Terminal 10 Buf DQS Model_name Aggressor Connection(3) Inverting

## Slide 17: Pre-Layout Default Qualifier
ID is Default also
If differential, Inverting or Non-Inverting Qualifier is required
If more than one Connection, then Connection(n) is required
Aggressor is optional
Power supplied to buffer is either
  Generated by B-Element
  Generated by EDA tool

## Slide 18: Pre-Layout Model Examples
One Single Ended
  Terminal 1 Pin Default Default
  Terminal 2 Buf Default Default
One Differential
  Terminal 1 Pin Default Default Non-Inverting
  Terminal 2 Pin Default Default Inverting
  Terminal 3 Buf Default Default Non-Inverting
  Terminal 4 Buf Default Default Inverting

## Slide 19: Pre-Layout Model Examples
Crosstalk (coupled)
Three Single Ended: one victim, two aggressors
Terminal 1 Pin Default Default Aggressor Connection(1)
Terminal 2 Buf Default Default Aggressor Connection(1)
Terminal 3 Pin Default Default Connection(2)
Terminal 4 Buf Default Default Connection(2)
Terminal 5 Pin Default Default Aggressor Connection(3)
Terminal 6 Buf Default Default Aggressor Connection(3)

## Slide 20: Hybrid Pre-Layout and Post_Layout Model Example
Crosstalk (coupled)
One DQ victim, two single ended aggressors, one differential aggressor
Terminal Pin Default Default Aggressor Connection(1)
Terminal Buf Default Default Aggressor Connection(1)
Terminal Pin A2
Terminal Buf A2
Terminal Pin Default Default Aggressor Connection(2)
Terminal Buf Default Default Aggressor Connection(2)
Terminal Pin Default Default Aggressor Connection(3) Non-Inverting
Terminal Buf Default Default Aggressor Connection(3) Inverting
Terminal Pin Default Default Aggressor Connection(3) Non-Inverting
Terminal Buf Default Default Aggressor Connection(3) Inverting