## Slide 1: Updated Interconnect Proposal Bob Ross, Teraspeed Labs bob@teraspeedlabs.com
Draft Presented September 23, 2015 at the Interconnect Working Group

## Slide 2: Background
Simplified from earlier presentations from Randy Wolff, Walter Katz, and Interconnect Task Group chair Michael Mirmak:
  http://www.eda.org/ibis/summits/may15/wolff2.pdf
  http://www.eda.org/ibis/summits/jan15/katz.pdf
  http://www.eda.org/ibis/summits/jun14/katz1.pdf
  http://www.eda.org/ibis/summits/may14/wolff.pdf
  http://www.eda.org/ibis/summits/jan14/katz.pdf
  http://www.eda.org/ibis/summits/may13/wolff.pdf
  http://www.eda.org/ibis/summits/jan13/mirmak2.pdf
  http://www.eda.org/ibis/summits/jan13/katz.pdf
Terminology simplification
  No model_name support
  No pre-layout distinction
  Simpler I/O buffer that uses existing IBIS syntax
Note, “I/O” here is generic for all 21 IBIS [Model] Model_types

## Slide 3: Goals
Update the Interconnect proposal Terminal section based on existing IBIS keyword
Illustrate locations for Buffer, Pad, Pin
Illustrate pin_name, signal_name, bus_label, and pad_name qualifiers
Illustrate buffer terminals Buffer_I/O, Puref, Pdref, (and not shown) Pcref, Gcref, Extref
Illustrate rail locations: Buffer_rail (not shown), Pad_rail, Pin_rail
Show chart of connections rules including Aggressor

## Slide 4: Definition Example
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels = signal_names
GND bus_labels = signal_names

## Slide 5: Partial Reference Diagram [Pin, Pad, Buffer] (A3, D1, D2 Omitted)
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
IBIS buffer model
One-to-one Pin-Pad connection is NOT required

## Slide 6: Terminal Syntax
[Begin Interconnect Model]
… | Other syntax
Number_of_terminals = <number> | List follows
<term_number> <terminal_type> <qualifier> <name> <Aggressor>*
… | More lines
…
[End Interconnect Model]
______________________________________________________
<qualifier>: pin_name, signal_name from [Pin] keyword,
or bus_label from [Pin Mapping] keyword,
*Optional <Aggressor> for Buffer_I/O
Convention: “shorted” connection
electrical connection

## Slide 7: Legal Interconnections
Terminal_Type / Qualifier  | pin_name | signal_name | bus_label | pad_name | Aggressor
Buffer_I/O | X |  |  |  | A
Puref | X |  |  |  | 
Pdref | X |  |  |  | 
Pcref | X |  |  |  | 
Gcref | X |  |  |  | 
Extref | X |  |  |  | 
Buffer_rail |  | Y | Y |  | 
Pad_I/O | X |  |  |  | 
Pad_rail |  | Y | Y | Z | 
Pin_I/O | X |  |  |  | 
Pin_rail | Y | Y | Y |  | 
X: I/O pin_names, Y,Z: POWER/GND names, Z: from [Die Supply Pads]
A: Optional Aggressor column to assign one or more aggressor buffers

## Slide 8: Legal Interconnections
Pin to on-die buffer
Pin to pad
Pad to on-die buffer
Note, Pin to pad to on-die buffer is illegal since pad terminals are not needed for external connections

## Slide 9: Reference Example Repeated
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels = signal_names
GND bus_labels = signal_names

## Slide 10: With bus_label = signal_name
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
New optional Bus_signal_name subparameter indicates that POWER/GND signal_name pins are assumed and do not have to be listed

## Slide 11: Pin-to-Buffer Interconnect Example using pin_names
[Pin Mapping] not needed, all connections are pin-to-buffer
(Similar to [Package] model direct connection to I/O buffer)

## Slide 12: Pin-to-Buffer Interconnect Example
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)

## Slide 13: Pin-to-Pad, Pad-to-Buffer
[Die Supply Pad] keyword
  Specifies the supply pad names for each supply
  Supports fewer or more pads than pins
[Die Supply Pad] signal_name bus_label
<pad_name> <name | NC> <name | NC>
Is bus_label needed??

## Slide 14: Pin-to-Pad Example with using pin_names and pad_names
[Pin Mapping] not needed

## Slide 15: Pin-to-Pad Example using pin_names and pad_names
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
P1a, P2a, G1a, G2a

## Slide 16: Pad-to-Buffer Example using pad_names and Buffer Nodes
[Pin Mapping] not needed

## Slide 17: Pad-to-Buffer Example using pad_names and Buffer nodes
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
P1a
P2a
G1a
G2a

## Slide 18: POWER/GND One-to-Several, Several-to-One Illustrations
Explicit connections available directly from pin_name and pad_name
No practical way to use signal_name unless signal_name is defined differently for one pin in several-to-one configurations, e.g., signal_names VDDa, VDDb
No practical way to define different bus_labels for one-to-several configurations
Next slides illustrate several cases using pin_name and pad_name directly

## Slide 19: One-to-Several Pin-to-Pad using pin_names & pad_names

## Slide 20: Pin-to-Pad One-to-Several Interconnect Example
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
P1a, P2a, G1a, G2a

## Slide 21: Pin-to-Pad Several-to-One Interconnect Example
[Pin Mapping] not needed

## Slide 22: Pin-to-Pad Several-to-One Interconnect Example
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
P1a, P2a, G1a, G2a

## Slide 23: Power Rail Interconnect Example using signal_name
[Pin Mapping] optional if bus_labels are signal_names

## Slide 24: Pin-to-Buffer Interconnect Example using signal_name for Rails
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS

## Slide 25: Example with bus_label Groups
pin_names
signal_names for POWER/GND pins
bus_labels for implicitly shorted pins or on-die shorted connections for POWER/GND pins
POWER bus_labels
GND bus_labels

## Slide 26: Power Rail Interconnect Example using signal_names and bus_labels

## Slide 27: Pin-to-Pad Interconnect Example with signal_names and bus_labels
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS
VDD1 VDD2 VDD3
VSS1 VSS2 VSS3

## Slide 28: Power Rail Interconnect Example using bus_labels Only

## Slide 29: Pin-to-Pad Interconnect Example with bus_labels Only
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD1 VDD2 VDD3
VSS1 VSS2 VSS3

## Slide 30: Power Rail Interconnect Example using signal_names Only

## Slide 31: Pin-to-Pad Interconnect Example with signal_names Only
Physical Buffer, its Model and On-Die Interconnect
Pads
Pins
A1
P1
P2
P3
P4
P5
G1
G2
G3
G4
G5
A2
Die
A1
A2
Pdref(A2)
Puref(A2)
Pdref(A1)
Puref(A1)
VDD
VSS

## Slide 32: Conclusions
Revised syntax
  Makes use of existing [Pin Mapping] for bus labels and defaults, [Diff Pin], [Series Pin Mapping] for two-node models
  Supports directly all 21 IBIS [Model] Model_types
  Overrides all [Package] model syntax including [Define Package Model]
  Supports IBIS-ISS (an HSPICE subset) and Touchstone electrical models
  Supports electrical models from pin-to-buffer, pin-to-pad, and pad-to-buffer (on-die)
  I/O buffer 1-to-1 connection assumed, but not so for POWER and GND interconnections – use pin_name and pad_name for such situations
Issues
  Can two or more [Begin Interconnect Model]s be used together? (E.g., a pin-to-pad simplified package model and a pad-to-buffer interconnect model with/without a separate buffer to pin path