## Slide 1: IBIS Advanced Technology Modeling Group (IBIS-ATM)* Status Report
Todd Westerhoff, SiSoft
(Chief Troublemaker)
DesignCon IBIS Summit
Feb 1, 2007
* Formerly IBIS-Macro

## Slide 2: Agenda
Updated Group Charter
Peak Distortion Analysis
HSpice investigations
Cadence’s Proposal / BIRD
Circuit vs. Signal Simulation
.DLL / Executables / Encypted Source, AMS / SystemC / Other Languages
Terminology Presentations
Current Status

## Slide 3: Updated Group Charter
Changed name to IBIS Advanced Technology Modeling Group (IBIS-ATM)
Current goal:
  Define a transmitter/receiver modeling standard for SERDES channel analysis that encompasses equalization and clock recovery.
The solution must:
  Support multiple EDA vendors
  Support multiple IC vendors
  Protect semiconductor vendor IP
  Support combined transmitter/receiver design
  Support design optimization

## Slide 4: Peak Distortion Analysis
Analytical method for predicting maximum eye closure based on channel pulse response
Implemented in VHDL-AMS and demonstrated by Arpad Muranyi of Intel
Reference presentation:
  http://download.intel.com/education/highered/signal/ELCT865/Class2_15_16_Peak_Distortion_Analysis.ppt

## Slide 5: HSpice Investigations
Request from Cadence at Asian IBIS Summit to extend [External Model] Spice syntax to allow parameter passing
Berkeley Spice [currently supported] does not provide this
Asked Synopsys if they would make HSpice syntax publicly available [de facto standard]
  Synopsys declined, not wanting to restrict future extensions to HSpice’s syntax
Issue currently considered closed
  Cadence invited to propose specific syntax for parameter passing

## Slide 6: Cadence Proposal
Ongoing discussions of Cadence’s proposal and algorithms therein
Related discussions on details of channel characterization and modeling
Cadence presented proposal as draft IBIS BIRD

## Slide 7: Circuit vs. Signal Simulation
Circuit Modeling/Simulation
  Interconnect models
  Network characterization
  Pulse Response
Signal Processing Analysis
  Transmitter equalization
  Receiver equalization
  Time-domain waveform generation (convolution)
  Clock recovery
Circuit Simulation Diagram
Signal Processing Diagram

## Slide 8: .DLL / Executables / Encypted Source, AMS / SystemC / Other Languages
Extensively discussed model development and distribution:
  Tradeoffs between different development languages
  System language trends
  Advantages / disadvantages of different distribution methods (.dll vs. executable vs. encrypted source)
  Strengths and weaknesses of different IP-protection schemes

## Slide 9: Terminology Presentations
Intel
  http://www.vhdl.org/pub/ibis/macromodel_wip/archive/20061024/arpadmuranyi/Channel%20analysis%20flow%20with%20IBIS/IBIS_API_flow.pdf
SiSoft
  http://www.vhdl.org/pub/ibis/macromodel_wip/archive/20061212/toddwesterhoff/Serial%20Link%20Terminology/serial_link_terminology.pdf

## Slide 10: Current Status
Still need better definition of target audience
  Model developers?
  End-users?
Network characterization terminology still unclear
  Impulse response vs. pulse response vs. transfer function vs. pole/zero representations
Cadence’s proposal is still the only one on the table
  Ongoing discussions of detailed implications
  SiSoft recommendations for enhancement
    Mechanism to publish model parameters for EDA tool
    Need analysis methodology-independent models

## Slide 11: For More Information
IBIS-ATM / IBIS-Macro Website
  www.eda.org/pub/ibis/macromodel_wip/
IBIS-Macro mail reflector
  Mail to: ibis-macro-request@freelists.org
  Subject: subscribe
IBIS-Macro mail archives
  www.freelists.org/archives/ibis-macro