## Slide 1: Strategies for Coping with Non-linear and Non-time Invariant Behavior for High Speed Serial Buffer Modeling
Richard Mellitz
Results from DesignCon2008 paper with Steve Pytel, Michael Tsuk, and Toni Donisi

## Slide 2: Linearity Enables Superposition
A linear system possesses the property of superposition, in other words, the system possesses both the additive and homogeneity properties. If
Then, by the additive property,
And by the homogeneity property
where a is a constant.

## Slide 3: Example of Non-Linearity
A resistance, capacitance, or inductance that changes with voltage creates non linear circuit behavior.
All transistors are non-linear
Many buffers have linear region of operations
IBIS is used to represent non linear characteristics
Full transistor models may include time variant effects.
  Not discussed today

## Slide 4: Simple Superposition Example: “Tales of a lone bit”
The lone pulse can be used to determine the response digital pulse stream.
This is true as long as superposition holds or the system is linear
  The interconnect channel is linear.
We will use an example to how a lone pulse with cursor value of 0.75 and post cursor tap of 0.25 results is an bit stream that can be recognized as 6dB pre-emphasis
Cursor=0.75
Post cursor =0.25
base = 0
Bit Time or Unit Interval
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Use superposition to string together a bit pattern out of lone bits with the amplitude of the taps
0 0 0 0 0 0 1 0 0 0 0 0
0 0 0 0 0 0 1 0 0 0 0 0
0 0 0 0 0 0 1 0 0 0 0 0
0 0 0 0 0 0 1 0 0 0 0 0
0 0 0 0 0 0 1 0 0 0 0 0
0 0 0 0 0 0 0 1 1 1 0 0 0 1 1 1 0 0 0 0 0 Bits
0 0 0 0 0 0 0 ¾ ½ ½ -¼ 0 0 ¾ ½ ½ -¼ 0 0 0 0 Value

0 0 0 0 0 0 1 0 0 0 0 0
0.75
0.0
-0.25
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: We now have a familiar waveform
Notice the familiar de-emphasized waveform which is a composition of lone bits
  Observe that Vshelf is ½ and Vswing is 1.
  For 2 tap systems we would call this 6dB de-emphasis 20*log(0.5)
Using this concept simulate or measure one lone bit and with out performing any more simulation we can:
  Determine the response of an arbitrary string bits
  Determining best or worst case signal distortion.
  Determining the eye opening due algorithmically piecing string to that produce aggregated performance
Renormalize to 1 peak to peak: Value-1/4
-¼ -¼ -¼ -¼ -¼ -¼ -¼ ½ ¼ ¼ -½ -¼ -¼ ½ ¼ ¼ -½ -¼ -¼ -¼ -¼ renorm
Vshelf = ½
Vswing = 1
0 0 0 0 0 0 0 1 1 1 0 0 0 1 1 1 0 0 0 0 0 Bits
0 0 0 0 0 0 0 ¾ ½ ½ -¼ 0 0 ¾ ½ ½ -¼ 0 0 0 0 Value
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: High Speed Signaling tools
Use superposition of edges to create long bits streams
Edge are altered in time to create jitter
Others convolve a channel system function with jitter and data
Adaptive equalization can be determined from bit streams, system function, or pulse response.
Ansoft’s QuickEye™ resembles some of the above
All these type of tools make the assumption that linear superposition is valid

## Slide 8: Rest of the Agenda
Review CML buffer
Making the CML buffer non linear
Determine effect of % of linearity for different equalization interpretations
Conclusion

## Slide 9: Simple Current Mode Logic (CML) Differential Buffer
Edge
filter
inverter
FIR Filter
Level Shifter
CMLSOURCE
Data Stream
Voutdiff
Routp
Routn
Coutp
Coutn

## Slide 10: FIR filter
data stream
UI
2*UI
4*UI
3*UI
delay
delay
delay
delay
Pre
post1
post2
post2
-
-
-
-
+


## Slide 11: Non-Linear Experiment
Voutdiff
Routp
Routn
Coutp
Coutn

## Slide 12: Non-linear Termination example
Rmax
Rmin
V
R
V
I

## Slide 13: Experiment setup
Buffer
channel
load
Tx Linear Equalizer
Math Process
Rx Linear Equalizer
Set taps at Tx
Set taps at Rx
Buffer I/V loads
Bitwise eye
Bit stream
Edge
Convolved eye ~ QuickEye™
1
2
1
3
2
3

## Slide 14: Experiments
CML Buffer Loads
  50  Rout
  30 to 70  Rout variation
  10 to 100  Rout variation
Data Pattern PRBS15
Loads
  50  both legs
Channels
  12” of a 72  differential transmission line (50  SE termination)
  2 connector “real” channel
UI=125ps
Simulation time 100ns

## Slide 15: Routn=Routp=load=50  Rout range: 10 to 90  load=50 
Bit stream (1) and edge convolution (2) are equal,
if taps are set at the transmitter
Rout range: 10 to 90 
Rout = 50 
“Single resistor equivalent”
Rx Mathematical equalization (3):
24.5 mv
error
Taps = 0.79 and -0.21

## Slide 16: Channel =72  12” line Rout range: 10 to 90 
Bit stream (1) and edge convolution (2) are close,
if tap are set in the transmitter
Rout range: 10 to 90 
Rx Mathematical equalization(3):
Taps = 0.79 and -0.21

## Slide 17: Channel = 72  12” line Rout range: 10 to 90 
Bit stream
Rx Mathematical equalization w/convolution:
Convolution
Taps = 0.79 and -0.21
Zoomed in
1
2
3

## Slide 18: Channel = 72  12” line Rout range: 10 to 90 
Convolution
Taps set at Tx
Bit Stream
~ 10 mv & 0.1ps difference
Taps = 0.79 and -0.21
1
2

## Slide 19: Channel = 72  12” line Rout range: 10 to 90 
Bit Stream
Convolution
Taps set at Rx
~ 2 mv & 2ps difference
Taps = 0.79 and -0.21
1
3

## Slide 20: Channel = 72  12” line Rout range: 10 to 90  ISI Jitter distributions
Taps = 0.79 and -0.21
1
2
3

## Slide 21: Channel = 72  12” line Rout range: 30 to 70 
Bit stream (1) and edge convolution(2) are very close,
if tap are set in the transmitter
Rout range: 30 to 70 
Rx Mathematical equalization(3):
Taps = 0.79 and -0.21

## Slide 22: Channel = 72  12” line Rout range: 30 to 70 
Bit stream
Rx Mathematical equalization w/convolution:
Convolution
Taps = 0.79 and -0.21
1
2
3

## Slide 23: Channel = 72  12” line Rout range: 30 to 70 
Bit Stream
Convolution
Taps set at Tx
About the same EO
Taps = 0.79 and -0.21
1
2

## Slide 24: Channel = 72  12” line Rout range: 30 to 70 
Bit Stream
Convolution
Taps set at Rx
1.5mV & 6 ps E0 Difference
Taps = 0.79 and -0.21
1
3

## Slide 25: Channel =2 connector real system Rout range: 10 to 90 
Bit Stream
Convolution
Taps set at Tx
30 min Simulation Time
2 min Simulation Time
Taps = 0.79 and -0.21
1
2
1.5mV & 1.5 ps E0 Difference

## Slide 26: Channel =2 connector real system Rout range: 10 to 90 
Bit Stream
Convolution
Taps set at Rx
Bit Stream
30 min Simulation Time
2 min Simulation Time
Taps = 0.79 and -0.21
1
0.7mV & 1.1 ps E0 Difference
3

## Slide 27: Channel =2 connector real system Rout range: 10 to 90 
Bit stream (1) and edge convolution(2) are very close,
if tap are set in the transmitter
Rout range: 30 to 70 
Rx Mathematical equalization(3):
Taps = 0.79 and -0.21

## Slide 28: Channel = 72  12” line Rout range: 0.5pf to 1.5pF
Bit Stream
Taps = 0.79 and -0.21
1
1.3mV & 0.5 ps E0 Difference
Convolution
Taps set at Tx
2

## Slide 29: Channel = 72  12” line Rout range: 0.5pf to 1.5pF
Bit Stream
Taps = 0.79 and -0.21
1
3
5mV & 7.5 ps E0 Difference
Convolution
Taps set at Rx

## Slide 30: Conclusion
Single resistor equivalent models are insufficient
Convolution Eye is OK if:
  Equalize taps are set at the Tx or if buffer impedance range is < 40% from nominal … or
  Predictive algorithms for solution space don’t require more than a few ps or mv of resolution
Adaptive equalization methods may be impacted by non-linearity
  Jitter distribution varies with method. More work is needed on impact of ISI jitter distributions on adaptive algorithms
  More work is required to determine if algorithms will hunt out correct Rx equalization
Result may be worse for higher data rates
  More data needed here