## Slide 1: A Selection of Common Mode Requirements in Industry Specifications Background for New IBIS Measurements
Michael Mirmak
January 22, 2008

## Slide 2: USB 2.0
TX, Full/low speed signaling: the crossover voltage (Vcrs) must be between 1.3 and 2.0 V
RX, High speed: (guideline) reliably receive signals with CM voltage (Vhscm) between -50 mV and 500 mV (nominal at 200 mV)
RX: Differential Common Mode Range (Vcm) must be between 0.8 - 2.5 V (includes Vdi range)

## Slide 3: Serial ATA
SATA 2.0 Vcm, AC Requirements
TX: 50 mVpp
RX: 100-150 mVpp
SATA 1.0 Vcm AC Requirements
TX, RX: 0-2.0 V on each signal,
all conditions
RX: 100 mV max
Sinusoidal amplitude, at connector;
Frequency between 2 and 200 MHz;
Common mode transients to settle
within 10% of DC value within 10 ns
SATA 1.0 Vcm DC Requirements
RX: 200-450 mV (at receiver connector)

## Slide 4: PCI Express*
Electrical Idle: the state of the output driver in
which both lines, D+ and D-, are driven to the
DC common mode voltage
VTX-CM-AC-PP TX AC common mode voltage:
100 mVPP (5.0 Gt/s)
VTX-CM-AC-peak TX AC common mode voltage:
20 mV (2.5 Gt/s)
VTX-AC-CM-PP and VTX-AC-CM-peak are measured over at least 106 UI.
VTX-DC-CM TX DC common mode voltage:
0 - 3.6 V for 2.5 and 5.0 Gt/s
Measured at the TX pins under any conditions.