## Slide 1: Electrical Module Description EMD
A new approach to describing packages and modules
Walter Katz
March 4, 2008

## Slide 2: Original IBIS Concept
Component
  Pins
  Behavioral Models
    Thresholds
    IV curves
    VT curves
  Package Parasitics
    Lumped RLC

## Slide 3: PKG Evolution
EBD style interconnect models
Lumped RLGC Matrix

## Slide 4: Module Evolution
Electronic Board Description (EBD)
  Distributed/Lumped RLC
  No matrix coupling
  Only Pin to Pad interconnect
  Multiple Components
  No pad to pad interconnect between components
  No power distribution

## Slide 5: ICM
More flexible interconnect modeling
  Coupling
  Better Loss representation
    S parameter
    W line (table driven)
Not integrated with IBIS

## Slide 6: Module Interconnect Modeling Requirements
Signal Interconnect Modeling
Signal Coupling (crosstalk)
Power Distribution
Coupling between Signal Interconnects and Power Distribution (SSO)

## Slide 7: Current Solution
Requires Full Module Layout Description
  Cad Data Base
    Routing
    Planes
    Stackup
  Analogy to IBIS is full transistor spice models
    IP issues
  “Min/Max” issues

## Slide 8: Min/Max Issue
Corners mean something different
Routing of individual nets on a module have a range of interconnect for a bus
  Net by net
  Best and worst of all nets in a bus, or more than typ min max
DIMM (PCIe) (rank, # sdrams, …)
  Systems require DIMM interchangeability

## Slide 9: EMD Solution
Contains the following sections
  [Pins]
  [Components]
  [Extended Nets]
  [Supply Nets] (Power Nets)
  [Subckts]
  [Coupled Subckts]

## Slide 10: [Pins] (Module Pins)
[Pins]
  Pin Number
  Signal Name
  Signal Type
[Diff Pins]
  Active High Pin Number
  Active Low Pin Number

## Slide 11: [Components]
Reference Designator
Part Number
IBIS File
  <file>.ibs
    “Bare Die Component”
  <file.ebd>
  <file>.emd
Convention for this document
  Pin is an EMD [Pin]
  Pad is a component [Pin].

## Slide 12: Power of Hierarchical .emd
What is the package model of a flip chip die.
  If it is mounted directly to the module, there is no “package model at all”.
  If it is wire bond, who knows how far the wire bond connection is, and height over what return path?
  If it is put into a small outline smd, then there is some interconnect model from the silicon pads to the point the package touches the PCB or MCM.
  If it is a stacked dram that might have some special three dimensional model to predict the s parameter model at very high edge rates
EMD files addresses all of this.

## Slide 13: On Die Power Supply Distribution
Enhancement to Bare Die .ibs Component
GROUND is just another Supply Net
Bare Die Supply Nets
  Associated with Component “Power” Pads
  Nominal DC Voltage
  Nominal Noise
  Switching Noise
On Die Power Delivery Model
  Capacitors between Supply Nets

## Slide 14: [Extended Nets]
Net Name
List of Pins/Pads
  EMD pins
  Components pads
  Discrete components are not included
    Blocking caps
    Series and parallel terminations
    Supply Caps

## Slide 15: Subckts
Data is contained in separate file
  File Extension .imod
“IBIS Spice” Meta format
It is expected that translators will be required for each target simulator
.subckt <name> <nodes> … <parameter>=<value> …

## Slide 16: Subckts (continued)
Subckt
  Typ, Min, Max (worst, best , …) (corners)
  File name
  Subcircuit Name
  Node List
  Parameters

## Slide 17: Subckt Elements
R Resistor
L Inductor
C Capacitor
T Tline
W Line
  RLGC
  Table Driven
S parameter element
V DC Voltage
X Subckt
Impulse Response
Poles and Zeros
.include
.parameter

## Slide 18: Subckt Levels
Level 1
  R Resistor
  L Inductor
  C Capacitor
  T Tline
  W Line (RLGC)
  V DC Voltage
This will handle >95% of System SI requirements
Level 2
  S parameter element
Level 3
  W Line (Table)
  Impulse Response
  Poles and Zeros
  X eleement

## Slide 19: Coupled Circuits
Explicit Coupled Circuits
  Subckt with pins and pads of specific Extended Nets
  [Interconnect Equivalent XNets]
  [Interconnect Equivalent Nets]
Implicit Coupled Circuits
  Subckt with pins and pads of [Interconnect Equivalent Nets].

## Slide 20: Example fbdimm.emd
[Module] fbmidd
[Pin]
1 Power VSS
2 Power VSS
3 Power VDD
4 Power VDD
5 Power VEE
6 Power VEE
7 PS1
8 PS1#
9 PN1
10 PN1#
11 CLK
12 CLK#
13 ADR0
14 ADR1
[Diff Pins]
7 8
9 10
11 12
[Components]
U1 AMB amb.ibs amb
U2 AMB amb.ibs amb
U3 SDRAM sdram.ibs sdram
U4 SDRAM sdram.ibs sdram

## Slide 21: Interfacing Extended Nets to Subckts
[Extended Nets]
PS1 7 8 U1.1 U1.2
PN1 9 10 U2.7 U2.8
PXX U1.7 U1.9 U2.1 U2.2
CLK 11 12 U3.1 U3.2 U4.1 U4.2
ADR0 13 U3.3 U4.3
ADR1 14 U3.4 U4.4
[Supply Nets]
VSS 1 2 U1.3 U2.3 U3.5 U4.5
VDD 3 4 U1.4 U2.4 U3.6 U4.6
VEE 5 6 U1.5 U2.5 U3.7 U4.7
[Voltages]
VSS 0.
VDD 2.2
VEE 12.5
[Subckts] ! One or more per Xnet
PS1 typ psn.imod psn_typ (7 8 U1.1 U1.2)
PN1 typ psn.imod psn_typ (9 10 U2.7 U2.8)
PN1 min psn.imod psn_min (9 10 U2.7 U2.8)
PN1 max psn.imod psn_max (9 10 U2.7 U2.8)
…
VSS all vss.imod vss (1 2 U1.3 U2.3 U3.5 U4.5)
[Begin Subckts] ! Per [Interconnect Equivalent Nets]
[Subckt] psn (pin pin_l pad pad_l)
Typ_Model psn.imod psn_typ
Min_Model psn.imod psn_min
Max_Model psn.imod psn_max
[Interconnect Equivalent Nets]
! Xnets with same number of Pins and Pads
! and use the same interconnect model
PS1 (7 8 U1.1 U1.2)
PN1 (9 10 U2.7 U2.8)

## Slide 22: Coupled Subckts
! Victim : Aggressor List
[Subckt] psn (victim_nodes aggressor_bodes …)
Best_Model psn_cpl.imod psn _cpl _Best
Worst_Model psn _cpl.imod psn _cpl _worst
Victim_Xnet PS1 PN1
Victim_Xnet PN1 PS1 PXX
Victim_Xnet PXX PN1
[Subckt] adr (victim_nodes aggressor_bodes …)
Best_Model adr_cpl.imod adr _cpl _Best
Worst_Model adr _cpl.imod adr _cpl _worst
Victim_Xnet ADR0 ADR1
Victim_Xnet ADR1 ADR0
! Grouping Nets in a BUS
[Subckt] psn (xnet1 nodes, xnet2 nodes)
Best_Model psn_cpl.imod psn _cpl _Best
Worst_Model psn _cpl.imod psn _cpl _worst
Xnet PN1 PS1 PXX
[Subckt] adr (victim_nodes aggressor_bodes …)
Best_Model adr_cpl.imod adr _cpl _Best
Worst_Model adr _cpl.imod adr _cpl _worst
Xnet ADR0 ADR1

## Slide 23: Subckt “Views”
Subckts can be significantly more detailed during the IC/Module design cycle.
The same subckts can be simplified for system design.
IC/Module designers can supply the more detailed subckts to high valued customers that have more need and expertise to do more refined analysis.

## Slide 24: amb.ibs sdram.ibs
[Component] amb
[Pads]
1 PS1 SerDesRx
2 PS1# SerDesRx
3 POWER VSS
4 POWER VDD
5 POWER VEE
7 PN1 SerDesTx
8 PN1# SerDesTx
[Diff Pin]
1 2
7 8
[Model] SerDesRx
External Model (Pad_H,Pad_L,VSS,VDD,VEE)
[Component] sdram
[Pads]
1 CLK CLK_IN
2 CLK# CLK_IN
3 ADR0 Input
4 ADR1 Input
5 POWER GND
6 POWER VX
7 POWER VY
[Diff Pin]
1 2
[On Die Caps]
Cap GND VX 1pF
Cap GND VY .2pF
[Model] Input
External Model (Pad, GND, VX, VY)
  need correct current behavior
    DC
    AC 1MegHz
    AC 5GHx