## Slide 1: Package and On-Die Interconnect Decisions Made and Proposed Solutions
Walter Katz
IBIS ATM
December 3, 2013

## Slide 2: Overview
Decisions Made
What These Decisions Means
Enhancement to IBIS Component to Support a List of Die Supply Pads
Enhancement to IBIS Component to Support a Buffer Reference Voltage Signal Names
Example IBIS File
Example IBIS Component Enhanced
Port Shorthand Notation
BIRD 125 Port Naming
EMD-Like is Equivalent to BIRD 125
Subckt Example Shorthand
Package Model
On-Die Model
Merging On-Die Model into Package Model
Signal Name Supply (PDN) Ports
Model Name Signal (I/O) Ports
Next Decisions
Conclusions

## Slide 3: Decisions Made
Decisions Made | In .ibs | In EMD
Connectors | No | Yes
Cables | No | Yes
Broadband EBD | No | Yes
MCM | No | Yes
Interposers | No | Yes
3-D structures | No | Yes
Stacked Memory | No | Yes
Splits/Joins of Signal (I/O) in Pacxkage or Die | No | Yes
RDL as separate element | No | Yes
New list of supply (PDN) die pads | Yes | Yes
Separate package and on-die interconnect model | Yes | Yes
Package model can include on-die model | Yes | Yes
Broadband I/O Package Modeling | Yes | Yes
Package PDN | Yes | Yes
Broadband I/O On-Die Modeling | Yes | Yes
On-Die PDN | Yes | Yes
Interconnect coupling (crosstalk) between I/O and I/O | Yes | Yes
Interconnect coupling between I/O and PDN | Yes | Yes
Optical Interconnect | No | No

## Slide 4: What These Decisions Mean
For signal (I/O) pins there is a one to one correspondence between Pin Number, Die Pad, and Buffer.
There is a Few to Many or Many to Few relationship between supply (PDN) pins and supply die pads, and buffer Pullup, Pulldown, Power Clamp and Ground Clamp Reference terminals.
There MAY be a one to one correspondence between signal (I/O) Pin Numbers and Signal Names (IBIS 6.0 is not clear on this).

## Slide 5: Enhancement to IBIS Component to Support a List of Die Supply Pads
Keyword: [Die Supply Pad]
Required: No
Description: Associates supply Die Pads to signal names.
Sub-Params: signal_name
Usage Rules: If this section exists, at least one supply die pad must be specified for each signal name that is used as a Pullup Reference, Pulldown Reference, Power Clamp Reference and Ground Clamp reference on any [Model]. The first column must contain the die pad name. The second column, signal_name, gives the data book name for the supply voltage on that die pad. There must be at least on pin in the [Pin] section that has the same signal_name. All pins in the [Pin] section that have the same signal_name must have a model_name of either POWER or GND. All pins in the [Pin] section that have the same signal_name cannot have a mixture of model_names POWER or GND.
Column length limits are:
[Die Supply Pad] 40 characters max
signal_name 40 characters max
Example:
[Die Supply Pad]
VCC_1 VCC
VCC_2 VCC
VCC_3 VCC
VSS_1 VSS
VSS_2 VSS
VDD_1 VDD
VDD_2 VDD

## Slide 6: Enhancement to IBIS Component to Support a Buffer Reference Voltage Signal Names
Keyword: [Buffer Supplies]
Required: No
Description: Associates model reference voltages with signal_names
Sub-Params: pullup_signal_name pulldown_signal_name power_clamp_signal_name ground_clamp_signal_name
Usage Rules: If this section exists, signal names are specified for each buffer instance pullup, pulldown, power clampo and ground clamp reference. The first column must contain a pin_name of a pin in the [Pin] section. The pin in the pin section may not have model_name POWER, GND or NC. The remaining columns specify the supply voltages for the model instance associated with the pin_name. The second column, pullup_signal_name, gives the data book name for the pullup reference voltage on the model. The third column, pulldown_signal_name, gives the data book name for the pulldown reference voltage on the model. Each line must contain either three or five columns. If the line contains three columns, then the power clamp reference is the same as the pullup reference, and the ground clamp reference is the same as the pulldown referenc. If there is five columns, then column four is the power_clamp_signal_name and column five is the ground_clamp_signal_name.
Column length limits are:
[Buffer Supplies] 5 characters max
pullup_signal_name 40 characters max
pulldown_signal_name 40 characters max
power_clamp_signal_name 40 characters max
ground_clamp_signal_name 40 characters max
Example:
[Buffer Supplies] signal_name|
A1 VCC VSS
A2 VCC VSS
A3 VCC VSS VDD VSS
A4 VCC VSS VDD GND

## Slide 7: Example IBIS File
[Pin] signal_name model_name R_pin L_pin C_pin
1 VDDQ POWER
2 VDDQ POWER
3 VSSQ GND
4 DQ0 DQ
5 DQ1 DQ
6 DQS+ DQS
7 DQS- DQS
8 A0 ADDCMD
9 A1 ADDCMD
|
[Diff Pins]
6 7
|
[Model Selector] DQ
DQ_34_2133 DQ Driving
DQ_IN_ODT240_2133 DQ Receiving
[Model Selector] DQS
DQS_2133 DQS Driving
DQS_IN_2133 DQS Receiving
[Model Selector] ADDCMD
ADDCMD_Near ADDCMD Near
ADDCMD_Far ADDCMD Far

## Slide 8: Example IBIS Component Enhanced
[Die Supply Pad]
| If a supply signal name is not in this list then one can assume that there
| are the same number of Die Supply Pads as there are supply pins for that
| signal name, and that their Die Supply Pad names are the same as the Pin number
VDDQ_1 VDDQ
VDDQ_2 VDDQ
VDDQ_3 VDDQ
VSSQ_1 VSSQ
VSSQ_2 VSSQ
|
[Buffer Supplies]
4 VDDQ VSSQ
5 VDDQ VSSQ
6 VDDQ VSSQ
7 VDDQ VSSQ
8 VDDQ VSSQ
9 VDDQ VSSQ

## Slide 9: Port Shorthand Notation
Pins
  Pin.<Pin number>
Die Pads
  Pad.<Pin_number | Die supply pad>
Buffer
  Buf.<Pin number>
  Buf_PUR.<Pin number>
  Buf_PDR.<Pin number>
  Buf_PCR.<Pin number>
  Buf_GCR.<Pin number>
Same As
  (Pin (Pin_number <Pin number>))
  (Pad (Pin_number <Pin number>))
  (Buf (Pin_number <Pin number>))

## Slide 10: BIRD 125 Port Naming
  BIRD 125 calls for a new section “[Package Circuit], [End Package Circuit]“ in [Define Package Model].
  The Die Pads Port Names associated with signal (I/O) Pin Numbers must be explicitly defined.
  [Pin Numbers] for use with [Package Circuit] are totally different then the existing [Pin Numbers] keyword in IBIS 6.0
  There is no method of defining Buffer I/O or reference voltage port names (Pullup Reference, Pulldown Reference, Power Clamp Reference, and Ground Clamp Reference)
    [Pin Numbers] would need to be enhanced to also define Buffer Terminal Port Names
Summary: BIRD 125 requires that Port Names be defined, while EMD and EMD-Like assign subckt ports to already defined electric points in a package with a parameter tree or shorthand naming convention.

## Slide 11: BIRD 125 [Package Circuit]
[Package Circuit]
Language IBIS-ISS
| Corner corner_name file_name circuit_name (.subckt name)
Corner Typ PackageModel.spi S_pkg
| Parameters List of parameters
Parameters TSFile = "My_TstoneFile.s16p"
| Ports are in same order as defined in SPICE
Ports 10 1 11 2 3 4a 4b 5
Ports IDiePort_5 pad_4 IDiePort_3 pad_2b
Ports pad_2a pad_11 IDiePort_1 IDiePort_10
[End Package Circuit]
Parameters do not have Typ, Min, Max Values

## Slide 12: EMD-Like is Equivalent to BIRD 125
Equivalent if we use a simple Port naming convention
Defining sub circuit file/subckt are equivalent
BIRD 125 Parameter definitions can be enhanced to handle Typ Min Max
BIRD 125 can be enhanced to handle Touchstone File directly
Once [Pin Number] section can be removed from BIRD 125, EMD-Like and BIRD 125 are essentially equivalent with only syntactical differences.

## Slide 13: Subckt Example Shorthand
Parameter Tree Format
(DQ0
(IBIS-ISS_File <file>.iss)
(Subckt (Corner <typ subckt> <min subckt> <max subckt>))
(Parameters
(Framis <value>)
(Length (Corner <typ value> <min/slow value> <max/fast value>))
(Ports
(1 (Pin (Pin_number 4))
(2 (Pad (Pin_number 4)))
Examples using the following shorthand notation:
DQ0 ?.s2p Pin.4 Pad.4
?.s2p
(IBIS-ISS_File <file>.iss)
(Subckt (Corner <typ subckt> <min subckt> <max subckt>))
Corner Typ PackageModel.spi S_pkg

## Slide 14: Package Models
DQ0 ?.s2p Pin.4 Pad.4
DQ1 ?.s2p Pin.5 Pad.5
DQS ?.s4p Pin.6 Pin.7 Pad.6 Pad.7
A0 ?.s2p Pin.8 Pad.8
A1 ?.s2p Pin.9 Pad.9
Full ?.s12p Pin.4 Pin.5 Pin.6 Pin.7 Pin.8 Pin.9 Pad.4 Pad.5 Pad.6 Pad.7 Pad.8 Pad.9
PDN ?.s5p Pin.1 Pin.2 Pad.VDDQ_1 Pad.VDDQ_2 Pad.VDDQ_3

## Slide 15: On Die Models
DQ0 ?.s2p Pad.4 Buf.4
DQ1 ?.s2p Pad.5 Buf.5
DQS ?.s4p Pad.6 Pad.7 Buf.6 Buf.7
A0 ?.s2p Pad.8 Buf.8
A1 ?.s2p Pad.9 Buf.9
Full ?.s12p Pad.4 Pad.5 Pad.6 Pad.7 Pad.8 Pad.9 Buf.4 Buf.5 Buf.6 Buf.7 Buf.8 Buf.9
PDN ?.s9p Pad.VDDQ_1 Pad.VDDQ_2 Pad.VDDQ_3 Buf_PUR.4 Buf_PUR.5 Buf_PUR.6 Buf_PUR.7 Buf_PUR.8 Buf_PUR.9

## Slide 16: Merging On-Die Model into Package Model
DQ0 ?.s2p Pin.4 Buf.4
DQ1 ?.s2p Pin.5 Buf.5
DQS ?.s4p Pin.6 Pin.7 Buf.6 Buf.7
A0 ?.s2p Pin.8 Buf.8
A1 ?.s2p Pin.9 Buf.9
Full ?.s12p Pin.4 Pin.5 Pin.6 Pin.7 Pin.8 Pin.9 Buf.4 Buf.5 Buf.6 Buf.7 Buf.8 Buf.9
PDN ?.s5p Pin.1 Pin.2 Buf_PUR.4 Buf_PUR.5 Buf_PUR.6 Buf_PUR.7 Buf_PUR.8 Buf_PUR.9

## Slide 17: Signal Name Supply (PDN) Ports
Pin_Sig.<signal name>
  All pins on this signal name are shorted together
Pad_Sig.<signal name>
  All pads on this signal name are shorted together
Buf_Sig.<signal name>
  All buffer PUR, PDR, PCR, and GCR on this signal name are shorted together and connected to this PDN Port
Example PDN circuits using Signal Name Supply Ports
PDN ?.s2p Pin_Sig.VDDQ Pad_Sig.VDDQ
PDN ?.s2p Pad_Sig.VDDQ Buf_Sig.VDDQ
PDN ?.s2p Pin_Sig.VDDQ Buf_Sig.VDDQ
PDN ?.s7p Pin_Sig.VDDQ Buf_PUR.4 Buf_PUR.5 Buf_PUR.6 Buf_PUR.7 Buf_PUR.8 Buf_PUR.9

## Slide 18: Model Name Signal (I/O) Ports
Pin_Mod.<model name>
  This port connects to the pin of a <model name> buffer
Pad_Mod.<model name>
  This port connects to the die pad of a <model name> buffer
Buf_Mod.<model name>
  This port connects to the I/O of a <model name> buffer
Example circuits using Model Name Supply Ports
DQ ?.s2p Pin_Mod.DQ Buf_Mod.DQ
DQ ?.s6p Pin_Mod.DQ Pin_Mod.DQ Pin_Mod.DQ
Buf_Mod.DQ Buf_Mod.DQ Buf_Mod.DQ
DQ1 ?.s6p L=.5 Pin.5 Pin_Mod.DQ Pin_Mod.DQ
Buf.5 Buf_Mod.DQ Buf_Mod.DQ

## Slide 19: Next Decisions
Do we support sNp directly without requiring they be wrapped in a subckt?
Port naming options
  Can we identify signal (I/O) ports using Signal_name?
  Can we identify supply (PDN) ports using Signal_name?
  Can we identify signal (I/O) ports using Model_name?
Syntax Details
  Should Parameters have Typ, Min, Max values?

## Slide 20: Conclusion
Interconnect subcircuit ports can have a naming protocol that uniquely identifies each pin, die pad and buffer terminal that can be used at each port of a package or on-die interconnect model.
The port naming protocol can be extended to classes of ports such as signal name, or model name in addition to pin number and die pad name.
Port naming protocol can be parameter tree, or shorthand naming convention.
EMD-Like and BIRD 125 are functionally similar, just syntactical details.