## Slide 1: IBIS-ISS Package Proposal Status
Walter Katz
IBIS ATM
January 7, 2014

## Slide 2: Overview
Decisions Made
What These Decisions Mean
Active Questions
Intent of this proposed syntax
New Keywords
  [Begin Package Models]
  [Begin Package Model]
  Language
  File
  Subckt
  Parameter
  Enhanced Parameter Formats
  Ports
  Sparse_Ports
Rules
  Port Naming Rules
  Signal (I/O) Port Naming Rules
  Supply (PDN) Port Naming Rules
  Unconnected Port Naming Rules
  Port Rules
Issues to be resolved, Next Steps
While we are at it

## Slide 3: Decisions Made
Decisions Made | In .ibs | In EMD
Connectors | No | Yes
Cables | No | Yes
Broadband EBD | No | Yes
MCM | No | Yes
Interposers | No | Yes
3-D structures | No | Yes
Stacked Memory | No | Yes
Splits/Joins of Signal (I/O) in Pacxkage or Die | No | Yes
RDL as separate element | No | Yes
New list of supply (PDN) die pads | Yes | Yes
Separate package and on-die interconnect model | Yes | Yes
Package model can include on-die model | Yes | Yes
Broadband I/O Package Modeling | Yes | Yes
Package PDN | Yes | Yes
Broadband I/O On-Die Modeling | Yes | Yes
On-Die PDN | Yes | Yes
Interconnect coupling (crosstalk) between I/O and I/O | Yes | Yes
Interconnect coupling between I/O and PDN | Yes | Yes
Optical Interconnect | No | No

## Slide 4: What These Decisions Mean
For signal (I/O) pins there is a one to one correspondence between Pin Number, Die Pad, and Buffer.
There is a Few to Many or Many to Few relationship between supply (PDN) pins and supply die pads, and buffer Pullup, Pulldown, Power Clamp and Ground Clamp Reference terminals.
There MAY be a one to one correspondence between signal (I/O) Pin Numbers and Signal Names (IBIS 6.0 is not clear on this).

## Slide 5: Active Questions
Do we support sNp directly without requiring they be wrapped in a subckt?
  Recommend Yes.
Port naming options
  Can we identify signal (I/O) ports using Signal_name?
    Recommend No.
  Can we identify supply (PDN) ports using Signal_name?
    Recommend Yes.
  Can we identify signal (I/O) ports using Model_name?
    Recommend Maybe.
Syntax Details
  Should Parameters have Typ, Min, Max values?
    Recommend Yes.
  Should Parameters have additional functionality (e.g. List, Range, Increment, …) ?
    Recommend Maybe.

## Slide 6: Intent of this proposed syntax
This is a proposed syntax that satisfies the requirement discussed in last weeks IBIS-ATM meeting. I took the liberty of adding some limited support for Touchstone Files, supporting Ports that reference Model Names, and some extended Parameter capabilities. These are functionality that we could support with additional usage rules.
Although we may not choose to support Touchstone files, Ports that reference Model Names and extended Parameter capabilities, I want us to use a syntax that could be easily extended to include these capabilities.
This syntax is a compromise between BIRD 125 and EMD-Like. It has most of the flexibility of parameter tree format, while keeping the IBIS line oriented format: “keyword <values>”

## Slide 7: [Begin Package Models]
Keyword: [ Begin Package Models]
Required: No
Description: New Section within [Component] containing IBIS-ISS Package and On-Die interconnect models
Sub-Params: [End Package Models], [Begine Package Model], [End Package Model]
Usage Rules: This section within [Component] contains one or more package or on-die interconnect models.
Example::
[Begin Package Models]
…
[End Package Models]

## Slide 8: [Begin Package Model]
Keyword: [Begin Package Model], <Package Model Name>
Required: No
Description: New Section within [ Begin Package Models] that defines an interface to a IBIS-ISS subckt or Touchstone File.
Sub-Params: [End Package Model], Language, File, Subckt, Parameter, Ports
Usage Rules: This section within [Begin Package Models] defines an interface to a IBIS-ISS subckt or Touchstone File.
Example::
[Begin Package Models]
[Begin Package Model] DQ1
…
[End Package Model]
[Begin Package Model] DQ2
…
[End Package Model]
[End Package Models]

## Slide 9: Language
Keyword: Language <language>
Required: Yes
Description: Language is either IBIS-ISS or Touchstone
Sub-Params: None
Usage Rules: This Keyword within [Begin Package Model] determines if the model is a IBIS-ISS subckt or a Touchstone file
Examples:
[Begin Package Model] DQ1
Language IBIS-ISS
…
[End Package Model]
[Begin Package Model] DQ2
Language Touchstone
…
[End Package Model]

## Slide 10: File
Keyword: File <format> <file name> {<file name> <file name> }
Required: Yes
Description: Defines the file(s) used by this package model
Sub-Params: None
Usage Rules: <format> is either Value or Corner. If <format> is Value, then requires one <file name>. If <format> is Corner, then requires three <file name>., interpreted as Typical, Slow and Fast. If Language is IBIS-ISS then the file(s) shall contains IBIS-ISS subckts. If Language is Touchstone then the file(s) shall be a Touchstone I or II file.
Examples:
[Begin Package Model] DQ2
Language IBIS-ISS
File Value DQ2_.iss
…
[End Package Model]
[Begin Package Model] DQ3
Language Touchstone
File Corner DQ3_Typ.s2p DQ3_Slow.s2p DQ3_Fast.s2p
…
[End Package Model]

## Slide 11: Subckt
Keyword: Subckt <format> <subckt name> {< subckt name> < subckt name> }
Required: Yes, if Language IBIS-ISS
Description: Defines the subckts (s) used by this IBIS-ISS package file
Sub-Params: None
Usage Rules: <format> is either Value or Corner. If <format> is Value, then requires one < subckt name>. If <format> is Corner, then requires three < subckt name>., interpreted as Typical, Slow and Fast.
Examples:
[Begin Package Model] DQ1
Language IBIS-ISS
File Value DQ1.iss
Subckt Corner DQ1_Typ DQ1_Slow DQ1_Fast
…
[End Package Model]
[Begin Package Model] DQ2
Language IBIS-ISS
File Corner DQ2_Typ.iss DQ2_Slow.iss DQ2_Fast.iss
Subckt Value DQ2
…
[End Package Model]

## Slide 12: Parameter
Keyword: Parameter <parameter name> <format> <value> < value > …
Required: No
Description: Defines a parameter passed to an IBIS-ISS subckt instance
Sub-Params: None
Usage Rules: <parameter name> is the name of a parameter passed to an IBIS-ISS subckt instance. Language must be IBIS-ISS. <format> is either Value or Corner. If <format> is Value, then requires one <value>. If <format> is Corner, then requires three < value >, interpreted as Typical, Slow and Fast. There may be none, one, or any number of Parameter keywords within a [Begin Package Model]
Examples:
[Begin Package Model] DQ1
Language IBIS-ISS
File Value DQ1.iss
Subckt Value DQ1
Parameter Length Value 1.3
Parameter Wline Corner ‘wline_typ’ ‘wline_slow’ ‘wline_fast’
…
[End Package Model]

## Slide 13: Enhanced Parameter Formats
Other possible <formats> that can be considered are:
  Gaussian <mean> <sigma>
  IntegerRange <min> <max>
  RealRange <min> <max>
  PDF <value> <probability> <value> <prob.> <value> <prob.> …
  List <value> <value> <value> <value> <value> …
Each <format> requires a definition of “Typ”
  Corner <typ>
  Gaussian <mean>
  IntegerRange (<min>+<max>)/2. (round down)
  RealRange (<min>+<max>)/2.
  PDF Mean|Median|Mode
  List FirstValue | MiddleValue
Three types of Parameter Value Selection
  All Parameters are Typ
    This is the current IBIS Package Modeling capability
  Corner Parameter are Typ|Slow|Fast (rest are Typ)
    Compatible with rest of IBIS using (Typ Min Max)
  User/EDA tool can select any allowed value for each Parameter
    “AMI Flexibility” to support more than 3 corners, DOE, …

## Slide 14: Ports
Keyword: Ports <port> <port> <port> <port> <port> <port> …
Required: No
Description: Defines the node names associated with the Ports (Terminals) of an IBIS-ISS subckt or a Toushtone file
Sub-Params: None
Usage Rules: Ports must be allowed <port> names that correspond to either a Component Pin, Component Die Pad, or Buffer Terminal. The order of the <ports> shall be the order of the Terminals of the IBIS-ISS subckt or Touchstone file. There may be more than one Ports keyword in a [Begin Package Model] . If there are more than one Ports record in a [Begin Package Model], then subsequent Ports records after the first Port record shall be considered continuation lines, and the <ports> shall be concatenated.

## Slide 15: Sparse_Ports
Keyword: Sparse_Ports <port #> <port> <port #> <port> …
Required: No
Description: Defines the node names associated with the Ports (Terminals) of an IBIS-ISS subckt or a Touchtone file
Sub-Params: None
Usage Rules: Sparse_Ports must be followed by port number and port names pairs. The port number must be a positive integer numerically less than or equal to the number of ports in the subckt, or Touchstone file. A port number may appear only once in the list of pairs. The port name must correspond to either a Component Pin, Component Die Pad, or Buffer Terminal. There may be more than one Sparse_Ports keyword in a [Begin Package Model] . If there are more than one Sparse_Ports record in a [Begin Package Model], then subsequent Sparse_Ports records after the first Port record shall be considered continuation lines.

## Slide 16: Signal (I/O) Port Naming Rules
Pin I/O
  Pin.<pin_number>
  Pin_Mod,<model_name>
  Pin_Mod+,<model_name>
  Pin_Mod-,<model_name>
Die Pad I/O
  Pad.<pin_number>:
  Pad_Mod.<model_name>
  Pad_Mod+.<model_name>
  Pad_Mod-.<model_name>
Buffer Terminal I/O
  Buf.<pin_number>
  Buf_Mod/<model_name>
  Buf_Mod+ .<model_name>
  Buf_Mod- .<model_name>

## Slide 17: Model Type Package Models
Input and I/O Ports
  I_Pin.<n>, I_Pad.<n>, I_Buf.<n>
  VI_Pin.<n>, VI_Pad.<n>, VI_Buf.<n>
Output and I/O Ports
  O_Pin.<n>, O_Pad.<n>, O_Buf.<n>
  VO_Pin.<n>, VO_Pad.<n>, VO_Buf.<n>
Input, Output and Input/Output Ports
  IO_Pin.<n>, IO_Pad.<n>, IO_Buf.<n>
  VIO_Pin.<n>, VIO_Pad.<n>, VIO_Buf.<n>
Differentials: I+, I-, …VIO_Buf+, VIO_Buf-
Ports with same <n> are connected
All Ports with same <n> must have same I,VI,O,VO,IO,VIO
If there are V Ports then they are valid Victim Ports

## Slide 18: Package Precedence Rules
Match by Pin, Pad, and Buf Ports
Match by Pin_Mod, Pad_Mod, Buf_Mod Ports
Match exactly by I, O, IO Ports
  I Input
  O Output
  IO I/O
Match by I, O, IO Ports
  I Input or I/O
  O Output or I/O
  IO Input, Output, I/O

## Slide 19: Example Default Model
[Begin Package Models]
[Begin Package Model] Single_Ended
Language Touchstone
File Corner SE_Typ.s2p SE_Slow.s2p SE_Fast.s2p
Ports IO_Pin.1 IO_Buf.1
[End Package Model]
[Begin Package Model] Differential
Language Touchstone
File Corner Diff_Typ.s4p Diff_Slow.s4p Diff_Fast.s4p
Ports IO+_Pin.1 IO-_Pin.1 IO+_Buf.1 IO-_Buf.1
[End Package Model]
[End Package Models]

## Slide 20: Nine Corner Crosstalk Model
[Begin Package Model] 9_Corner_Xtalk
Language IBIS-ISS
File Delay_Corner Typ.mod Fast.mod Slow.mod
Subckt Xtalk_Corner TypXtalk MinXtalk MaxXtalk
Ports IO_Pin.1 IO_Buf.1 VIO_Pin.2 VIO_Buf.2 IO_Pin.3 IO_Buf.3
[End Package Model]
[Begin Package Model] Diff_9_Corner_Xtalk
Language IBIS-ISS
File Delay_Corner Diff_Typ.mod Diff_Fast.mod Diff_Slow.mod
Subckt Xtalk_Corner TypXtalk MinXtalk MaxXtalk
Ports IO_Pin+.1 IO_Pin-.1 IO_Buf+.1 IO_Buf-.1
Ports VIO_Pin+.2 VIO_Pin-.2 VIO_Buf+.2 VIO_Buf-.2
Ports IO_Pin+.3 IO_Pin-.3 IO_Buf+.3 IO_Buf-.3
[End Package Model]

## Slide 21: Supply (PDN) Port Naming Rules
Pin PDN
  Pin.<pin_number>
  Pin_Sig.<signal_name>
Die Pad PDN
  Pad.<die_supply_pad_name>
  Pad_Sig.<signal_name>
Buffer Terminal Supply (PDN)
  Buf_PUR.<pin_number>
  Buf_PDR.<pin_number>
  Buf_PCR.<pin_number>
  Buf_GCR.<pin_number>
  Buf_Sig.<signal_name>

## Slide 22: Unconnected Port Naming Rules
Several Options
  R.<value>
    Connect this node to GND with a resistance of <value>
    <value> can be either
      Non-negative IBIS number
        Treated as Resistance in Ohms
      Blank
        Can only be used when Language Touchstone
        Simulator shall use the Tstonefile reference resistance of the port in ohms.
  S.<file>.<subckt>
    <subckt> shall be a single Port sub–circuit in IBIS-ISS <file>
  0
    Language is IBIS-ISS
      Equivalent to R.0
    Language Touchstone
      Tstonefile reference resistance of the port in ohms.

## Slide 23: Port Rules
The model creator is responsible for the data in each package model (Language, File, Subckt, Parameter, and Ports) are consistent and follow the following rules:
  Package Models may have the following combinations of Ports:
    Pins and Pads (Package only models)
    Pads and Buffer (On-Die only Models)
    Pins and Buffer (combined package and on-die models.
  If there are any Pin_Mod(+/-), Pad_Mod(+/-) or Buf_Mod(+/-) ports, then all I/O ports must be either Pin_Mod(+/-), Pad_Mod(+/-) or Buf_Mod(+/-) ports, and the interconnect model may only represent a single “channel”, i.e. crosstalk or coupling is not supported with such models.
    We could support crosstalk by assuming the above port names are victim port names and that aggressor ports would be named Pin_Mod(+/-)<n>, Pad_Mod(+/-)<n> or Buf_Mod(+/-)<n>, where <n> would identify each unique aggressor.

## Slide 24: Issues to Be Resolved, Next Steps
Decisions that are still unresolved
  Can we identify signal (I/O) ports using Model_name (uncoupled)?
  Can we identify signal (I/O) ports using Model_name (with crosstalk)?
  Can we identify signal (I/O) ports using Model_type (with and without crosstalk)?
  Should Parameters have additional functionality (e.g. List, Range, Increment, …)?
  Corner? Typ/Slow/Fast Typ/LessXtalk/MoreXtalks
Next steps
  Review Syntax
  Make EMD Syntax similar

## Slide 25: While we are at it
Allow all Pin Names (aka Pin number) in IBIS Component and EBD to be 40 characters
  Pin_names in [Pin List] cannot exceed 8 characters
  Pin names in [Pin] cannot exceed 5 characters
Allow upper and lower case file names
Allow lines longer that 120 characters, e.g.
  256 characters
  512 characters
  1000 characters
  4000 characters