## Slide 1: BIRD 166 Redriver Flow
Walter Katz
SiSoft
April 4, 2017

## Slide 2: Repeater Link
Repeater
Rx
Tx1
Rx1
Tx2
Rx2
channel 1
channel 2
Repeater
Repeater Tx
Incoming
(upstream)
channel
outgoing
(downstream)
channel

## Slide 3: Rx2 Input Impulse Response (IR)
In order for the Rx AMI_Init function to optimize itself correctly, the Impulse Response (IR) input must contain all the upstream equalization and channel.
  Retimer IR should include
      Channel 2
      Tx2 equalization
  Redriver IR should include
      Channel 2
      Tx2 equalization
      IR output of Rx1

## Slide 4: In the Current Redriver Flow
IR input to Rx2
  Channel 2
  Tx2 equalization
The Rx1 output is included by convolving the Rx1 IR output with the Rx2 IR output.

## Slide 5: Source of Problem is Tx can Optimize Itself
It is legal for Tx2 to optimize itself to open the eye at the Rx2 input.
Non-Repeater flow requires that the input to the Tx is the downstream channel.
The current redriver flow is flawed because it does not give the Tx the opportunity to optimize itself based on the actual IR at the Rx2 input which includes the Rx1 IR output.

## Slide 6: Simple Solution
The IR input to Tx2 should be the convolution of the downstream channel (Channel 2) with the IR output of Rx1.
The IR output of Rx2 should not be convolved with the IR output of Rx1.

## Slide 7: BIRD 166 simplified BIRD 166.1