## Slide 1: Problems in BIRD166 Flow
Fangyi Rao
Keysight Technologies

## Slide 2: BIRD166 Flow
Rx1 output IR includes Tx1 EQ, channel 1 and Rx1 EQ
Tx2 output IR includes Tx2 EQ and channel 2
Rx2 input IR includes Tx1 EQ, channel 1, Rx1 EQ, Tx2 EQ and channel 2
Rx2 output IR includes Tx1 EQ, channel 1, Rx1 EQ, Tx2 EQ, channel 2 and Rx2 EQ
For simplicity, consider Rx2 only has DFE,
DFE is included in IR by adding to but not convolving with Rx2 input IR
Tx2
Rx2
Channel 2
Tx1
Rx1
Channel 1
∗

## Slide 3: Case: Rx1 has GetWave, Tx2 and Rx2 are Both Init-only
Denote input digital waveform to Tx1 as d(t)
Denote Rx1 GetWave output waveform as VRx1GW(t)
Rx2 output waveform Vout(t) = VRx1GW(t) h2, where h2 includes Tx2 EQ, channel 2 and Rx2 EQ
In BIRD166 flow Rx2 Init doesn’t return h2 and h2 has to be obtained by deconvolution
Tx2
Rx2
Channel 2
Tx1
Rx1
Channel 1
?

## Slide 4: Rx2 has GetWave, Tx2 and Rx2 are both Init-only (cont’d)
Now rewrite Rx1 GetWave output as VRx1GW(t) = d(t)h1 + dV. Here dV represents
Nonlinearity in Rx1, e.g. limiting mode redriver and compression
Redriver internal noise
Xtlk signals that enter Rx1
Tx2
Rx2
Channel 2
Tx1
Rx1
Channel 1
Note that . If upstream channel has X dB loss, then
redriver nonlinearity, noise and xtlk are amplified by X dB when they reach Rx2 DFE

## Slide 5: Summary
This problem is caused by having to obtain h2 by deconvolution, which in turn is caused by including upstream channel IR h1 in the input IR to Rx2 Init
Problems of deconvolution intensify with the presence of redriver
Can’t be resolved by incremental changes of current flow
Tx2
Rx2
Channel 2
Tx1
Rx1
Channel 1