## Slide 1: To Dual Or Not To Dual That Is The Question
Walter Katz
SiSoft
May 16, 2017

## Slide 2: There Are Three AMI Model Configurations
Init-Only
  Init_Returns_Impulse True
  GetWave_Exists False
GetWave-Only
  Init_Returns_Impulse False
  GetWave_Exists True
Dual
  Init_Returns_Impulse True
  GetWave_Exists True

## Slide 3: Additional Configuration Subtleties
AMI_GetWave functions may operate differently depending on the impulse response input to their AMI_Init, whether the Init_Returns_Impulse is True or False.

## Slide 4: The Flows Described in IBIS 6.1 with BIRD 166.3 are Valid If
Statistical Flow is valid if
  Every model in the simulation has
    Init_Returns_Impulse True
Time Domain Flow is valid if
  Every non-terminal model in the simulation has
    Init_Returns_Impulse True
    GetWave_Exists True
  Terminal Rx Model
    GetWave_Exists True
    No requirement on Init_Returns_Impulse

## Slide 5: Problematic Flows
The Statistical Flow is problematic if any model has Init_Returns_Impulse False
  The simulator would need to infer the impulse response of the equalization from the GetWave output of the model. This can be done, and there are papers describing how do this, but it requires sophisticated mathematical operations on the input and output waveforms and these operations can be unstable.
The Time Domain Flow is problematic if any model has Init_Returns_Impulse False
  Some GetWave models have their equalization determined by the impulse response input to their AMI_Init function (whether Init_Returns_Impulse is True or False).
  Exceptions are Rx models at the terminus of a channel or Rx models in Repeater/Retimers.

## Slide 6: Problematic Configurations (continued)
The Time Domain Flow is problematic if any model has GetWave_Exists False
  In order to do time domain simulations, the simulator must create a “proxy” AMI_GetWave function by mathematical operations on the input and output impulse responses of its AMI_Init function (such as de-convolution)
The Time Domain Flow is very problematic if there are some models that have GetWave_Exists=False and some other models that have Init_Returns_Impulse=False.
  This just compounds the problems in the previous two configurations.

## Slide 7: Ways To Fix Init-Only Models
Model makers should never deliver Init-Only models.
How to fix Init-Only Models
  Init-Only models can be easily converted to Dual Models.
  One suggestion is to make the source code available that has the plumbing to enable model makers to do this on their own models.
  A BIRD proposed by Keysight is an alternative
    Adds additional impulse response outputs that allow simulator to create a proxy AMI_GetWave without doing deconvolution
    Requires additional functionality in the AMI_Init function and the EDA tool
    Is it any easier than just writing the AMI_GetWave function and making it a Dual Model?

## Slide 8: Ways To Fix Tx GetWave-Only Models
Tx AMI Models are always (almost always) LTI, and therefore can and should be represented well in AMI_Init.

## Slide 9: Ways To Fix Rx GetWave-Only Models
An Rx terminal model has a clock that is recovered from the data that is used to sample the data. The models are found at the terminus of a channel or in Repeater/Retimers. These models are valid for Time Domains simulations.
An Rx Repeater/Redriver Model that is GetWave-Only will not be able to influence the AMI_Init inputs to the downstream Tx and Rx models.

## Slide 10: Conclusion
IBIS should make it clear that Dual models are preferred, with the only exception of Rx models that are terminal models (i.e. not used in a Repeater Redriver)
  There is no real excuse for any Init-Only models.
  There is no real excuse for a Tx GetWave-Only model
One Problematic Case – Rx Model in Repeater/Redriver
  Rx Models in Redrivers typically have a CTLE and AGC (filter and gain).
  The filter/gain are often designed to saturate.
  AMI_Getwave is required to represent this saturation accurately.
  Model maker should still output an AMI_Init with a best approximation of the Rx equalization when the downstream Rx models require an impulse response of the full upstream channel to set the equalization for its AMI_GetWave.