## Slide 1: Back Channel Statistical Training Supported in IBIS
Walter Katz
Signal Integrity Software, Inc.
September 3, 2019

## Slide 2: Overview
Justification
New AMI DLL Function, Parameters
Communication Mechanism Between the DLL’s
Statistical Training Flow
How to Proceed
  How to resolve BIRD issues
  Develop, in parallel, a DDR5 DQ Write Protocol

## Slide 3: Justification
Capability requested by SiSoft and MathWorks customers (IC Vendors and Users)
Personal experience in developing optimization algorithms based on statistical models in QCD and SerDes Toolbox.
Desire to move these algorithms into Tx and/or Rx AMI models in an IBIS compliant way.
Enable all EDA companies to support BCI optimization in both Statistical and/or Time Domain modes.

## Slide 4: Will Require a “New Function” Like AMI_Init and …
Uses, does not allocate memory handle
Protocol determines the information transfer between the Tx and Rx (and Repeater DLLs if present)
Need to determine communication mechanism between the DLL’s
Need new reserved parameter to indicate if BCI Statistical is available and how to apply it
  (BCI_Training_Type (List “GetWave” “TBD” “Both”) …
Use existing BIRD 147 reserved parameters

## Slide 5: “New Function” Like AMI_Init
Function: AMI_Init
Required: Yes
Declaration: long AMI_Init (double *impulse_matrix,
long number_of_rows,
long aggressors,
double sample_interval,
double bit_time,
char *AMI_parameters_in,
char **AMI_parameters_out,
void **AMI_memory_handle,
char **msg)

## Slide 6: “New Function” Like AMI_Init
Function: AMI_<TBD>
“Old Function” AMI_Resolve, AMI_Init, AMI_<TBD> , AMI_GetWave, AMI_Close
Some proposed names AMI_Impulse, AMI_GetImpulse,AMI__Sussudio, AMI_TBD, …
Required: No
Declaration: long AMI_<TBD> (double *impulse_matrix,
long number_of_rows,
long aggressors,
double sample_interval,
double bit_time,
char *AMI_parameters_in,
char *BCI_parameters_in,
char **BCI_parameters_out,
char **AMI_parameters_out,
void *AMI_memory**AMI_memory_handle,
char **msg)

## Slide 7: Communication Mechanism Between the DLL’s
Could be file I/O like in BIRD 147
  EDA tool does nothing different then AMI_Init calls, except it calls “New Functions” iteratively.
Could be strings generated by one AMI_<TBD> and passed into the other AMI_<TBD>
  EDA tools needs to use output string pointer from one AMI_<TBD> (**BCI_parameters_out) as an input string pointer to the other AMI_<TBD> (**BCI_parameters_in).
  Will improve performance, especially if large amounts of data is communicated between the AMI_<TBD>.
Other suggestions?

## Slide 8: Statistical Training Flow
EDA tool will alternatively call the Tx and Rx AMI_<TBD> if
  Training is On
  BCI Statistical is allowed and enabled on Tx and Rx
Training stops when “Converged”, or …
Results of last call to “new function” should be used for statistical analysis
Can go on to GetWave, which could also have training enabled.

## Slide 9: How I Propose Proceeding
Schedule brainstorming sessions to:
  Determine the AMI_<TBD> name
  Determine communication mechanism between the DLL’s
  Determine the AMI_<TBD> arguments
  Determine new Reserved Parameter(s)
    Tells EDA tool if model can do Statistical and/or GetWave Training
    Tells Model if it is doing Statistical and/or GetWave Training
  Develop a DDR5 DQ Write BCI Protocol.
    Invite additional memory and controller vendors
  Develop a Generic Tx N-Tap FFE BCI Protocol.