## Slide 1: BIRD 198 Response
Walter Katz
Signal Integrity Software, Inc.
September 10, 2019

## Slide 2: Comments on BIRD 198.1
I do not understand what their model selector concept was.
I totally object to having a new Model_type.
So the questions I would have:
  Is it enough to have a list of [PDN Model]s that had two terminals, each being a bus_label or signal_name, and 3 parameters, [C pdn], [R pdn], [R leak]
  Should the names be [Cpdn], [Rpdn], [Rleak]
    [Rgnd], [Rpower], [Rac], [Cac]
  Why do we a need a model selector?
  Do we really need bus_label, or is signal_name enough
How does it interact with BIRD 189 on-die PDN Models
  Use Both – By far the easiest to implement and document
  If use one, not the other.
  Complicated overlapping rules.
What does corner mean?
  Magnitude Typ, Min, Max
  Correlated with IV/VT curve Typ, Min, Max
I personally though that these would always have been enough for on-die PDN.

## Slide 3: Simple Format
New section under [Component], [On Die PDN Models]
[On Die PDN Models]
  [Corner] Process|Magnitude ???
  [PDN Model] VDDAVSS
    [Rail Bus Labels] VDDA VSS | (Note) Bus_Labels can be Rail signal names
    [C pdn] 3n 2.9n 3.1
    [R pdn] .1 .1 .1
    [R leak] 200 200 200
  [End PDN Model]
  [PDN Model] VDDBVSS
    [Rail Bus Labels] VDDB VSS
    [C pdn] 3n 2.9n 3.1
    [R pdn] .1 .1 .1
    [R leak] 200 200 200
  [End PDN Model]
[End On Die PDN Models]