## Slide 1: BIRD201/BIRD147 Back-channel Protocol Generic_Tx
Walter Katz
IBIS-ATM
February 4, 2020

## Slide 2: General fBCI Flow
Tx_Read reads Rx rx2tx protocol data,
Tx_Write writes Tx tx2rx protocol data
Rx_Read reads Tx tx2rx protocol data
Rx_Write writes Rx rx2tx protocol data
If BCI_State is still “Training” then go to Step 1 above.

## Slide 3: What the Tx tells the Rx First Time
(BCI
  (BCI_State “Training”)
  (WhoAmI “Tx”)
  (Sequence “1”)
  (Pre_cursor_taps 1)
  (Post_cursor_taps 2)
  (Taps
  (-1 0 -5 0 .01) | <tap #> <current register value> <min register value>
  <max register value> <current analog tap value>
  (1 0 -20 0 .01)
  (2 0 -10 0 .01)))
(BCI
  (BCI_State “Training”)(WhoAmI “Tx”)(Sequence “1”)(Pre_cursor_taps 1)(Post_cursor_taps 2)Taps((-1 0 -5 0 .01)(1 0 -20 0 .01)(2 0 -10 0 .01)))

## Slide 4: What the Rx tells the Tx Every Time
(BCI
  (BCI_State “Training”)
  (WhoAmI “Rx”)
  (Sequence “2”) | always one more then (Sequence from last Tx output
  (Taps_Register
  (-1 -1) | Requested tap-1 register value = -1
  (1 -4) | Requested tap1 register value = -4
  (2 -2))) | Requested tap2 register value = -2
(BCI
  (BCI_State “Training”)(WhoAmI “Rx”)(Sequence “2”) (Taps_Register (-1 -1) (1 -4) (2 -2))

## Slide 5: What the Rx tells the Tx Every Time (alternatives)
(BCI
  (BCI_State “Training”)(WhoAmI “Rx”)(Sequence “2”) (Taps_Register (-1 -1) (1 -4) (2 -2))
(BCI
  (BCI_State “Training”)(WhoAmI “Rx”)(Sequence “2”) (Taps_Value (-1 -.01) (1 -.04) (2 -.02))
(BCI
  (BCI_State “Training”)(WhoAmI “Rx”)(Sequence “2”) (Taps_Increment (-1 -1) (1 -1) (2 -1))

## Slide 6: What the Tx tells the Rx After First Time
(BCI
  (BCI_State “Training”)
  (WhoAmI “Tx”)
  (Sequence “3”)
  (Taps
  (-1 -1 -.01) | <tap #> <current register value> <current analog tap value>
  (1 -4 -.04)
  (2 -2 -.02)))
(BCI
  (BCI_State “Training”) (WhoAmI “Tx”) (Sequence “3”) (Taps (-1 -1 -.01)(1 -4 -.04) (2 -2 -.02)))