## Slide 1: DDR5 DQ Write Protocol
Walter Katz
Signal Integrity Software, Inc.
March 3, 2020

## Slide 2: Overview
BCI Statistical Methods
BCI DDR5 DQ Write Protocol based on iterating AMI_Impulse and AMI_GetWave

## Slide 3: (BCI …) String for DDR5 DQ Write Protocol
AMI_Impulse has two arguments used to communicate between the Tx and Rx
  **BCI_parameters_out
    Used to communicate to the other end
  * BCI_parameters_in
    Used to communicate from the other end
The EDA tool is responsible for setting *BCI_parameters_in to the **BCI_parameters_out of the other end
(BCI …) strings use same parameter tree format as in **AMI_parameters_out and *AMI_parameters_out
EDA tools need not parse this string (but could for parse it and report debug information as QCD does for GetWave)
Some communications (e.g. Rx AMI_Impulse to Tx AMI_GetWave may require BCI_ID file I/O.

## Slide 4: Tx (BCI …) Output
| Tx tells Rx how to set its gain and taps
(BCI
  (Sequence <sequence #>)
  (From “Tx”)
  (BCI_State “Training|Converged”)
  (Gain <gain register>) | Integer, (Range 0 -3 3)
  (VrefDQ <VrefDQ register>) | Integer, (Range 32 -1 63)
  (VrefDQ _V <VrefDQ Vref>) | Float, (Range 0.6 0.4 0.8)
  (DFE1 <tap1 register>) | Integer, (Range 0 -40 10)
  (DFE2 <tap2 register>) | Integer, (Range 0 -15 15)
  (DFE3 <tap3 register>) | Integer, (Range 0 -12 12)
  (DFE4 <tap4 register>) | Integer, (Range 0 -9 9)
  (DFE1_V <tap1 coefficient>) | Float, (Range 0.0 -0.200 0.50)
  (DFE2_V <tap2 coefficient>) | Float, (Range 0.0 -0.075 0.075)
  (DFE3_V <tap3 coefficient>) | Float, (Range 0.0 -0.060 0.060)
  (DFE4_V <tap4 coefficient>) | Float, (Range 0.0 -0.045 0.045))
(BCI(Sequence 1) (From “Tx”) (BCI_State “Training”) (Gain 0)
(VrefDQ -1)(DFE1 0 ) (DFE2 0 ) (DFE3 0 ) (DFE4 0))

## Slide 5: VrefDQ and DFE Taps Can be Integer Index Register or Floating Voltage Value
It is up to the Tx whether to specify DFE taps as integer register values or DFE coefficient voltage values.
It is up to the Tx whether to specify VrefDQ as an integer register value or float voltage.
The Rx must be able to support both methods.
Note that to support using VrefDQ, the Rx model must have DC_Offset in its .AMI file.
If the Tx specifies Index Resister values, the Rx would return the voltage values used.
If the Tx specifies float voltage values, the Rx would return the integer index values used.

## Slide 6: Rx (BCI …) Output
| Rx sets up Gain and DFE taps from Tx instructions in Tx (BCI …)
| Rx tells Tx what it did with the following (BCI …)
(BCI
  (Sequence <sequence>)
  (From “Rx”)
  (BCI_State “Training”)
  (BER <used BER>) | May be > 1e-16, if no 1e-16 contour
  (VrefDQ <VrefDQ used by Rx when input VrefDQ = -1>)
  (VrefDQ <VrefDQ register>) | Integer, (Range 32 -1 63)
  (VrefDQ _V <VrefDQ Vref>) | Float, (Range 0.6 0.4 0.8)
  (DFE1 <tap1 register>) | Integer, (Range 0 -40 10)
  (DFE2 <tap2 register>) | Integer, (Range 0 -15 15)
  (DFE3 <tap3 register>) | Integer, (Range 0 -12 12)
  (DFE4 <tap4 register>) | Integer, (Range 0 -9 9))
  (DFE1_V <tap1 coefficient>) | Float, (Range 0.0 -0.200 0.50)
  (DFE2_V <tap2 coefficient>) | Float, (Range 0.0 -0.075 0.075)
  (DFE3_V <tap3 coefficient>) | Float, (Range 0.0 -0.060 0.060)
  (DFE4_V <tap4 coefficient>) | Float, (Range 0.0 -0.045 0.045))\
  (Eye_Height <eye height at used BER>)
  (Eye_Width <eye width at used BER>)
  (Eye_Area <eye area at used BER>) )
(BCI (Sequence 1) (BCI_State “Training”) (From “Rx”) (BER 1e-16)
(VrefDQ 32) (VrefDQ_V 0.6) (DFE1_V 0.0 ) (DFE2_V 0.0 ) (DFE3_V 0.0 ) (DFE4_V 0.0 )
(Eye_Height .3) (Eye_Width 50e-12) (Eye_Area 30e-12) )

## Slide 7: This is All There Is
This is the extent of the DDR5 DQ Write Protocol
The protocol will include a detail method for the Rx to calculate the Eye Height and Eye Area Metrics from an Impulse Response
Memory and Controller vendors may want to add jitter and noise impairments to the protocol
Memory and Controller vendors may want to add additional or alternative metrics