## Slide 1: Alternative DQ DQS Clocking BIRD
Walter Katz
IBIS-ATM
April 7, 2020

## Slide 2: Overview
Background
Introduce a new BIRD that DQ *clock_times can be used as an input as well as an output. As an input it can be
  Ignored (as it is today)
  DQS *clock_times output
  DQS *wave output
One new AMI Reserved Parameters
Advantages

## Slide 3: Background
For DDR5 channels the skew between DQ and DQS has two components:
  The N*UI skew (e.g. from a DQS clock tree)
  The fine skew to get the DQS clock at the center of the DQ eye.
It would be nice to have a DDR5 DQ Rx model that has as input both the DQ waveform and either the DQS clock tics or DQS waveform to be able to correctly locate the clock in each UI of a DQ waveform.

## Slide 4: This Alternative BIRD
The *clock_times array that is passed to the DQ GetWave can
  Contents ignores as in the IBIS 7.0 specification
  Contain the *clock_times output of the DQS GetWave
  Contain the *wave output of DQS GetWave

## Slide 5: New AMI Reserved Parameter Rx_Use_Clock_Input
New DQ Reserved Parameter Rx_Use_Clock_Input
  (Rx_Use_Clock_Input (Usage In)(Type “String”)
  (List “None” ”Times” ”Wave”) (Description
  “This model supports using DQS *clock_time or *wave output”))
Other List options:
  (List “None” ”Times”) (Description
    “This model supports using DQS *clock_time output”)
  (List “None” ”Wave”) (Description
    “This model supports using DQS *wave output”)

## Slide 6: Similar to GetWave2 BIRD except at step 2: *clock_times contains either DQS *clock_times or DQS *wave.
+
-
…
…
DQ0
DQ Tx DLL
DQS Tx DLL
DQ Tx DLL
DQ7
DQS0
+
-
…
…
DQ8
DQ Tx DLL
DQS Tx DLL
DQ Tx DLL
DQ15
DQS1
DQ0
DQ7
+
-
+
-
DQS0
DQ8
DQS1
DQ15
…
…
…
…
DQS Rx DLL
DQ Rx
*clock_times
DQ Rx
*clock_times
DQS Rx DLL
DQ Rx
GetWave2
DQ Rx
GetWave2
1
1
1
1
1
1
2
2
3
3
3
3
Step 1: compute analog channel output according to IBIS 5.1-7.0 (crosstalk taken into account)
Step 2: compute output of all DQS Rx DLLs according to IBIS 5.1-7.0
Set DQ *clock_times pointer to DQS *clock_times or *wave pointer
Step 3: compute output of all DQ Rx DLLs
Channel
This BIRD
GetWave2 BIRD
This figure adapted from BIRD_GetWave2_draft.docx

## Slide 7: Advantages
No loss of functionality that is in GetWave2 BIRD
No new function signature AMI_GetWave2
Model will work in 7.0 flow on tools that do not support this BIRD
Does not require DQS simulations in order to evaluate DQ data path