## Slide 1
IBIS Conn
Sub-Committe Participants
Simulation Vendors
AMP
Ansoft
HyperLynx
ViewLogic
Connector Companies
AMP
Berg / FCI
Molex
Teradyne
End Users
EMC
Multi Faceted

## Slide 2
IBIS Conn
Why have an IBIS connector standard?
No standard presently exists which works without modification in all simulators.
Present methods do not address problems encountered in automatically attaching connector models to SI, EMC, and Timing simulators.
Present methods used in modeling IBIS IC’s do not allow cascade and/or tee methods of using coupled matrices.
Present methods do not allow model scaling and simplification provided by the SWATH mechanism.

## Slide 3
IBIS Conn
Status:
Concepts determined
Specification created
Example Models created
CDROM created with the following:
  Preliminary Specification
  Example Models
  This slide presentation
Pick one up from Kellee or Matt at the meeting today.
NOTE: The CDROM is not a released specification it is intended to facilitate comment towards ratification by the IBIS forum. The CDROM is being provided by HyperLynx and will be distributed to any simulation or connector vendor interested. They will also be provided to ended users on request until the 50 we made are gone.

## Slide 4
IBIS Conn
ReUsed Concepts and Syntax from IBIS V3.2
The following keywords are the same as those used in the IBIS IC and .pkg specification:
[File Rev]
[Comment Char]
[Date]
[Source]
[Notes]
[Disclaimer]
[Copyright]
[Manufacturer]
Sparse_matrix, Banded_matrix, Full_matrix

## Slide 5
IBIS Conn
Some of the New Features!
Stand alone specification to facilitate ease of use by connector companies or end users
Pictures (JPEG) to assist users with choosing connector models
Stub Matrices (tee matrices)
Cascaded Matrices (series matrices)
Swath Matrix (for variable size connectors)
Diagonal_matrix (same as width 0 banded)
Pin Naming methods for connectors
Extended file extension name to reduce the potential conflict with existing connector model naming. “.ibiscnn”
Relaxed line width restrictions under some circumstances

## Slide 6
IBIS Conn
New Features
Q: So why make it a stand alone specification?
A: The existing specification is getting VERY large and difficult for an entry person to comprehend. To solve this problem the connector specification restates the keywords in common to both documents and contains only syntax needed for the connector model.
Q: Why add a new diagonal_matrix keyword if it does the same thing as a width 0 banded matrix?
A: Width 0 matrix is very commonly used. This is the method used to describe “Single Line Uncoupled Models” in this specification. This format takes half as much text in the file so it is easier to create, understand and has a much smaller file size.

## Slide 7
IBIS Conn
What is a Matrix?...
Q: What do we mean when we talk about a Matrix?
A: Generally, in electromagnetics, a matrix is a table of numerical values that represent one of the parameters of a connector (transmission line). Specifically, the matrix represents the electrical relationships between all conductors of a given geometry. Further, the matrices used in this specification generally follow previous IBIS model examples.
As represented in the Connector specification:
[Begin_Section] NameA
[Inductance Matrix] Full_matrix
.
.
[Capacitance Matrix] Full_matrix
.
.
[Resistance Matrix] Full_matrix
.
.
[End_Section] NameA

## Slide 8
IBIS Conn
Swath Matrix (variable size)
Q: So what is a swath?
A: It is a method of using a small matrix to define a much larger and variable size connector. This facilitates faster simulations, smaller file sizes, and makes the
creation of a family of connectors much easier.
For example:
[Begin_Cn_Swath]
[Cn_Z] 50
[Cn_Horizontal_Swath] 2 2
[End_Cn_Swath]

## Slide 9
IBIS Conn
Cascade Matrices (series)
Q: What are a cascaded matrices?
A: Cascaded matrices are a series of matrix slices that walk down the connector from one side to the other. The matrixes are defined the same as in the IBIS .pkg specification and may be full, spares, banded, or diagonal.
For example:
[Begin_Cn_Model] Hdi20 Hdi20Pin Hdi20Phy MLM
Cn_Section NameA
Cn_Section NameB
[End_Cn_Model] Hdi20

## Slide 10
IBIS Conn
Stub Matrices (tee's)
Q: What is a stub matrix?
A: A matrix that is connected to the cascaded matrix sections
by a tee.
For example:
[Begin_Cn_Model] Hdi100 Hdi100Pin Hdi100Phy MLM
Cn_Section NameA
Cn_Section NameB
Cn_Stub StubNameB
Cn_Section NameC
[End_Cn_Model] Hdi100

## Slide 11
IBIS Conn
Put all the matrices together...
[Begin_Cn_Model] Hdi200 Hdi200Pin Hdi200Phy MLM [Cn_Number_of_Conductors] 40
[Cn_Columns_of_Pins] 20
[Cn_Rows_of_Pins] 2
[Begin_Cn_Swath]
[Cn_Z] 50
[Cn_Horizontal_Swath] 2 2
[End_Cn_Swath]
Cn_Section NameA
Cn_Section NameB
Cn_Stub StubNameB
Cn_Section NameC
[End_Cn_Model] Hdi200
[Begin_Section] NameA
[Inductance Matrix] Full_matrix
[Capacitance Matrix] Full_matrix
[Resistance Matrix] Full_matrix
[End_Section] NameA
.
.
.

## Slide 12
IBIS Conn
What's Next?
Short Term Goals:
  Transfer the specification to the IBIS archive
  Solicit feedback from the IBIS open forum
  Make changes per the feedback.
  Adopt the .ibiscnn specification into V3.3 of IBIS
Long Term Goals:
  Create a parser for syntax checking
  Accuracy confirmation of .ibiscnn model
    compare to SPICE model
    compare to IBIS Package model
  Add features to Swath method
  Add lossy modeling
  Consider adding support for .EBD capabilities.

## Slide 13
IBIS Conn
SPICE Model Types
Two types of SPICE connector models are in common use today:
Note: Coupling Removed for simplicity
Un-Balanced RLC
Side A
Side B
…
…
Side B
Side A
Balanced RLC

## Slide 14
IBIS Conn
SPICE Model Types
Comparisons should include at least:
  Reflection magnitudes
  Propagation Delay
  Crosstalk
  Risetime Degradation
To compare the IBIS connector models with SPICE the balanced type is recommended.
…
Side B
Side A

## Slide 15
IBIS Conn
Special Thanks:
Special thanks to Gus Panella of Molex Inc. for providing so many hours of his time to this project.
Special thanks to the following companies
  EMC (for providing the phone bridge)
  HyperLynx (for providing MAJOR specification enhancements and CD-ROMs)
Kellee Crisafulli, 1-28-99
The following people participated in the IBIS connector sub-group:
Eric Bogatin, Bogatin Enterprises (formerly at Ansoft) Jeff Walden, (formerly at AMP),
Steve P. Chau, AMP, Fabrizio Zanella, EMC,
Kellee Crisafulli, HyperLynx, Gus Panella, Molex Inc.
Mark Gailus, Teradyne , Michael Khusid, Teradyne,
John Ellis, FCI/Berg, Guy de Burgh, Viewlogic Systems