## Slide 1
Integrated Circuits modeling
ICEM
Integrated Circuits Electromagnetic Model
PROPOSAL : IEC 62014 - 3

## Slide 2
PLAN
ICs AND EMC SIMULATION NEEDS
UTE EMC TASK FORCE
ICEM MODELS
- Power lines contribution
- I/Os contribution
ICEM IMPLEMENTATION IN IBIS DATABASE
CONCLUSION

## Slide 3
ICs AND EMC
SIMULATION NEEDS

## Slide 4
INTEGRATED CIRCUITS MANUFACTURERS.
  New ICs design have to take into account EMC/EMI
  To include EMC in development phenomena need to be simulated.
PRINTED CARD BOARD DESIGN
COMPLY EMC DIRECTIVES AND STANDARDS.
  Predict and improve EMC performances requires to be able to simulate phenomena
SIMULATION TOOLS or behavioural model (like IBIS ) available on the market for PCB simulation do not take into account EMC phenomena, mainly signal integrity.
ICs AND EMC SIMULATION NEEDS

## Slide 5
UTE EMC TASK FORCE

## Slide 6
Leader PERRIN Jean Claude TEXAS INSTRUMENTS
Members HUET Claude EADS AIRBUS
LEVANT Jean Luc ATMEL
MAROT Christian SIEMENS AUTOMOTIVE
MAURICE Olivier VALEO
PERRAUD Richard EADS CCR
SAINTOT Pierre ST MICRO ELECTRONIQUE
SOUBEYRAN Amaury EADS MSI
University SICARD Etienne INSA
RAMDANI Mohamed ESEO
LUBINEAU Marc IERSET
UTE TEAM

## Slide 7
PROGRAM STATUS
1994 : WORKING GROUP UTE/CEF 93GT5 EMC
06 / 1997 : IEC 93 / 67 NP
1998 : DATE 98 / INTERNATIONAL TASK FORCE
2000 : DATE 2000 / IEC INTERNATIONAL EXPERTS MEETING
03 / 2001 : IEC 62014 - 3
CDV proposal sent to IEC
for standard approval
03 / 2001 : DATE 2001 MUNICH IBIS SUMMIT MEETING

## Slide 8
ICEM MODEL
Integrated Circuits Electromagnetic Model

## Slide 9
ELECTROMAGNETIC AND HF NOISE SOURCES
Power supply lines emission :
Switching activity in different modules (Internal/peripheral)
High frequency current through package connections
I/O connections noise emission :
Noise due to output fast signals and package characteristics
Noise coupling through package to the other I/O pins
Noise coupling through package to other powers supplies
IC Direct emission :
Package Bonding and metal die connections

## Slide 10
ICEM model
Mechanisms for parasitic emission covered by ICEM model

## Slide 11
Power lines contribution

## Slide 12
I/Os contribution, single supply structure

## Slide 13
I/Os contribution, multiple supply structure

## Slide 14
ICEM IMPLEMENTATION
IN IBIS DATABASE

## Slide 15
PACKAGE MODELING
Keyword [ define package model]
Keyword [manufacturer]
Keyword [second order]
Keyword [description]
Keyword [number of pins]
Keyword [pin numbers]

## Slide 16
PACKAGE L, R, C DESCRIPTION
Keyword [pin numbers]
Keyword [All]
Keyword [bonding]
Keyword [package pin]

## Slide 17
Example of Package description from manufacturers
[Package]
| Variable Typ Min Max
R_pkg 0.1034 0.048 0.2592
L_pkg 2.263e-09 1.098e-09 4.827e-09
C_pkg 2.045e-13 8.363e-14 3.75e-13
|
[Pin] signal_name R_pin L_pin C_pin
1 PIN_1 NC 0.07963 1.849e-09 1.187e-13
2 PIN_2 NC 0.08791 2.116e-09 1.73e-13
3 PIN_3 NC 0.1445 3.071e-09 2.239e-13
4 PIN_4 NC 0.08285 1.841e-09 1.315e-13

## Slide 18
Example of Package description from manufacturers
* CONDUCTOR LAYER NAME TYPE HEIGHT(MM) THICKNESS(MM) *
********************************************************************
* 11 LF 0.46000 0.01000
* 10 BW 0.47000 0.02540
********************************************************************
* MISC
Electrical Data By Pin (at DC):
Pin R (ohms) L (nH) C (pF)
Whole BW Whole BW Whole BW
1. 0.080 0.072 1.849 1.643 0.119 0.105
2. 0.088 0.065 2.116 1.489 0.173 0.108
3. 0.144 0.063 3.071 1.432 0.224 0.107
4. 0.083 0.061 1.841 1.390 0.132 0.106
5. 0.060 0.060 1.372 1.372 0.105 0.105

## Slide 19
CURRENT GENERATOR DESCRIPTION
[Ib generator]
[Cb capacitor]
| Variable Typ Min Max
C_pkg 2.045e-13 8.363e-14 3.75e-13
[Vdd Vss Pin]
[Ib current]
Variable
Ib (mA) 1 10 50 100 80 60 40 20
t (nS) .5 1 1.5 2 2.5 3 3.5 4
[Frequency]
| Variable Typ Min Max
F(MHz) 13 6 50

## Slide 20
INTER COUPLING POWER SUPLIES Zsub
[Zsub ]
[Csub capacitor]
| Variable Typ Min Max
C_pkg 2.045e-13 8.363e-14 3.75e-13
[vss1 vss2 pins]
[z impedance]
Variable s
dI(mA) .01 1 2 5 10 50 100
dv (nS) .1 .2 .3 .4 .5 .6 .7
[Frequency]
| Variable Typ Min Max
F(MHz) 13 6 50

## Slide 21
DIRECT IC ELECTROMAGNETIC EMISSION
Emission Mainly due to package
Variables
Pin length
Frequency
RLC ( Resonances )

## Slide 22
CONCLUSION

## Slide 23
CONCLUSION
ICEM Gives a capability to simulate EMC due to internal activity and of I/Os noise coupling
ICEM model easy to add as modification od add on files to standards like IBIS .
ICEM model parameter can be obtained if data are not available from ICs manufacturers.

## Slide 24
CONCLUSION
ACTIONS PLAN TO PERFORM
COOK BOOK to be writen to explain how to obtain
ICEM Model parameters. (First draft is on going)
Evaluation through IBIS forum
Integration in standard models database ( For ex IBIS)
PCB simulation tools integration to provide EMC
simulation capability.
Softwares Validation