## Slide 1: IBIS Futures Subcommittee
Intel: Arpad Muranyi, Stephen Peters
InnovEDA: Al Davis, John Angulo
Mentor Graphics: Bob Ross
Cadence: Mike LaBonte
IBM: Mike Cohen
Texas Instruments: Stephen Nolan

## Slide 2: General Themes
Format consistency
Nodal circuit descriptions
Basic circuit elements, plus tables, equations, triggers, advanced t-lines
Separation of circuit topology and data
Dataset correlation beyond min/typ/max
Existing IBIS files still work

## Slide 3: Top Level Format
Light discussion only, so far. Nothing in writing.
Borrow from Connector Specification
  Same header section
  [Model]
  [End Model]
Borrow from XML
  [Model name=“gt5623yf” type=“I/O”]
Backward compatibility: parser mode or translator?

## Slide 4: Separation of Circuit Topology and Data
[Model] switchout
Model_type Terminator
Enable Active-Low
| variable typ min max
C_comp 0pF NA NA
[Temperature Range] 25 100 0
[Voltage Range] 5.0 4.75 5.25
[Rac] 1k NA NA
[Cac] 0.5 NA NA
[Define Model] Terminator
.inherit model_base
.node t1
resistor Rac (pin t1) R = [Rac] || short
capacitor Cac (t1 gnd) C = [Cac] || open
resistor Rpwr (pin power_clamp_ref) R = [Rpower] || open
resistor Rgnd (pin gnd_clamp_ref) R = [Rgnd] || open
[End Define Model]
Data
Circuit Topology

## Slide 5: Nodal Interconnect
Interconnect that lies outside of buffers, but how far out?
  Die to package only?
  Including package parasitics?
  Same scope as EBD?
Little discussion so far
May or may not use macro language format
Frequency-dependent RLGC transmission lines are possible

## Slide 6: Macro Language
Language used inside [Define Model] sections
Most discussed topic
Debate over how much new simulator development should be required
  Dependent sources controlled by any circuit nodes
  Full equations vs. simple arithmetic
  General purpose charge and flux elements (SPICE B element)