## Slide 1
A Tour of the IBIS Quality Specification
DesignCon East IBIS Summit April 5, 2004
Robert Haller
rhaller@sisoft.com
Signal Integrity Software, Inc.
6 Clock Tower Place – Suite 250
Maynard MA. 01754
978-461-0449 X 15

## Slide 2: IQ Specification and Example
http://www.sisoft.com/ibis-quality/docs
IQ_Specification.txt
IQ_Example.ibs
Notes: Why are we here today

## Slide 3: IBIS Quality Specification Levels
Level 0 requirements
  Level 0 requirements can be checked by ibischk3 version 3.2.9 or later software
  Ibischk3 is highly recommended, to avoid performing level 0 checks manually
Level 1 requirements
  Level 1 includes all items in level 0
  Plus checks for correctness and completeness, and basic simulation tests
Level 2 requirements
  Level 2 includes all items in levels 1 & 0, plus correlation:
  Spice Correlation
  Bench Correlation
  IBIS Accuracy Handbook figure of merit (FOM)
Notes: Why are we here today

## Slide 4: IQ Specification Index
1.0 IBIS Quality Summary
1.1 IBIS Quality level definitions
1.2 IBIS Quality summary as comments in file
2.0 General Header Section Requirements
3.0 Component Section
3.1 Component Package Requirements
3.2 Component Pin Requirements
3.3 Component Diff Pin Requirements
3.4 Component Model Selector Requirements
4.0 Model Section
4.1 Model General Requirements
4.2 Model Waveform Processing Requirements
4.3 Model I-V Table Requirements
4.4 Model V-T Table Requirements
4.5 Model Ramp Data Requirements
5.0 Possible Errors that should be checked
6.0 Correlation
6.1 SPICE correlation
6.2 Lab correlation
7.0 Model Limitations
Notes: Why are we here today

## Slide 5: IQ Document Example
  [File Name] iq_example.ibs
  [File Rev] 1.0
  [Date] 3/30/2004
  [Source] Developed by: Signal Integrity Software, Inc.
  [Notes]
  Revision History
  Rev 1.0
  - 03/30/04 Release as iq_example. RJH
  |###############################################################
  |IQ IBIS Quality Notes
  |IQ SUMMARY Overall Quality of component and models Level 2
  |
  |IQ Level 0 - 0 errors 12 warnings
  |IQ Level 1 - All checks done for completeness and correctness
  |IQ Level 2 - HSPICE Coorelation (2003.09) completed FOM =99%
  |
  |IQ Buffer SSTLDATIO: Quality level 2
  |IQ Buffer SSTLADDIO: Quality level 2
  |
  |IQ Level 0
  | All I/O Models: When running through ibischk3, this file
  | contains 12 warnings about pullup and pulldown being non-monotonic.
  | This is due to an IBIS Parser Bug, BUG71. Example warnings;
  | WARNING (line 209) - Pulldown Maximum data is non-monotonic
  | WARNING (line 210) - Pulldown Typical data is non-monotonic
  | IBISHCK 4.0 produces 0 errors and 0 warnings
  |IQ Level 1
  |(insert grep)
  |IQ Level 2
  |(insert trailer)
Notes: Why are we here today

## Slide 6: IQ Checklist Example

## Slide 7: Summary
IBIS Quality Specification
  http://www.sisoft.com/ibis-quality/docs
IQ Levels
IQ Index
IQ Example

## Slide 8: Additional Resources
Mailing list
  Ibis-quality@freelists.org
  http://www.freelists.org/archives/ibis-quality
Web site
  http://www.sisoft.com/ibis-quality
Come visit IBIS booth
Come to our SI and Timing paper
  Wed 2pm (6-WP1)
Come to PASS/FAIL Panel
  Wed 4 pm
Thank you
Questions