## Slide 1: IBIS Quality Review
A status review of the IBIS Quality specification
Mike LaBonte, Cisco Systems

## Slide 2: IBIS Quality Task Group
Web:
  http://www.vhdl.org/pub/ibis/quality_wip
Email list:
  http://www.freelists.org/list/ibis-quality
  Or send email
  To: ibis-quality-request@freelists.org
  Subject: subscribe
Meetings:
  Tuesdays from 11:00am to 12:00pm Eastern Time
Questions? Mike LaBonte milabont@cisco.com

## Slide 3: Brief History
2002 March - Barry Katz started IBIS-Quality
2004 November - IQ 1.0 specification completed
2005 August - Parser bug 90 submitted and approved
2006 March - Parser bug 94 submitted and approved
2006 April - Book “Semiconductor Modeling” discusses IQ
2006 August - IQ 1.1 specification initiated
2009 August – IQ 1.1 specification release expected

## Slide 4
[Package]
[Pin] RLC
[Diff Pin]
[Model Selector]
IQ0
IQ3
IQ2
IQ1
IQ4
M
S
X
[Receiver Thresholds]
C_comp
Rat hole
IQ
[Model Spec]
[Temperature Range]
[Voltage Range]
[Pulldown]
[Pullup]
Symbol swamp
[GND
Clamp]

## Slide 5: Specification Version 1.0
IBIS Quality Levels
  0 – Can be checked by IBISCHK, plus a few others
  1 – Correctness, completeness, and simulation checks
  2a – Simulation correlated
  2b – Bench measurement correlated
  3 – Simulation and measurement correlated

## Slide 6: Issues with IQ Version 1.0
Passing IQ Level 0 does not sound like much of an accomplishment
  Is a non-compliant file level -1?
There should be a strict level for “Passes IBISCHK”
No other IQ check should duplicate IBISCHK
Can’t have a correlated model without full IQ check
Some checks are weak (“should” vs. “must”)
Feedback from JEITA

## Slide 7: Specification Version 1.1
IBIS Quality Levels
  IQ0 – Not Checked
  IQ1 – Passes IBISCHK
  IQ2 – Suitable for Waveform Simulation
  IQ3 – Suitable for Timing Analysis
  IQ4 – Suitable for Power Analysis * (defined, but no checks)
Special Designators
  S – Simulation correlated
  M – Measurement correlated
  X – Exceptions
  G – Has Golden Waveforms
IQ0
IQ3
IQ2
IQ1
IQ4
M
S
X

## Slide 8: The Only LEVEL 1 Check (IBISCHK)
2.1 {LEVEL 1} IBIS file passes IBISCHK
IBIS models are expected to pass the checks performed by the IBISCHK program before they are released to the public. Passing IBISCHK insures that the file will attain at least an IQ1 level designation. The IBISCHK program is found at http://www.eigroup.org/ibis/tools.htm.
A best practice is to insert the full output from the IBISCHK program into the IBIS file as comments, with explanation for any warnings annotated within. When doing this it is important to insure that the added comments do not cause new “line too long” IBISCHK warnings.
In general it is best to use the latest available version of the IBISCHK program, as the latest version may include new tests and fixes for bugs found in the older versions. The IBISCHK program used must, at a minimum, be able to accommodate the [IBIS Ver] of the IBIS file at hand. The [IBIS Ver] used in the IBIS file is set by the model maker based on the set of IBIS keywords required to completely and correctly represent the behavior of the part. The [IBIS Ver] value can be set to at least 3.2 because this version is supported by a wide variety of EDA tools.
…

## Slide 9: Example LEVEL 2 Checks (Waveforms)
5.2.5 {LEVEL 2} [Model Spec] S_Overshoot subparameters complete and match data sheet
All input and I/O buffers have S_overshoot_high and S_overshoot_low in the [Model Spec] section. The values must match the voltage limits beyond which the device may not function correctly. These limits may be different from the absolute maximum ratings, which may be related to device destruction. The functional limits may not be found in some data sheets.
5.2.6 {LEVEL 2} [Model Spec] S_Overshoot subparameters track typ/min/max
When overshoot voltage limits are different in min and max corners, S_overshoot_high and S_overshoot_low should track these differences. For example, S_overshoot_high may increase with the higher supply voltage assumed for max mode.

## Slide 10: Example LEVEL 3 Checks (Timing)
3.2.2. {LEVEL 3} [Pin] RLC parasitics are present and reasonable
For a LEVEL 2 model, pin parasitics are optional, but they are mandatory for a LEVEL 3 model (that is, a model suitable for timing). To pass this check the RLC values must be present for all signal pins in the [Pin] section, or [Package Model] must be present. Pin parasitics should either be measured or extracted using a 2D or 3D solver. Reasonable signal pin parasitics will result in impedance and delay characteristics that fall in the ranges:
  TD = SQRT(LC) < 300ps
  Z0 = SQRT(L/C) < 100ohm
Note that IQ check 3.1.2. also requires that each [Pin] RLC value falls within the min/max range as given by the [Package] keyword. The [Package] keyword can be adjusted to accommodate.
3.3.1. {LEVEL 3} [Diff Pin] Vdiff and Tdelay_* complete and reasonable
For input and I/O pins Vdiff must be defined, non-zero and positive. For output and I/O pins Tdelay_typ, Tdelay_min, and Tdelay_max data can be zero, but must be defined. Both Vdiff and Tdelay_* are measured relative to the die pads and must not include additional package delays and offsets. Output pins should have NA for Vdiff. For input pins Tdelay_typ, Tdelay_min, and Tdelay_max must be NA.

## Slide 11: No Level 4 Checks (Power)
A [Pin Mapping] Complete and Correct check was proposed
Power analysis really needs new features:
  BIRD95 - Power Integrity Analysis using IBIS
  BIRD98 - Gate Modulation Effect (table format)
IBIS 5 adoption still in progress
  Not yet an EIA/ANSI standard
  IBISCHK 5 parser in development now
  Have not yet seen IBIS 5 power keywords in IBIS files
IQ 1.2 will have level 4 checks

## Slide 12: Notes on IQ Version 1.1
“Possible Errors” section removed
  Some items made into regular checks
“Correlation” section minimized
  Refers to IBIS Accuracy Handbook for details
IC vendor push-back on overshoot parameters
  Not many IBIS files have this
  Buffer developers simply do not measure it
  Difference between functional and destruction limits
  BIRD103 D_overshoot parameters may work better

## Slide 13: IQ Version 1.1 Status
44 draft revisions posted
In editorial review phase
  Going through feedback from Anders Ekholm
  Need to have consistent spelling of terms, etc
Probably will take 5 or 6 more meetings

## Slide 14: After Version 1.1
File parser bug reports
Update the IBIS Accuracy Handbook
  Emphasis on feature-selective correlation
Begin drafting IQ 1.2
  Level 4 power analysis checks

## Slide 15: Regular 2009 IQ Meeting Participants
Cisco Systems
Ericsson
Huawei Technologies
Micron Technology *
Nokia Siemens Networks
Texas Instruments *
Teraspeed Consulting Group *
Xilinx *
* IBIS model makers

## Slide 16: Not participating: JEDEC
IC makers increasingly defer to JEDEC specs
  IBIS gets lower priority
  Lack of certain keywords is a barrier to IQ compliance
JEDEC specifies parameters beyond IBIS
Why so few IBIS files with [Receiver Thresholds]?
  Developed for JEDEC DDR conformance
  DDR2 “area” specs go beyond [Receiver Thresholds]
  BIRD103 addresses this in IBIS 5
JEDEC could produce IBIS files to facilitate adoption