## Slide 1: SpiTran: A GUI for S2IBIS2 Mike LaBonte IBIS Summit 21 June 1999

## Slide 2: SpiTran: A GUI for S2IBIS2
Written as a Java application - platform portable
Audits SPICE files
Prepares top level test circuit
Prepares S2IBIS control file
Runs NCSU s2ibis2

## Slide 3: SpiTran Main Window
Click the “New Document” icon.

## Slide 4: Creating a New Project Directory
Enter the name of a new directory and click “Create”.
Notes: Use directory name “iobuff”.
You can hit return to create the directory.

## Slide 5: Import a SPICE File To the Project
The selected SPICE file is copied into the project directory. Required process library files may be added here. Click “OK”.
Notes: Set Technology “CMOS”
Either type “iobuff.sp” for the SPICE file name or browse for it.
This file is in the ModeDemo\spitran folder.
The fields on the lower half of the form are for adding process
library files associated with the buffer. This testcase has none.
After clicking “OK” there will be a confirmer saying typical values will be
used for min and max.

## Slide 6: SPICE File Audit
The SPICE file is audited for elements that look like a built-in test fixture. Click “Edit Spice” to remove them, and then “Reparse”.
Notes: The demo will actually have only one warning. It can be ignored because
it is a voltage source inside an unused test fixture subckt. If you wish,
click “Edit” and show the SPICE subckts. But don’t click “Reparse”.
Skip 2 slides.

## Slide 7: Contents of iobuff.sp
...
.SUBCKT IO_IN OUT IN VDD VSSD1 IN VDD DD2 VSS IN DR1 IN 1 10
M1 OUT 1 VDD VDD pm L = 5U W = 120.00U
M2 OUT 1 VSS VSS nm L = 5U W = 50.00U .ENDS IO_IN
.SUBCKT IO_TEST_LOAD LOAD
R1 LOAD 1 50
V1 1 0 1.8
C1 LOAD 0 10p
.ENDS
XOUT 1 2 3 4 5 IO_OUT
XIN 6 1 4 5 IO_IN
XLOAD 1 IO_TEST_LOAD
VDD 4 0 5
VSS 5 0 0
VDATA 2 0 PULSE(0 5 0 10n 10n 50n)
VENA 3 0 5
RDUM 6 0 1e6
*simulator lang = spectre
model pm mos0 type=p
model nm mos0 type=n
model d diode
simulator lang = spice
The main circuit is a test fixture and must be commented out.
Notes: The demo “iobuff.sp” desn’t have the main circuit stuff in red.

## Slide 8: Passes Audit without Warnings
The fixed-up file now passes the audit cleanly. Click “Continue”.
Notes: There will be one warning. Ignore it.

## Slide 9: Main Window Shows Available Subckts
Three subckt definitions are found in the SPICE file. Select “IO_OUT” and “IO_IN”, and click “Instantiate”.
Notes: Select the first 2 rows and “Instantiate”.

## Slide 10: Instantiated Subckts
The instantiated subckts appear in the lower section. Change the node names to establish the test circuit netlist.
Notes: Set the node name by triple clicking before you type. The names are:
pad input ena vdd vss
rcvrout pad vdd vss
After entering the last name, be sure to click on some other cell, to
have the last entry taken.

## Slide 11: Node names set
Click “Configure Nets”.

## Slide 12: Telling S2IBIS How Each Node is Used
Establish how each external node is to be used by s2ibis. The pin type of each node is set.
Notes: You have to click in a cell, then click again to get the menu.

## Slide 13: Nodes Configured
The “rcvrout” node is unused by s2ibis, so it must be “floated” with a terminating resistor. Click “OK”.

## Slide 14: Prepare the S2IBIS Control File
Choose the “Options” item from the “Translate” menu.

## Slide 15: Node Options
Set the nodes to be used for power, ground, enable, etc.
Notes: Click on Nodes to get this screen.
At this point you can enter file name “iobuff.s2i” and click Import, so that
all settings will be made.

## Slide 16: Mode Options
Choose the simulator to be used, and other s2ibis options.

## Slide 17: Voltage Options
Set voltages.
Notes: Double click “Operating Range” to expose the “Voltages” item. If you set
the Operating Range fields you don’t have to set the others.

## Slide 18: Temperature Options
Set temperatures.
Notes: Watch out, the best temperature is HIGHER than the worst.

## Slide 19: Stimulus Options
Set simulation duration and input stimulus times and voltages.
Notes: Riase and Fall times of “0.2n” should work.

## Slide 20: Model Options
Set logic thresholds and C_COMP.
Notes: NOT SHOWN: also check the “Active-High” box.

## Slide 21: Buffer Delay Options
Set Vmeas and test fixture values.
Notes: Double-click “Fixture” to expose this item.

## Slide 22: VT Options
Set test fixture values for 1st waveform set.
Notes: L and C values in fixtures are not recommended.
The DUT fields are going away.

## Slide 23: VT Options for 2nd Waveform Set
Set test fixture values for 2nd waveform set.

## Slide 24: Ramp Load Options
Set load resistance for ramp time simulation.
Notes: Used in spearate simulations to determine Ramp rates.

## Slide 25: Post-Processing Options
Set derating values for optional curve post-processing.
Notes: Don’t fill these in. These are s2ibis features.

## Slide 26: Running S2IBIS
Choose the “Execute” item from the “Translate” menu.
Notes: If a bunch of windows flash open while simulations are running, you do
not have JDK 1.2 installed. There is one window for each spectre run,
and then 2 more for Spitran post-processing to cleanup the data.

## Slide 27: S2IBIS Messages
Notes: If ANYTHING has been missed, there will be an error message at
the end. But an IBIS file may still have been produced.

## Slide 28: IBIS Model File in Project Directory
Notes: Open ModelDemo\spitran\iobuff\iobuff.ibs
If there were errors it may have some wrong numbers, though.