## Slide 1: A Tour of the IBIS Quality Specification DesignCon East IBIS Summit April 5, 2004
Robert Haller
rhaller@sisoft.com
Signal Integrity Software, Inc.
6 Clock Tower Place – Suite 250
Maynard MA. 01754
978-461-0449 X 15
Notes: Good Afternoon (morning )
Thank you for coming
I am Bob Haller Principal Consultant for SiSoft
SiSoft is a SI EDA Software and Si consulting services company
Today will present a tour of the ibis quality specification
Recently renamed from IBIS Quality Document

## Slide 2: IQ Specification and Example
http://www.sisoft.com/ibis-quality/docs
IQ_Specification.txt
IQ_Example.ibs
IQ_Checklist.xls
Notes: So in this presentation I will present the IBIS Quality Specification
An IBIS Quality Example IBIS file
And an IBIS Quality Checklist (which will be contained within the IBIS file).

## Slide 3: IBIS Quality Specification Levels
Level 0 requirements
  Most Level 0 requirements can be checked by ibischk3 version 3.2.9 or later software.
  Ibischk3 is highly recommended, to avoid performing level 0 checks manually
Level 1 requirements
  Level 1 includes all items in level 0
  Plus checks for correctness and completeness, and basic simulation tests
Level 2 requirements
  Level 2 includes all items in levels 1 & 0, plus correlation:
  Spice Correlation and/or Bench Correlation
  IBIS Accuracy Handbook
    Correlation Levels (1,2,3)
    Figure of Merit (FOM)
Notes: The IBIS quality created specific quality levels to distinguish different levels of quality

## Slide 4: IQ Specification Index
1.0 IBIS Quality Summary
1.1 IBIS Quality level definitions
1.2 IBIS Quality summary as comments in file
2.0 General Header Section Requirements
3.0 Component Section
3.1 Component Package Requirements
3.2 Component Pin Requirements
3.3 Component Diff Pin Requirements
3.4 Component Model Selector Requirements
4.0 Model Section
4.1 Model General Requirements
4.2 Model Waveform Processing Requirements
4.3 Model I-V Table Requirements
4.4 Model V-T Table Requirements
4.5 Model Ramp Data Requirements
5.0 Possible Errors that should be checked
6.0 Correlation
7.0 Model Limitations and model maker notes
Notes: Walk through section
Consistent with IBIS specification
Correlation section recently updated

## Slide 5: IQ IBIS File Example
  [File Name] iq_example.ibs
  [File Rev] 1.0
  [Date] 3/30/2004
  [Source] Developed by: Signal Integrity Software, Inc.
  [Notes] Rev 1.0 - 03/30/04 Release as iq_example. RJH
  |IQ SUMMARY Overall Quality of component and models Level 2
  |IQ Level 0 - 0 errors 12 warnings
  |IQ Level 1 - All checks done for completeness and correctness
  |IQ Level 2 - HSPICE Correlation (2003.09) completed FOM =99%
  |IQ Buffer SSTLDATIO/SSTLADDIO: Quality level 2
  |IQ Level 0
  | All I/O Models: When running through ibischk3, this file
  | contains 12 warnings about pullup and pulldown being non-monotonic.
  | This is due to an IBIS Parser Bug, BUG71.
  | IQ WARNING (line 209) - Pulldown Maximum data is non-monotonic
  | IQ WARNING (line 210) - Pulldown Typical data is non-monotonic
  | IBISHCK 4.0 produces 0 errors and 0 warnings
  |IQ Level 1
  | All Level 1 checks performed and are either OK or NA
  | Limitations: Ccomp is a compromise between driving and receiving.
  |IQ Level 2
  | Using VT IBIS Data compared to source HSPICE models FOM = 99%.
|IQ BEGIN IBIS Quality Checklist
|
|IQ FILE: iq_example.ibs IQ Level: 2
|IQ XX 2.1 LEVEL 0 Header passes IBISCHK
|IQ XX 2.2 LEVEL 0 Latest [IBIS ver] used
|IQ XX 2.3 LEVEL 0 Do not use [Comment Char]
|IQ XX 2.4 LEVEL 0 [File Name] is correct
|
|IQ COMPONENT: IQ_EXAMPLE IQ Level: 2
|IQ XX 3.1.1 LEVEL 0 [Package] must have typical values
|IQ XX 3.1.2 LEVEL 0 [Package] Parasitics must be reasonable
|IQ XX 3.1.3 LEVEL 0 [Define Package Model] present if
|IQ XX 3.1.4 LEVEL 1 [Package] parasitics are validated datasheet
|IQ XX 3.2.1 LEVEL 0 [Pin] section complete
|IQ XX 3.2.2 LEVEL 0 [Pin] model names not too long
|IQ XX 3.2.3 LEVEL 0 [Pin] models present in file
|IQ XX 3.2.4 OPTIONAL [Pin] RLC complete
|IQ XX 3.2.5 LEVEL 1 [Pin] RLC parasitics are validated datasheet
|IQ NA 3.3.1 LEVEL 0 [Diff Pin] referenced pins exist
|IQ NA 3.3.2 LEVEL 0 [Diff Pin] Vdiff and Tskew complete
|
|IQ MODEL: SSTLADDIO IQ Level: 2
|IQ XX 4.1.1 LEVEL 0 [Model] parameters have correct typ/min/max
|IQ XX 4.1.2 LEVEL 0 [Model] Model_type
|IQ XX 4.1.3 LEVEL 0 [Model] C_comp is reasonable
|IQ XX 4.1.4 LEVEL 1 [Model] C_comp is correct
|IQ XX 4.1.5 LEVEL 2a [Model] C_comp SPICE correlation
|IQ __ 4.1.6 LEVEL 2b [Model] C_comp laboratory correlation
Notes: SAMPLE ibis file used to implement IQ specification
And checklist
Checklist is contained within the IBIS file

## Slide 6: IQ Checklist Example
Notes: Thanks to Mikes Help I have an updated check-off list.
This Should be included in the NOTES section of the ibis file
Preceded with |IQ comment character.
Previous example clearly implements this

## Slide 7: Summary
IBIS Quality Specification
  IQ Levels
  IQ Index
IQ IBIS File Example
IQ Checklist Example
Notes: In Summary
We have written a spec
that contains levels and appropriate documentation
Generated an example ibis file and checklist
Demonstrating the practicality of performing this work.
Now we would like some Semiconductor Vendors
Or model Makers in general to try and implement it.
Feedback is encouraged …

## Slide 8: Additional Resources
Mailing list
  Ibis-quality@freelists.org
  http://www.freelists.org/archives/ibis-quality
Web site
  http://www.sisoft.com/ibis-quality
  http://www.sisoft.com/ibis-quality/docs
Come visit IBIS booth
Come to our SI and Timing paper
  Wed 2pm (6-WP1)
Come to PASS/FAIL Panel
  Wed 4 pm
Thank you and thanks to IQ committee
Questions ?
Notes: There is additional information available…
Read slide