## Slide 1: Issues with C_comp and Differential Multi-stage IBIS Models
Michael Mirmak
Intel Corporation
IBIS Summit
DesignCon East 2004
April 5, 2004

## Slide 2: Agenda
Background
  Typical serial/diff. interface buffer design
  How Pre-emphasis is addressed in IBIS
Initial Approach to C_comp
  How tools use C_comp
  Proportional splitting
  Over-estimation of buffer loading
New Approach
  “Backing Out” C_comp
  Adding external capacitance
  Combined V-t correlation
  Multi-variate c_comp
Guidelines and Future Work
Note: many slides in this presentation are animated

## Slide 3: Typical Ser/Diff TX Design
Single stage buffer
  Example shown in S-ATA Gen. I specification
  http://www.serialata.org
A
B
TX+
TX-
Main
Data Stream In
Output
(into 100 Ω load)
Single-ended
Differential
I=13mA
R=50 Ω

## Slide 4: Adding Pre-emphasis
  Another source with different stimulus
    Second source usually a fraction of the first
A
B
C
D
TX+
TX-
Main
Boost

## Slide 5: Adding Pre-emphasis
  Another source with different stimulus
A
B
C
D
TX+
TX-
P
Pre-Emphasis
A = P C = P
B = P D = P
Main
Boost
Data Stream In
Main &
Boost
in concert
Main
+
Boost
Load between TX+ & TX-
sees Main + Boost

## Slide 6: Adding Pre-emphasis
  Another source with different stimulus
A
B
C
D
TX+
TX-
P
De-Emphasis
A = P C = P
B = P D = P
Main
Boost
Data Stream In
Main &
Boost
opposing
Main
Boost
Load between TX+ & TX-
sees Main - Boost

## Slide 7: Pre-emphasis Output
Typical implementation
  1 Bit = Crossover to Crossover
  Each bit after a crossover is emphasized
  Compensates for ISI and other loss effects
Output for
Data Pattern:
1 0 1 0 1 0 1 0
Output for
Data Pattern:
1 0 0 1 1 0 0 1

## Slide 8: IBIS Implementation
Wired-OR
configuration
Main (+ & -)
Boost (+ & -)
Input
stimulus
pattern
Emphasis
stimulus
pattern
  In IBIS, two differential pairs are combined
    One differential pair represents the main
    One differential pair represents the boost
  Each pair has a distinct stimulus pattern
    Main pair driven by the desired output pattern
    Emphasis pair driven by different data pattern
TX+ Pad
TX- Pad
X
X
Y
Y

## Slide 9: IBIS Implementation
Emphasis (t) = Input (t-1)
Main (+ & -)
Boost (+ & -)
Input
stimulus
pattern
Emphasis
stimulus
pattern
TX+ Pad
TX- Pad
  What is the emphasis pair’s stimulus pattern?
    If only transition bits are emphasized…
    Emphasis bit = inverse of input bit, delayed by 1 bit time
    Logical proof has 20+ steps
    Fairly simple to demonstrate empirically
1000 1000
0111 0111
1000 1000
0111 0111
(emphasized)
X011 1011
X100 0100
in concert
in opposition

## Slide 10: IBIS Grouping
A
B
C
D
TX+
TX-
Pre-Emphasis
A = P C = P
B = P D = P
De-Emphasis
A = P C = P
B = P D = P
Main
Boost
Pullup – Main (+ & -)
Pullup – Boost (+ & -)
Ground Clamps
Main + & -

## Slide 11: IBIS Data Extraction
As pre-emphasis uses two buffers…
  I-V curves are individual to each buffer
    Main I-V & Boost I-V are separately generated
    Internal terminations should NOT be double-counted!
  V-t curves are individual to each buffer
    Main V-t & Boost V-t are separately generated
    Internal terminations should NOT be double-counted!
Good designs will have test modes for disabling the sources and the terminations
What about c_comp?
  C_comp is collected only once, for entire buffer
  “Turning off” sections will not remove loading effects
  Most designs cannot be easily “split” into main and boost for purposes of c_comp measurement

## Slide 12: Two Approaches to C_comp
Method 1: split c_comp proportionally to Main and Boost relative drive strengths
  Example: “Buffer X” has total die capacitance of 8 pF
    See below for calculation
  Main is 18 mA
  Boost is 3 mA (6:1 ratio)
  Main c_comp: 6.857 pF
  Boost c_comp: 1.1424 pF
Main (+ & -)
Boost (+ & -)
TX+ Pad
TX- Pad
X
X
Y
Y
1.1424 pF
6.857 pF

## Slide 13: How was C_comp generated?
Initial method used to get 8 pF value
  Use Vsource with known edge rate, dV/dt
  Measure the input current
  Calculate capacitance (may have to take an average)
Driver
I
Vsource
dV/dt

## Slide 14: Results of Method 1 on Buffer X

## Slide 15: The Problem
IBIS is 27% slower than the transistor model!
  Same Main V-t curve as transistor model
  Same Boost V-t curve as transistor model
  I-V curves match to within 1%
  Die capacitance (C_comp) is only area of change...
Question: How is C_comp treated by EDA tools?
  IBIS V-t curves include C_comp effects
  C_comp also affects incoming (and reflected) waves
  Tools therefore remove C_comp effects from V-t curves
    Cap with C_comp value is placed external to buffer
    “Cap-less” V-t curves are used for driving simulations
    Output waveform at pad should be equivalent to IBIS
V-t
(including
c_comp)
V-t’
(without
c_comp)
TOOL

## Slide 16: The Problem with Method 1
For Pre-Emphasis, tool approach breaks down…
Assuming…
  C_comp (transistor) = C_comp’ A + C_comp’ B
When Buffer A drives with adjusted curves…
  A sees its own cap load PLUS the load at Buffer B
  A’s V-t curves were only adjusted for C_comp’ A!
  Equivalent output edge rate will be too slow!
V-t B
(including
C_comp)
V-t A
(including
C_comp)
Main
Boost
V-t’ B
(without
C_comp’ B)
V-t’ A
(without
C_comp’ A)
C_comp’ A
C_comp’ B
TOOL

## Slide 17: Proposed Fix
Method 2: Adjust all V-t curves for the total C_comp value before using the models for simulation
  Each V-t curve reflects total C_comp load
  Adjust each curve (Main, Boost) for total C_comp
  Set IBIS C_comp for Main, Boost to 0 pF
  Add external cap equal to original total C_comp
images and equations from A. Muranyi
Vwfm_pu (V-t)
Vfx_pu
fixture
Current through fixture
is function of current
through pullup AND
through die cap

## Slide 18: Extraction – Main Rising

## Slide 19: Extraction – Main Falling

## Slide 20: Steps & Notable Features
New curves should be much sharper
  I-V setting point should be the same
Non-monotonic “bumps”?
  C_comp does not differentiate between sources of capacitance
  Possibly due to Miller cap effects
Adjustment Procedure Details
  Start with Vload-t curve (IBIS V-t curve)
  Use Rload to calculate Iload-t curve (V = IR)
  Take derivative of Vload-t to get dVload/dt curve
  Multiply C_comp by dVload/dt to get Icap (I = C*dV/dt)
  Subtract Icap from Iload to get Iadj (watch signs!)
  Multiply Iadj * Rload to get Vadj-t curve
    Easily done in Microsoft Excel*
  Add C_comp external to buffers in simulation

## Slide 21: Results of Using New Method
New c_comp = 14pF ?

## Slide 22: Comments
Matching
  IBIS edge rate now < 0.5% match to transistor edge rate
Issues
  Peak voltage & settling still not matching transistor
  Match only good for 1100 pattern
    IBIS lacks ISI coupling to current sources
    Matching to other patterns not yet studied
  Needed to add 14 pF externally, not 8 pF, to match edges
    Recall: C_comp is added external to adjusted buffers
    Transistor and IBIS edge rates only matched with 14 pF
    What explains discrepancy?
      Under investigation (see below)…

## Slide 23: A Further Complication
Transistor model capacitance behaviors are not simple
  Capacitance for “Buffer X” vs. Frequency and bias V
  Frequency-based measurement not constant 8 pF
Recall A. Muranyi’s
analyses:
“Details on
True Differential Buffer
Characterization Revisited”
October, 2003
V
Hz
F

## Slide 24: A Further Complication
Differential view of transistor model capacitance
  Differential capacitance not included in adjusted model
  Note that finding of femto-farad differential capacitances described in previous summits may not always apply!
Recall A. Muranyi’s
analyses:
“Details on
True Differential Buffer
Characterization Revisited”
October, 2003
V
Hz
F

## Slide 25: Guidelines and Future Work
Collect three types of V-t curves from source
  Main-only V-t
  Boost-only V-t
  1100 correlation curve from full model
    Combination of main and boost, at pad with R load
    Pre- and de-emphasis behaviors will be shown
    Other data patterns may yield different results!
Use equations to “back out” c_comp
  Adjust external capacitance to match 1100 correlation curve
  Measurement method used for c_comp could make a difference!
Alternatives for investigation
  Equation-based capacitance, for example: C(V,f)
    Would require collecting additional data from source
    Very possible under IBIS 4.1
    “Backing out” c_comp from Main, Boost is non-trivial
  Driver Schedule
    Check sim tool implementation of c_comp adjustment
    V-t curve adjustment may still be needed before simulations