## Slide 1: IBIS Hierarchical Overrides and BIRD88
Bob Ross
DesignCon East IBIS Summit Meeting
Boxborough, Massachusetts
April 5, 2004

## Slide 2: What is Hierarchical Override?
Add Override rather than “Conditional” Replacement
  Letting higher order detail/functionality win
  Practical needs drove expansion
History
  IBIS grew from 8 pages in 1993 to 140+ in 2004 with layers of capability blended into EBD (later), [Component], [Package], [Model] – Cornerstone skeleton for surrounding development
  Least disruptive with downward/upward compatible changes
  Presentation motivation: BIRD88 [Driver Schedule] initialization
Many cases from the early days, for example:
  L_pin overrides default L_pkg,
  [Rising/Falling Waveform] overrides [Ramp]
Plus EDA interface overrides (e.g., model and differential pin assignments)

## Slide 3: Why this Approach?
Least disruptive
  Keeps SIMPLE rules rather than “conditional”
  Keeps IBIS sections similar – easier visual inspection
  Keeps parser simple – lower cost, fewer “conditional” upgrades to specify, track, check, repair, …
  Keeps original required “defaults”, even if not fully meaningful for syntactical robustness (Typ column always required)
Penalties
  Not always technically robust or correct ([Ramp] for LVDS)
  Redundant (or wrong) information confusing and wasteful
  Inheritance of capabilities differences (e.g., [Driver Schedule] versus [Submodel] with inheritance of voltage rails)
  Burden falls on EDA vendors to sort out and implement properly

## Slide 4: Package Example Overrides (H to L)
EBD’s a separate issue (calls EBDs or components)
ICM under discussion possibly using [Alternate Package Model Mechanism]
[Define Package], [Package Model] (V. 2.1, V. 3.2)
  Coupled package Matrices (V. 2.1), or Len L, R, C/ (V. 3.2) overrides *_pin and *_pkg below
    [Number of Sections]/[Model Data] “flags” instead of overrides
  [Package Model] in .ibs file overrides same model in .pkg file
[Model] L_pin, R_pin, C_pin (V. 1.1)
  Optional specific pin overrides default package
[Package] L_pkg, R_pkg, C_pkg (V. 1.1)
  Required Typ column – lowest order default

## Slide 5: Voltage Rail Overrides
[External Model] under [Model] (V. 4.1) (external power)
[Pin Mapping] assignments and EDA or multi-lingual rail voltage assignments – some EDA vendors may override voltages (V. 3.2, V. 4.1))
[Pullup Reference], [Pulldown Reference], [Gnd Clamp Reference], [Power Clamp Reference], (V. 2.1), [External Reference] (V. 4.1)
  SIMPLE RULE: [Voltage Range] REQUIRED (unless first FOUR rails are given) – no conditional mix and match
  Gives added detail not available from [Voltage Range] – such as ECL and PECL voltage, hot swap clamps, etc.
[Voltage Range] and implied default 0 V ground (V. 1.1)
  Typ column required

## Slide 6: Threshold Overrides
[External Model] under [Model] thresholds (V. 4.1)
  D_receive
[Diff Pin] threshold vdiff (V. 2.1)
  Overrides single ended thresholds below
[Receiver Thresholds] under [Model] (V. 4.1)
  Adds detail and new thresholds including some differential checking conditions
[Model Spec] thresholds under [Model] (V. 3.2)
  Adds typ/min/max detail and more choices
[Model] subparameters (V. 1.1, V. 2.1)
  Some still required for certain Model_types
  Historical Vinh, Vinl requirements retained even if overridden by [Model Specification] (with legacy 2.0 V and 0.8 V defaults)

## Slide 7: C_comp – an Exception
[External Model] under [Model] (V. 4.1)
  C_comp, C_comp_* optional
[Model] C_comp_pullup, C_comp_pulldown, C_comp_gnd_clamp, C_comp_power_clamp (V. 4.1)
  Different rule, C_comp NOT required if any of above exist
  So rule is at least one of C_comp or C_comp_* must exist
[Model] C_comp (V. 1.1)
  Required Typ value
Scheduled [Model] under [Model]
  C_comp values should be “0”, should be ignored since the overall mode control (Model_type) is at the higher level [Model]
  Still required entry in scheduled [Model] for simplicity of documentation

## Slide 8: [Diff Pin] and [Model] Overrides
[Diff Pin] partial overrides of [Model] (V. 2.1)
  Polarity set by [Diff Pin] and inv_pin columns
    Needed since same [Model] can be used for any pin
  vdiff threshold used instead of model thresholds
  Skewing of inverting operation with respect to non-inverting (tdelay_*)
[Model] (V. 1.1)
  Polarity and other subparameters override those below
  [Model] STATE is central
[Driver Schedule] references to models (V. 3.2)
  Initiation and polarity of scheduled models made relative to the [Model] STATE and [Driver Schedule] delays
  Specified in BIRD88

## Slide 9: My (stated/unstated) [Driver Schedule] Assumptions (in BIRD35.3)
Under [Model], the model state assumptions must prevail
  Works for single transition and one cycle (Rising and Falling)
  FULL CYCLE for [Driver Schedule]
    Rise_on_dly Rise_off_dly Fall_on_dly Fall_off_dly
    r1 or NA r2 or NA f3 or NA f4 or NA
    Full cycle => down-up (d-u), (u-d), (d-u-d-u), (u-d-u-d) sequencing for “slow” clock (assumes no over-clocking)
    16 possibilities, but 5 [r/f || NA] table variations with 8 total variations considering numerical ordering, finite durations
  Follows top-level [Model] state (Low or High) and input stimulus in transparent manner including Polarity
  Everything is relative to Rise or Fall edges of “internal simulator pulse”
Therefore known initial state (High or Low) allows single switch and one cycle simulation

## Slide 10: Scheduled Model Initial States (should be implemented for full capability)
R_on R_off F_on F_off Model Low Model High
r NA f NA Low High
NA r NA f High Low
r1 r2 NA NA Low Low
r2 r1 NA NA High High
NA NA f1 f2 High High
NA NA f2 f1 Low Low
r1 r2 f2 f1 Low Low
r2 r1 f1 f2 High High

## Slide 11: Illegal Cases
R_on R_off F_on F_off Reason
NA NA NA NA unknown initial state
r NA NA f u-u sequencing
NA r f NA d-d sequencing
r1 r2 f1 f2 u-d-d-u sequencing
r2 r1 f2 f1 d-u-u-d sequencing
And just 1 or 3 numerical entries (sequencing)

## Slide 12: Summary
Expansion of IBIS based mostly on evolutionary hierarchical overrides
  Simple rules (easier specification and parser maintenance)
  Some exceptions – and complicated rules
[Driver Schedule] insertion consistent with [Model] states
  Initial scheduled model states defined in BIRD88, as originally intended