## Slide 1: Case Study: Using IBIS Buffer Models for Pre-emphasis Lance Wang DesignCon East - IBIS Summit, April 2003

## Slide 2: Pre-emphasis Application
Main Source
Boost Source
Delay
(1 Bit)
Stimulus
Emphasized
Signal

## Slide 3: IBIS Buffer Models for Pre-emphasis
Extract Buffer Data for Main Source
Extract Buffer Data for Boost Source
  From common applications, they could be scaled from Main Sources
Stimulus Delay for Boost Source

## Slide 4: It works
An example

## Slide 5: It works (Parameter Setting)
("pre-emphasis_driver"
(MacroModel
(MacroType TDiffIO )
(NumberOfTerminals 8 )
(Parameters
(Buffers
(BUFF pre_emph_dB_drvr ) )
(MinTypMaxParams
(eqdb -3.5 )
(bitp 400p )
(padcap 0.3p) ) )
(SubCircuits “
Equalization Fact
(Main Source vs. Boost Source)
Bit Width
C_comp

## Slide 6: It works (Boost Source Scaling)
.param eqf='1.0 - (10.0 ^ (eqdb/20.0))'
.param cf1='cf0 * eqf'
xtx0 nvdd out ngnd in0 en tx scale='cf0'
xtx1 nvdd out ngnd in1 en tx scale='cf1'
.subckt tx nvdd out ngnd in en scale=1
bdrvr nvdd out ngnd in en Model=BUFF File=ibis_file c_compX=0
+ VIScale_pulldown='scale' ……
.ends tx
Scale conversion
Circuit calls with
Scaling fact
Bdrvr element
You can use other Spice Syntax
to produce the same functionality

## Slide 7: It works (Stimulus Delay)
xin0 in0 in ngnd delayin inv=inv0
xin1 in1 in ngnd delayin inv=inv1 del='bitp'
.subckt delayin in1 in ngnd inv=0 del=0
einp in2 ngnd v='inv * (1 - v(in,ngnd)) + (1-inv) * v(in,ngnd)'
ein1 in1 ngnd pwl in2 ngnd delay=del
datapoints vv
0 0
1 1
end vv
.ends delayin
Stimulus Delay
On Boost Source
Stimulus Delay
circuit
You can use other Spice Syntax
to produce the same functionality

## Slide 8: It works (Results)

## Slide 9: It works (Results)

## Slide 10: It works (Results)

## Slide 11: It works (Results)

## Slide 12: It works (Results)

## Slide 13: Conclusions
Keys for IBIS Implementation
  Boost Source Data Extraction
    Main Source Scaling
    C-comp and Internal Terminations
  Stimulus Delay (1 bit for Pre-emphasis)
More Complicated DSP Applications are coming

## Slide 14: What IBIS could do (Discussion)
Support Scalable Current Sources
  Add “Scale Fact” into [Pin] section
  Or, Introduce “Scaled” [Model] Refer to the Main Source
Support Multiple Stimulus Inputs with Delays
  Add “Stimulus Delay” into [Model] section
  Or, Introduce new [Signal] keyword for Signal Grouping with Stimulus Delays, Signal Logic Operations (OR, AND, …) etc. Even Scaling Facts.