## Slide 1: Gate Modulation Solution Validated by VHDL-AMS IBIS Implementation
Antonio Girardi
Giacomo Bernardi
Roberto Izzi
STMicroelectronics
Flash Memory Group
R&D CAD

## Slide 2: Agenda
IBIS “Gate Modulation” solution: ST Proposal overview
Implementation and Validation by the VHDL-AMS IBIS architecture
BIRD98 & ST proposal convergence
Conclusions

## Slide 3: IBIS Gate Modulation Criticality
Effective (SPICE) working point evolution
The IBIS simulation of a simultaneous switching noise does not model correctly the MOS Vgs voltage variation because the working point can move only along the same Vgs =VDD characteristic.
The higher is the bouncing noise, the higher is the mismatching between IBIS and Spice results
DRIVER
CONTROL LOGIC
ctr
Input/data
VDD
VDD
Vgs
Vgs=VDD
IBIS working point evolution

## Slide 4: Benchmark SPICE vs IBIS Standard (IBIS-STD)
SSO – Rise Transition
Output
Power/Ground
SPICE
SPICE
IBIS-STD
IBIS-STD
SSO – Fall Transition
Output
Power/Ground
SPICE
SPICE
IBIS-STD
IBIS-STD
Max Delay
22%
Max overshoot/undershoot
25%
Diff. Power supply
32%
Relative Percentage Error
Initial case of study: Simultaneous Switching Output (SSO) simulations by IBIS standard (IBIS-STD), compared with the related SPICE ones, have revealed strong discrepancies.
Initially, no equivalent load/impedance has been considered on the power and ground nodes of IBIS models.
Test-case: 128M Nor Flash Memory (120nm)

## Slide 5: Gate Modulation Coefficients
I_effective = Kssn(Vgs,Vds)*I_IBIS-STD
I(Vgs, Vds) = Kssn(Vgs,Vds)*I(Vgs=VDD,Vds)
IBIS standard current
Effective SPICE current
The ST “Gate Modulation” solution is based on the introduction of two coefficients, one for the Pullup and one for the Pulldown stage, which modulate properly the IBIS standard current (I_IBIS-STD) when a bouncing noise occurs on the power and ground nodes

## Slide 6: Kssn(Vgs, Vds) Implementation by Table-format
IBIS DEVELOPER
The effort has been focused on identifying a table-format implementation of Kssn coefficients, which could also be the best trade-off between accuracy and development/simulation time
How can I interpolate them?
Is this approach convenient in terms of development and simulation time?
Vgs=VDD
Table n
How many I(Vgs, Vds=K) or I(Vgs=K, Vds) tables are needed?
I(Vgs, Vds =K) Tables
Table 1
Table n
Table 1
I(Vgs=K, Vds) Tables
Note: K means constant value!!!

## Slide 7: Gate Modulation Coefficient Characteristics
Vds
Kssn
MOS Saturation zone
MOS Linear zone
The Kssn coefficient is independent from the Vds voltage in the saturation zone and, approximatively, also in the linear zone, in the case of small Vgs changes.
It implies that one table Kssn(Vgs, Vds=K), with K in the saturation zone, can be enough for Pullup and Pulldown, respectively.
Therefore, a Two-Table approach may be a good compromise accuracy-complexity.
Vds = K
Vgs > VDD
Kssn > 1
Ieffective > I_IBIS-STD
Vgs < VDD
Kssn < 1
Ieffective < I_IBIS-STD
Vgs = VDD
Kssn = 1
Ieffective = I_IBIS-STD
Corrective behaviour of the Kssn coefficient

## Slide 8: Two-Tables Solution
K has been chosen equal to VDD (best choice if the MOS channel modulation effect is negligible)
Kssn(Vgs, Vds=VDD) implies that the effective current to be drawn is
I_effective_pulldown=I(Vgs, Vds=VDD)
I_effective_pullup=I(Vsg, Vsd=VDD)
Vds
Saturation zone
Linear zone
Kssn
Vds=VDD
Vds=VDD
Vgs=VDD

## Slide 9: Effective Currents Extraction
Pulldown I(Vgs, Vds=VDD) table extraction
Pullup I(Vgs, Vds=VDD) table extraction
Kssn_pulldown
Kssn_pullup
I(Vgs, Vds=VDD) Table
I(Vsg, Vsd=VDD) Table
I_effective =Kssn*I_IBIS-STD
Since it is not possible to change the proprietary code of EDA tools that manage the IBIS models, the unique way identified for implementing and validating the solution has been to use the VHDL-AMS IBIS architecture, adding the Gate modulation coefficients algorithm.
?
Vsweep=[-VDD, VDD]; Vgate is kept stable -- the collected effective current is related to the source voltage (Vs) changes
VHDL-AMS

## Slide 10: Extension of the VHDL-AMS IBIS Implementation
entity IBIS_IO is generic (C_comp : real := 4.55e-12;
…………………………………………………………………………
[Pullup Reference] and [Pulldown Reference] values
V_pu_ref : real := 5.0; V_pd_ref : real := 0.0;
Vectors of the IV curve tables
I_pc : real_vector := ( 0.08, 0.00, 0.00, 0.00);
………………………………………………………………………..…
if (Extrapolation = "IV") and (X <= Xdata(0)) then m := (Ydata(1) - Ydata(0)) / (Xdata(1) - Xdata(0)); yvalue := Ydata(0) + m * (X - Xdata(0));
return yvalue;
……………………………………………………………………..........
VHDL-AMS IBIS
Traditional IBIS (Muranyi)
I-V tables: Pullup&Power_clamp
V-t tables: Rising & Falling waveform
Ramp values: dV/dt_r; dV/dt_f
C_comp values
Kssn-pulldown & Kssn-pullup
I_effective = Kssn*I_IBIS-STD
+
Gate Modulation Algorithm
I(Vgs,Vds=VDD)Pulldown table
I(Vsg,Vsd=VDD) Pullup table

## Slide 11: Implementation and Validation Strategy
NOR Flash memories test-cases
SSO simulations have been carried out
The VHDL-AMS IBIS implementation (IBIS-AMS) has been used
The “Gate modulation” algorithm has been added to the VHDL-AMS IBIS initial code
Equivalent impedance of power rails is also been considered
VDD_IO
GND_IO
IN
EN
OUT
IBIS
VHDL-AMS
VDD
VDD_IO
GND_IO
GND
Kssn_Pullup
Kssn_Pulldown
+

## Slide 12: Benchmark SPICE vs IBIS-AMS
SPICE
IBIS-AMS
SPICE
IBIS-AMS
SSO – Rise Transition
Output
Power/Ground
Output
Power/Ground
SPICE
IBIS-AMS
IBIS-AMS
SPICE
SSO – Fall Transition
Relative Percentage Error
Max Delay
3% (22% IBIS-STD)
Max overshoot/undershoot
8% (25% IBIS-STD)
Diff. Power supply
1% (32% IBIS-STD)
Test-case: 128M Nor Flash Memory (120nm)
A remarkable improvement has been achieved by implementing the ST “Gate Modulation” solution in the IBIS-AMS architecture.
Note: The main contribution on recovering the error on the power/ground signals is due to the equivalent impedance put on the power nodes.

## Slide 13: IBIS-STD vs SPICE vs IBIS-AMS Comparison
Additional benchmarking results, extracted recently by SSO simulations on a 512Mb NOR Flash Memory (90nm).
Probing on package’s ball
Probing on IC’s pad
IBIS-AMS_ball
SPICE_ball
IBIS-STD_ball
IBIS-AMS_pad
SPICE_pad
IBIS-STD_pad

## Slide 14: BIRD98 & ST Proposal Convergence
Today it is mandatory to provide to the IBIS community a reliable solution of the “Gate Modulation” problem. In fact, it is becoming a heavy bottleneck in every applications in which the SPICE simulations are not a possible alternative.
Especially in the context of system-in-package design, where third parties’ components may only be simulated by IBIS, and the power noise is critical because the ground planes are usually missing, it is impossible to predict fails before of the prototype-phase.
Moreover, it has to be considered that the SPICE simulations seem too time-expensive, as IBIS alternative, in verifying the modern-system, whose complexity is rapidly increasing.
The BIRD98 proposal is already a good solution for solving the “Gate Modulation Effect”, but two changes are advised for making it much more accurate and general purpose. As well as for matching the ST proposal, validated by the IBIS-AMS implementation.

## Slide 15: BIRD98 Suggested Change (1)
GNDQ
VDDQ
VDD
Output pad
Final Stage
Control Logic
To consider the instantaneous source voltage value (Vs) instead of the power supply one for the current scaling. This approach is more general purpose. In fact, it is not always true that the Vgs instantaneous value is the same of the power supply one during a bouncing noise. A typical case is when the control logic and the final stage are supplied with different supply voltages.
Vgs = (Vdd – Vgndq)
Vgs
(Vddq – Vgndq)

## Slide 16: BIRD98 Suggested Change (2)
It is preferable to draw the “effective” pullup (pulldown) currents by disconnecting the pulldown (pullup) stage from the pad, instead of the short current. In fact, to short the output pad to the reference node causes a change into the correct behaviour of the control logic driving capability when the control logic and the final stage are supplied by the same supply voltage.
Below are reported the two advised circuits for drawing the “effective” pullup and pulldown currents

## Slide 17: ST Proposal - Lowlights
The Miller’s capacitances (AC effects) are not included
The final-stage’s Ron instantaneous change is still a little bit under estimated compared to spice behaviour
This proposal has been developed and validated only for CMOS driver

## Slide 18: ST Proposal - Highlights
It is a table-format solution
Validated by the IBIS-AMS architecture on several test-cases
Good trade-off between accuracy and complexity (both development and simulation time)
Does not reveal proprietary information (full compliant with IBIS philosophy)
Easy implementation into transistor-level EDA tools
This proposal seems a reliable way for solving rapidly the gate modulation problem, which makes IBIS unusable in every non-ideal power supply simulation.

## Slide 19: Reference Documents
BIRD98 proposal (Arpad Muranyi, Intel)
http://www.vhdl.org/pub/ibis/birds/bird98.txt
IBIS Simultaneous Switching Output Simulations Criticality (A. Girardi, STMicroelectronics)
http://www.vhdl.org/pub/ibis/futures/ST_Vgs_Presentation.pdf
IBIS Gate Modulation Effect Proposal (A. Girardi, STMicroelectronics)
http://www.vhdl.org/pub/ibis/futures/ST_IBIS_Gate_Modulation_Effect.pdf
IBIS Gate Modulation Effect (STMicroelectronics Proposal) (A. Girardi, G. Bernardi, R. Izzi, STMicroelectronics)