## Slide 1: Forward looking trends in SERDES modeling
Eric Rongere
Stephane Rousseau
© Mentor Graphics Corp., 2007,
Reuse by written permission only. All rights reserved.

## Slide 2: AGENDA Forward looking trends in SERDES modeling
Current Status & Modeling Options
AMS Case Studies: SERDES and DDR2
Looking Forward

## Slide 3: Current Status
Traditional IBIS still adds value for modeling behavior, but lacks the ability to adequately characteristics of devices used in state of the art communication channels:
  Drivers with pre-compensation
  Receivers with input slew rate sensitivity
  Phase-locked loop clock and data recovery
  Simple and adaptive equalization
  Multi-level signaling
  Multiple receiver thresholds (e.g, DDR2/3)
We have additional challenges with measurement ... E.g.,
  Receivers with slew-rate sensitivity
  Self-clocked data streams
Though it’s still the first choice where it is sufficiently accurate, IBIS no longer supports the 99% criteria
  We need a new “lowest common denominator” solution for these needs

## Slide 4: IBIS 4.2 Multi-lingual Extensions Addressing Most or All of the Limitations
IBIS only
IBIS Parasitics with external SPICE model (e.g., Eldo or HSPICE)
IBIS model with external SPICE circuit and external VHDL-AMS model
IBIS Model
PIN
Component
Pin
Composite Model
SPICE
Buffer
Model
PIN
Component
Pin
Composite Model
Package
Model
External
Buffer
Model
PIN
Component
Pin
SPICE or Touchstone format
Any number of possible formats ... Discussed in the next section

## Slide 5: Option 1: Transistor-Level SPICE
Pros
  IC manufacturers can use the internal models that were developed from the Silicon
Cons
  Encryption is required to hide vendor IP; Each EDA vendor has their own encryption package and proprietary foibles in their transistor primitives
  Simulation is slow compared to IBIS or other options
  Complicated models are prone to hidden problems and instability
  Implementing flexible measurements in the model (e.g., dynamic overshoot) is too difficult
  To solve the overall problem we would have to add a comprehensive measurement language to IBIS
Notes: 10 million bits take weeks to simulate in SPICE; many BER requirements assume a Billion Bit product lifecycle. Clearly, we need something faster than this to make reasonable BER predictions.

## Slide 6: Option 2: Macro-models
Pros
  Will work with any EDA vendor that has AMS, or is willing to add the (macro) building blocks into their SPICE-like simulator
  Faster simulation than transistor level models
Cons
  The current building blocks have only been proven in their support of IBIS 3.2
  It is likely that new building blocks will soon be needed
  Implementing flexible measurements in the model (e.g. the new dynamic overshoot) is too difficult
  To solve the overall problem we would have to add a comprehensive measurement language to IBIS

## Slide 7: Option 3: Analog-Only AMS*
Pros
  Most EDA vendors have access to analog-only AMS
  Stepping stone to full AMS
  Relatively easy for the model to do its own measurements
    Can be output as text messages ready for the spreadsheet
    Augment in IBIS with a simple list of column headings to add to the spreadsheet
  Fast simulation
Cons
  The languages are complex and no vendor has every feature supported
    Could be alleviated by agreeing to a preferred language subset
  Implementing digital features—e.g., extended history in an equalizer requires jumping through hoops
* Analog “AMS” generally differs from “A” in its support for discontinuous functions

## Slide 8: Option 4: AMS
Pros
  VHDL-AMS and Verilog-AMS are international standards
  The most flexible solution, compared to Options 1-3
  Easy for the model to do its own measurements
    Can be output as text messages ready for the spreadsheet
    Augment in IBIS with a simple list of column headings to add to the spreadsheet
  Fast simulation
    Models are compiled to machine code just like built in primitives
    Digital content is handled in event driven kernel
Cons
  Only one EDA vendor currently offers AMS in their SI tools
  The languages are complex and no vendor has every feature supported
    Could be alleviated by agreeing to a preferred language subset
Notes: VHDL-AMS and Verilog-AMS are international standards
  IEEE and Accellera

## Slide 9: Option 5: Algorithmic Modeling
Description
  Vendor-neutral, C-based models that would be owned, developed and compiled by IP vendors
  Based on a yet-to-be-defined API/spec from the IBIS committee
Pros
  Measurements would likely be supported
  EDA Vendor neutral
  Encryption would hide IP
  Fast simulation
    Models are compiled to machine code as a DLL or executable
Cons
  No EDA vendor currently offers this support
  While easy for some vendors—because they’re already creating these models—many vendors would require a good bit of work to create these models

## Slide 10: AGENDA Forward looking trends in SERDES modeling
Current Status & Modeling Options
AMS Case Studies: SERDES and DDR2
Looking Forward

## Slide 11: AMS Case Study 1 Full non-linear analysis of a SERDES channel
Objectives:
  VHDL-AMS Driver with non-linear drive characteristics and pre-compensation
  Employ a realistic S-Parameter model for packages, two connectors and a backplane
  VHDL-AMS receiver model with built-in (AMS) envelope recorder
  Simulate to 10 million data bits using a custom data pattern on an average single-processor notebook computer running Microsoft Windows and an appropriate simulation time-step for accurate results

## Slide 12
AMS PRBS Generator
AMS SERDES TX
S-Parameter TX Package, Stub, Connector, Backplane, Connector, Stub, RX Package
AMS RX and Envelope Generator

## Slide 13: The VHDL-AMS SERDES Transmitter Model
begin
-- output the proper current based on the state of signal din,
-- and values of constants Ipe and Imain
if domain = quiescent_domain use – if DC then
itxp == Ipe/2.0; itxn == Ipe/2.0; -- set both outputs to half
elsif din='1' and din'delayed(bit) = '0' use
itxp == Ipe; itxn == 0.0; -- first pulse (txp positive)
elsif din='1' and din'delayed(bit) = '1' use
itxp == Imain; itxn == Ipe-Imain; -- normal pulse (txp positive)
elsif din='0' and din'delayed(bit) = '1' use
itxp == 0.0; itxn == Ipe; -- first pulse (txn positive)
elsif din='0' and din'delayed(bit) = '0' use
itxp == Ipe-Imain; itxn == Imain; -- normal pulse (txn positive)
end use;
break on din, din'delayed(bit) ; -- deal with the discontinuities
-- P and N-side C_comp, R_term, Vdd
i_r_term_p == (vtxp - Vdd)/R_term; i_c_comp_p == c_comp * vtxp'dot;
i_r_term_n == (vtxn - Vdd)/R_term; i_c_comp_n == c_comp * vtxn'dot;
end architecture;

## Slide 14: Results: Simulation to 10 Million Data Cycles (All simulations completed overnight)
10 Cycles
100 Cycles
1,000 Cycles
10,0000 Cycles
100,000 Cycles
1,000,00 Cycles
10,000,000 Cycles

## Slide 15: AMS Case Study 2: Automated DDR2 Measurements
Objectives:
  Implement all measurements specified in the DDR2 datasheet in a VHDL-AMS model
  Utilize off-the-shelf IBIS 3.2 driver and receiver models
  We want to be able to include DDR2 nets in an automated scan of the whole PCB
  We do not want to hard code DDR2 specific features into the waveform analysis or results spreadsheet
    This would be a never ending job and delivered later than typical delivery schedules
Issues:
  The clock and data receivers are slew-rate sensitive
  Dynamic overshoot is specified using a VT area

## Slide 16
overshoot area
absolute overshoot
slew rate
monotonicity
crossing zone
runt pulse
undershoot area
min pulse width
absolute undershoot
overshoot area
absolute overshoot
pos set runt pulse
undershoot area
pos setup tangent
absolute undershoot
pos hold tangent
neg setup tangent
neg hold tangent
neg hld runt pulse
pos derated setup
pos derated hold
neg derated setup
neg derated hold
Delta TF
pos hld runt pulse
neg set runt pulse
DDR2 Electrical and Timing Constraints
Notes: While certainly not meant to summarize the entire JEDEC DDR2 specification, this diagram does quickly convey the complexity and difficulty of thoroughly testing a typical CPU to DDR2 memory interface. Add to this the fact that these tests must be made on each data line individually and the task quickly becomes overwhelming. Required tests include absolute over/undershoot which tests for the never-to-exceed voltage limits, and the over/undershoot area which limits the power dissipated by clamp diodes. Slew rate is measured on both DQS and DQ which is then applied to the derating table to determine the required setup and hold time based on the rise and fall characteristics. Measuring the DQ slew rate is complicated by the requirement that the slew be based on the line with the maximum slope that originates at the AC crossing and is tangent to the measured signal. Additional tests include the crossing of the differential DQS signal within a certain voltage zone, and the requirement that DQS be monotonic within another voltage zone. Both DQS and DQ must be monitored for runt pulses, where the signal crosses the threshold but fails to reach a certain voltage before crossing back through the threshold. Finally, DQS must be checked for minimum pulse width, and the DQ must be checked for setup and hold requirements based on the slew-rate derated calculations.

## Slide 17: DDR2 IBIS 4.2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
DQS
DQ0
Results
Notes: The measurement model can be used stand-alone as a distinct device in the pre-layout editor …
The model monitors the clock and data pins, and performs the measurements as outlined on the previous slide. If a violation occurs, an appropriate message is generated. Unfortunately, the IBIS standard does not deal with standard message formats, or how to transfer the message out of the model and into the underlying tool for a consistent display to the user. This is an issue the IBIS committee may want to address.

## Slide 18: Pre-Layout Analysis Using the DDR2 IBIS 4.2 Measurement Model
Notes: Which will look like this in a pre-layout tool …

## Slide 19
TANGENT MEASUREMENT
Wait for vref crossing
Store data points
Wait for vix_ac cross
Calculate the slope from each point to the vix_ac crossing point
Return the maximum slope
Wait for vix_dc crossing
Calculate the slope from each subsequent point back to the vix_dc crossing
Wait for vref crossing
Return the max slope
(error and exception handling removed for clarity)
Notes: This code demonstrates how the maximum tangent line is determined. The calculation of the setup tangent line is complicated by the fact that we do not know the tangent line pivot point (the AC crossing point) until after the datapoints for the free-end of the tangent line have passed. For this reason, the free-end data points must be stored until the AC crossing occurs.
The process begins by waiting for a reference crossing. At that point, the module then stores all the analog solution points (ASPs, also known as “time-points”), until the signal crosses the AC threshold. Instantaneously after the AC crossing, the slopes of the lines from each stored point to the AC crossing point is calculated, and the maximum of these is stored. The “nominal” slope line is the line drawn directly between the reference and AC crossing. If the slope of the signal curves left of the nominal line, the nominal line will end up having the greatest slope and thus its slope will be used as the entry to the derating table. If the signal curves to the right of the nominal line, the resulting tangent line with the greatest slope will be used as the entry to the derating table.
The “Hold” tangent measurement is slightly easier, as we know the pivot point of the tangent line first, so we do not need to store any data points. This section of the process waits until the DC crossing, then calculates the slope from that crossing point to each analog solution point until the reference crossing is detected. The line with the largest slope is used as the tangent line, and used as the index into the hold derating lookup table.
Unfortunately, IEEE 1076.1 does not define a signal for analog solution points. This is left up to the simulator vendors to provide, and might not be a universally supported extension. A work-around to this is to use some fixed period sampling instead of ASPs, but this requires some knowledge of the expected time-step so that an appropriate sampling period can be chosen. Unnecessary sampling could also slightly increase the simulation time for this model. The addition of an ASP signal would be a valuable enhancement for the IEEE 1076.1 committee to provide in their next revision of the standard.

## Slide 20
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 2337
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 4790
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 7290
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 9815
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 12294
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 14816
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 17293
U2 pin 1 Violation - MAXOVERSHOOT or MAXUNDERSHOOT Level Exceeded at time: 19816
U2 pin 2 Violation - DQS exceeded VIXACMIN at Differential Crossing at time: 1275
U2 pin 2 Violation - DSQ exceeded VINDCMAX or VINDCMIN at time: 5914
U2 pin 2 Violation - DSQ exceeded VINDCMAX or VINDCMIN at time: 5955
U2 pin 1 Setup Check PASSED. Expected: 0.275 ns. Actual: 1.55 ns at time: 4536
U2 pin 2 Warning: dqs slew value out of range of table.
dqs_slew= 4.33e+9. Max table index value= 4.00e+009 at time: 5799
U2 pin 2 Warning: dq slew value out of range of table.
dq_slew= 3.566e+9. Max table index value= 2.00e+009 at time: 5799
U2 pin 1 Hold Check PASSED, Expected: 0.32 ns. Actual: 1.177 ns. at time: 5799
Notes: The Orange signal DQ, the purple is subtracted differential DQS, and the light blue is the a plot of the calculated tangent line. The model automatically applies the tangent line slope to the de-rating tables and determines if the de-rated timing constraints have been met, so The tangent line is for visualization purposes only.
The model automatically performs the 25 electrical and timing tests as outlined earlier, and outputs the results. The model can be configured to output any combination of violations, passes, measurements, and margins.

## Slide 21: Model for the Full DDR2 Channel Integrating both Behavior and Measurement *
IBIS 3.2 Model
DDR2 Memory Digital HLD Model
(responds to read cycles)
IBIS 3.2 Model
CPU Digital HLD Model
(generates real write/read cycles)
Printed Circuit Board
…
DDR2 Measurement Model
IBIS 3.2 Model
IBIS 3.2 Model
IBIS 4.1 Chipset Model
IBIS 4.1 Memory Model
DQS
DQ0
DQ[63:1], A[18:0], etc[26:0]
…
Msgs
Chipset Measurement Model
Msgs
… (108)
… (108)
…
* Note: This model is not in strictly IBIS 4.2 compliant because it uses an external circuit that references an IBIS 3.1 model
Notes: As mentioned earlier, the measurement model can be incorporated into the post-layout IBIS 4.1 device model to allow a complete post-layout analysis. This diagram shows the model being incorporated into the DDR2 Functional SI analysis (See DesignCon 2006 IBIS Summit for more details).
Once in IBIS 4.1 format, all that is left to the model user is to import the IBIS 4.1 model into their IBIS 4.1 compatible tool, assign the model to the memory part, and invoke the simulator. The IBIS 4.1 models take care of providing stimulus to the PCB, and measuring the resulting signals at the memory pins. All the user need do is review the resulting messages to see if there has been a violation … infinitely simpler than previous alternatives of manual inspection and interpretation.

## Slide 22: AGENDA Forward looking trends in SERDES modeling
Current Status & Modeling Options
AMS Case Studies: SERDES and DDR2
Looking Forward

## Slide 23: Conclusions
IBIS 4.2 Multi-lingual extensions
  The model maker and user can best decide whether it is best to create models using the IBIS 4.2 multi-lingual extensions utilizing SPICE or AMS
  The best solution for the SI Engineer may well be a tool that supports the mixing of both
Necessary IBIS enhancements
  Create intelligent multi-lingual input models that delay their output signal based on the slew rate
  Enhance the IBIS measurement facilities to support the new dynamic overshoot constraint
    Describe how to make the measurement
    Inform the spreadsheet to add new columns for the data

## Slide 24: Summary of SERDES Modeling Options
1. SPICE
  Slow as it is, SPICE performs an important function, and isn’t going away
2. Macro-modeling
  Died a slow death in committee
3. Analog-only AMS
  Hasn’t gotten much traction, but might represent the middle ground between functionality and vendor neutrality
4. AMS
  Not vendor-neutral, but supported today for 45% of the market
  Additional models and development tools are needed
5. Algorithmic modeling
  Still in its infancy, but would meet functional requirements and be vendor-neutral
6. Statistical modeling (AKA: Linear Channel Analysis or Fast Eyes)
  Still in it’s infancy, but would meet functional requirements and be vendor-neutral
Pulse
Pre-Emphasis
Channel
Package, Traces and Vias
Transmitter
Receiver
Impulse Response
Statistical Analysis
BER