## Slide 1: Three Facets of IBIS: Interface, Behavior and Measurement December 2005
Ian C Dodd
Architect, High Speed Tools
SDD Division
Henry Li
Technical Marketing Engineer
Mentor Graphics (Shanghai)
Electronic Technology Co Ltd

## Slide 2: What are the Objectives of the SI Engineer?
Maximize performance
  Highest possible clock speed
Ensure reliable operation
  Meet timing constraints
  Keep overshoot below levels that will cause device malfunction or destruction.
  Maintain adequate switching margins
Minimize per unit costs
  Minimize the number of components (including terminators)
  Use lowest cost PCB materials

## Slide 3: How can these objectives be met?
By investing in accurate timing and SI analysis so that safety margins can be controlled
  Accurate static or dynamic timing models for the internal paths of active devices
  Accurate SI models for drivers, loads and passive devices
  Accurate models for the interconnect including the associated dielectrics
  Using fully automated analysis tools so all vulnerable nets can be analyzed

## Slide 4: Basic timing analysis
Static timing analysis: Input setup and
hold time
Static timing analysis: Clock edge to data out delay
Spreadsheet: Constraints
and violations
SI analysis: Driver, receiver,
package, trace
delays

## Slide 5: Part One: Summary of IBIS to version 3.2

## Slide 6: Highlights of IBIS 3.2 Behavior
IBIS 3.2 assumes fixed topologies for drivers, inputs and terminators
Support process range: Typ, Min & Max
Drivers and Inputs
  Two steady state Current versus Voltage (IV) tables representing power and/or ground clamps.
  Capacitance
Drivers
  Nominal edge rates
  Two additional steady state Current versus Voltage (IV) tables representing pull-up and pull-down transistors.
  Optional Dynamic Voltage versus Time (VT) tables
    Load conditions must be specified for each table

## Slide 7: Highlights of IBIS 3.2 Behavior (continued)
Series and Parallel Terminators
  Resistance, Capacitance and Inductance
Package Description
  Assumes each external pin connects to one internal (die) pin
  Default Package
    Assumes no coupling: simple resistance, capacitance and inductance
  Package Model
    Allows multiple sections, each with coupled or uncoupled: resistance, capacitance and inductance

## Slide 8: IBIS 3.2 Interconnect
Provides mapping of the pins on a physical part to the models providing electrical behavior.
Allows EDA tools to automatically build complete simulation models for nets on your PCB
  Less error prone than creating simulation netlists manually
  Allows for simulation coverage of the majority of nets on your PCB.

## Slide 9: Highlights of IBIS 3.2 Interconnect
IBIS Pin Section
  Assigns driver, load and parallel terminator models to pins
Series Pin Mapping Section
  Assigns series terminators (and switches) to pins
Diff Pin Section
  Identifies differential pin pairs & adds differential delay info
Electrical Board Description (EBD)
  Limited description of a PCB containing IBIS components
  Does not support modeling of trace to trace coupling.

## Slide 10: Highlights of IBIS 3.2 Measurement
Overshoot limits
  If exceeded device may malfunction or be destroyed
  Static and dynamic
Input switching thresholds
  Logic low
    Vinl (or with hysteresis Vinl+ and Vinl-)
  Logic high
    Vinh (or with hysteresis Vinl+ and Vinl-)
Timing Reference Voltage (Vmeas)
  Transition voltage on driver pin used when measuring static timing delays e.g. “clock edge to data out”
  Associated with a reference load
    Vref, Rref and Cref

## Slide 11: Basic timing analysis
Static timing analysis: Input setup and
hold time
Static timing analysis: Clock edge to data out delay
Spreadsheet: Constraints
and violations
SI analysis: Driver, receiver,
package, trace
delays
IC 1
IC 2

## Slide 12: Putting it all together with IBIS 3.2
Simple synchronous example
  First consider the data path
Simulate the data path for the rising and the falling edges
  Find the time at which the input pin on U2 leaves the initial logic state (raw minimum delay)
  Find the time at which the input pin on U2 becomes stable at the final logic state (raw maximum delay)
Simulate the driver connected to the timing reference load
  Find the time to Vmeas
Normalize the raw delays by subtracting the time to Vmeas
  Removes any initial delay in VT table and partial edge time already included in the “clock edge to data out” delay.

## Slide 13: Including Clock Skew
Determine Clock Period
    Tclock
Simulate Data Path
  Find Normalized Data Path Delays
    TDdata_min, TDdata_max for rising and falling edges
Simulate Clock Paths
  Clock Driver to Clock Input on IC1
    TDclock1_min, TDclock1_max for active edge
  Clock Driver to Clock Input on IC2
    TDclock2_min, TDclock2_max for active edge
Get Internal Path Delay and Minimum Setup and Hold constraints from Databook
    TDpath, Tsetup_min, Thold_min

## Slide 14: Including Clock Skew (continued)
Worst Case Analysis
  Calculate the actual setup and hold times for the rising edge
  Compare the results to the timing constraints from the databook
  Repeat for the falling edge
  Tsetup = Tclock - TDdata_max + TDclock2_min - TDclock2_max
  Thold = Tclock - TDdata_min + TDclock2_max - TDclock2_min
EDA tools that have integration between timing and SI analysis commonly have spreadsheets that automate these calculations and highlight timing violations

## Slide 15: Part Two: Beyond IBIS Version 3.2

## Slide 16: Technology Changes
Data rates on PCB have dramatically increased.
PCB trace lengths have not shrunk in proportion
  clock periods are often shorter than the interconnect delay
  Source synchronous design must be used either with a separate clock signal or with an embedded clock
Power budgets have decreased
  Signaling voltages have been accordingly decreased
PCB materials have not dramatically improved
  Dielectric losses become the predominant circuit effect
  Differential signaling is required to overcome attenuation
  Pre-compensation or equalization is becoming common to compensate for wavefront distortion

## Slide 17: Highlights of Post IBIS 3.2 Behavior
ICM provides multi-stage coupled lossy transmission line or S-parameter modeling for connectors
  Presently considering allowing ICM package descriptions so we can have consistent S-parameter support
Multi-lingual extensions support behavior modeled in SPICE, VHDL-AMS and Verilog-AMS.
  Almost no limit to the complexity of behavior that can be modeled
  Depending on the simulator, model types can be mixed across the PCB and even on individual nets
Power Integrity extensions

## Slide 18: Highlights of Post IBIS 3.2 Interconnect
Multi-lingual extensions provide flexible connectivity between SPICE, VHDL-AMS or Verilog-AMS models and the external component pins
  Allows EDA tools to automatically build complete simulation models for nets on your PCB including the multi-lingual models

## Slide 19: Existing Post IBIS 3.2 Measurement
No enhancements to IBIS built in measurements since version 3.2
Multi-lingual input models can determine when a transition has occurred
  External models and circuits for inputs have a standard terminal which can be monitored by EDA tools
Multi-lingual models can do extensive analysis and use (external circuit) terminals to present the results of analysis
  No conventions as to how an EDA tool should interpret signals on these terminals
  Cannot presently be used for automated analysis or to populate constraint spreadsheets

## Slide 20: Recommendation for New IBIS Measurements
We want to validate a high percentage of nets on PCBs
  Requires automated measurement and constraint validation
  IBIS is needed to provide the interface and measurement functions even when SPICE or AMS descriptions are used for behavior
Measurement enhancements
  Support measurements specified for any IBIS external pin or internal terminal
  Provide voltage or current thresholds
  Provide logic and equations that the EDA tool should use to determine values to be reported
  Provide limits for reported values

## Slide 21: Part Three: IBIS 4.1 Multilingual Example

## Slide 22: Typical IBIS 4.1Model
Traditional
IBIS
IBIS 4.1
Syntax
IBIS 4.1 adds four new keywords
  [External Model] (new part of [Model])
  [External Circuit]
  [Circuit Call], [Node Declarations]
Spice/Behavioral model is in external file

## Slide 23: IBIS 4.1 Traditional and Multi-Lingual
SPICE or Behavioral Model
IBIS 4.1
Simulator
Multi-Lingual
IBIS
Wrapper
Traditional IBIS Model
[Pin]
1 dcp CIRCUITCALL
2 dcm CIRCUITCALL
3 bpn CIRCUITCALL
4 bpp CIRCUITCALL
|
|**********************
|
[Diff Pin]
1 2
4 3
|
[Series Pin Mapping]
2 3 R_1G_ohm
|
[Circuit Call] component
Port_map inp 1
Port_map inm 2
Port_map outp 3
Port_map outm 4
[end circuit call]
[External Circuit] component
Language Spice
Corner typ comp.sp comp
Ports inp inm outp outm
[End External Circuit]
*
.subckt comp
+ inp inm outp outm
*S-parameter model
*RLC SPICE model,
*Transistor model,
*VHDL-AMS Model
.ends
comp.sp
Spice/Behavioral model simulator
Simulator

## Slide 24: Import like any other IBIS model
Screenshot from ICX 3.4

## Slide 25: And PROBE, just like any IBIS model
User is completely insulated from SPICE complexity
Screenshot from ICX 3.4

## Slide 26: IBIS 4.1 Supports BOTH Transistor-level and AMS Models
Allows easy switch between transistor-level and AMS models
Screenshot from ICX 3.4

## Slide 27: IBIS 4.1 “Parameters” Provide for Automation
Screenshot from ICX 3.4