## Slide 1: IBIS and Behavioral Modeling
Michael Mirmak
Intel Corporation
Chair, EIA IBIS Open Forum
IBIS Summit
Shenzhen, China
December 6, 2005
迈克尔.莫马克
英特尔公司
IBIS 委员会主席
亚洲 IBIS 技术研讨会
中国深圳
2005 年 12 月 6 日

## Slide 2: Legal Disclaimers
THIS DOCUMENT AND RELATED MATERIALS AND INFORMATION ARE PROVIDED "AS IS" WITH NO WARRANTIES, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY IMPLIED WARRANTY OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, NON-INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION, OR SAMPLE. INTEL ASSUMES NO RESPONSIBILITY FOR ANY ERRORS CONTAINED IN THIS DOCUMENT AND HAS NO LIABILITIES OR OBLIGATIONS FOR ANY DAMAGES ARISING FROM OR IN CONNECTION WITH THE USE OF THIS DOCUMENT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel may make changes to specifications, product descriptions, dates and plans at any time, without notice.
Copyright © 2005, Intel Corporation. All rights reserved.

## Slide 3: What is IBIS?
IBIS* (I/O Buffer Information Specification)
  A standard format for expressing I/O buffer electrical behavior plus component pin and package information
  ANSI/EIA* 656-A, IEC* 62014
Most buffers expressed through
Current vs. Voltage (I-V tables)
Voltage vs. Time (V-T tables)
Buffer capacitance (C_comp)
Components include
Pin assignments and names
Package information

## Slide 4: Behavioral Modeling
IBIS is only one type of behavioral model
  Others include:
    ICM* (IBIS Interconnect Modeling Specification)
    IMIC* (I/O Model for Integrated Circuits, JEITA* ED-5302)
    ICEM* (Integrated Circuit Electrical Model, IEC 62014-3)
    VHDL-AMS* (IEEE* 1076.1)
    Verilog-AMS* (Accelera*)
Behavioral models replace internal design information with observations of electrical ports or terminals
Pad
Vcc
In
En
Vss

## Slide 5: An Example
IBIS, as a behavioral modeling standard, offers
  Protection of internal design information
  Availability under multiple software tools
  Increases in simulation speed over transistor-based models
IBIS behavioral vs. transistor-based models
  For a serial-differential design, IBIS can be 100 times faster!
  Careful model creation preserves accuracy
IBIS vs. SPICE*
(time-shifted to
show correlation)
Image from SiSoft*:
IBIS Models at 2.5 GHz and Beyond;
used with permission
Speed quotation from
Multi-Gigabit SerDes
System Level Analysis…
by Huq/Dodd; used with permission

## Slide 6: The Future of Modeling
Why behavioral instead of transistor-based models?

## Slide 7: The Future of Modeling
Buffer complexity is keeping pace with processor power!

## Slide 8: Supporting Future Designs
Buffers becoming more complex
  Size is tracking processing power
New designs need more analysis
  Power delivery and switching noise
  Pre-emphasis, active feedback and compensation
IBIS expanding to address needs
  New links to VHDL-AMS, Verilog-AMS, Berkeley SPICE*
  Enable equations within IBIS
  Links to ICM are in development
Berkeley
SPICE
VHDL-AMS
IBIS
ICM
Verilog-
AMS
The industry needs behavioral modeling
for today and tomorrow
IBIS provides a standard, unified solution
for behavioral buffer modeling

## Slide 9: You Are Invited!
IBIS Welcomes Worldwide Participation!
http://www.eigroup.org/ibis/
http://www.eda.org/ibis/
Specifications
IBIS: http://www.eda.org/ibis/ver4.1/
ICM: http://www.eda.org/ibis/icm_ver1.1/
Training
Including IBIS history and tutorials
http://www.eda.org/ibis/training/
IBIS Cookbook
Features explained plainly
http://www.eda.org/ibis/cookbook/
Task Groups
Futures, Macromodel Library, Quality
Free Model Review service!
IBIS appreciates your input and support!

## Slide 10: BACKUP

## Slide 11: A Related Specification: ICM
ICM = IBIS Interconnect Modeling Specification
  Standard text format for interconnect modeling data
  “Interconnect” can be connector, cable, PCB traces or even an IC package
    Defines structure as path between “sections”
    Defines the electrical data for each section
Connector
Stub
Connector
T-line
Described by
[Begin ICM Model]
…
(path description)
…
[End ICM Model]
Described by
[Begin ICM Section]
…
(RLGC or S-params)
…
[End ICM Section]
Connector
Stub
T-line