## Slide 1: Practical Measurement vs. Simulation Correlation with DDR2 667 Interface
Kazuyoshi Shoji
HITACHI ULSI Systems Co., Ltd.
Practical Measurement vs. Simulation
Correlation with DDR2 667 Interface
Kazuyoshi Shoji
Hitachi ULSI Systems Co., Ltd.

## Slide 2
People say :
IBIS model is NOT accurate.
Is that really TRUE?

## Slide 3
People say :
HSPICE model is essential for design.
Is that really TRUE?

## Slide 4
Let’s see what’s happening in the real world and make wise decisions!!

## Slide 5
Experiments
Step1
For a given target system, prepare following;
1. Measurement waveforms
2. Simulated waveforms using IBIS model
3. Simulated waveforms using HSPICE model
Step2
Verify accuracy with figure of merit method
(100% is perfect match)
Step3
Compare simulation time

## Slide 6
Target System
Digital consumer system
Point-to-point application
Memory interface with 333MHz ( DDR2 667 )
DRAM
ASIC
Layer1
50 ohm
1mm
Layer2
44 ohm
50mm
Layer1
50 ohm
1mm
via
via
Transmission lines
Probing point
Parameters extracted from real design
using Cadence Allegro

## Slide 7
Simulation condition
Memory device:
DDR2-667 333MHz DRAM
IBIS model created by HITACHI ULSI systems
Receiver:
ASIC Model
provided from system vendor
Models
Synopsys HSPICE 2005.3 SP1
Tool

## Slide 8
Measurement equipments
Oscilloscope:
Agilent technologies
Infiniium54855A 6GHz 20GSa/sec
InfiniiMax1134 probe
Single-End Solder (E2679A)

## Slide 9
IBIS vs. Measurement
Time (ns)
0
1
2
3
4
5
6
0
1
2
Voltage (V)
DRAM IBIS model
Measurement waveforms
Good match with Figure Of Merit of 96%

## Slide 10
HSPICE vs. Measurement
Time (ns)
0
1
2
3
4
5
6
0
1
2
Voltage (V)
DRAM HSPICE model
Measurement waveforms
Close match with FOM of 96%

## Slide 11
Nearly equal with FOM of 98%
IBIS vs. HSPICE
Time (ns)
0
1
2
3
4
5
6
0
1
2
Voltage (V)
Time (ns)
0
1
2
3
4
5
6
0
1
2
Voltage (V)
DRAM HSPICE model
DRAM IBIS model

## Slide 12
Simulation time comparison
Simulation CPU time
HSPICE
model
IBIS
model
4 times
FASTER!

## Slide 13
Summary
1) Simulation results of DDR2 667 system shows
IBIS & HSPICE DDR2 memory model simulation
Correlation with measurement within FOM of 96%
2) IBIS model simulation faster than HSPICE model
by four times.
3) Using IBIS model simulation is fairly accurate and fast.
Good choice for practical purpose.

## Slide 14
Thank you!