## Slide 1: Splitting C_comp for Power Integrity Simulations
Zhiping Yang, Ph.D.
Cisco Systems, Inc.
(Now with Apple Computer, Inc.)
Asian IBIS Summit in ShenZhen, China
12/6/2005

## Slide 2: Acknowledgment
The author would like to thank Cisco Systems, Inc. for the support and approval of this presentation material
The author would like to thank Apple Computer, Inc. for providing travel arrangements to make this presentation happen
The author would like to thank Randy Wolf from Micron for his support and help on HSPICE buffer model

## Slide 3: Content
Why C_comp and its split ratio are important for power integrity simulations?
The procedures to extract the C_comp and C_decap values from HSPICE simulations
Simulation results for Micron U27_a_dq buffer

## Slide 4: Why C_comp and its split ratio are important for power integrity simulations?
C_comp could impact the power integrity simulations in following ways:
C_comp at non-switching I/O could act as effective local decoupling caps. The ratio has a big impact.
C_comp split ratio heavily impacts the noise level coupled from power supply to quite I/O pins, especially at high frequency.
C_comp split ratio will have direct impact on dynamic current distribution for switching I/O buffers
Note: C_comp split ratio has no impact on SI simulations when voltage supply is ideal.

## Slide 5: Simplified I/O model for IBIS specification
VDDQ
GND
I/O
C_comp_up
C_comp_up
R_pullup
R_pulldown
C_decap
R_decap
C_decap’
R_decap’

## Slide 6: Zvddq_open
VDDQ
GND
I/O
+
_
Zvddq_open
Zvddq_open=Zdecap//(Zup+Zdown) (1-1)
Yvddq_open=Ydecap+(Yup*Ydown)/(Yup+Ydown) (1-2)

## Slide 7: Z_vddq_short_to_gnd
VDDQ
GND
I/O
+
_
Zvddq_0
Zvddq_0=Zdecap//Zup (2-1)
Yvddq_0=Ydecap+Yup (2-2)
Output is low
VDDQ
GND
I/O
+
_
Zvddq_0
Output is high
+
_

## Slide 8: Z_vddq_short_to_pwr
VDDQ
GND
I/O
+
_
Zvddq_1
+
_
VDDQ
GND
I/O
+
_
Zvddq_1
Output is low
Output is high
Zvddq_1=Zdecap//Zdown (3-1)
Yvddq_1=Ydecap+Ydown (3-2)

## Slide 9: Z_io
VDDQ
GND
I/O
+
_
Zio
VDDQ
GND
I/O
+
_
Zio
Output is low
Output is high
+
_
Zio=Zdown//Zup (4-1)
Yio=Ydown+Yup (4-2)

## Slide 10: Extraction of Yup, Ydown and Ydecap
Yvddq_0=Ydecap+Yup (2-2)
Yvddq_1=Ydecap+Ydown (3-2)
Yio=Yup+Ydown (4-2)
Yup=(Yvddq_0+Yvddq_1+Yio)/2-Yvddq_1 (5-1)
Ydown=(Yvddq_0+Yvddq_1+Yio)/2-Yvddq_0 (5-2)
Ydecap=(Yvddq_0+Yvddq_1+Yio)/2-Yio (5-3)

## Slide 11: I/O pin impedance

## Slide 12: Power/ground impedance when I/O pin is open

## Slide 13: I/O pin capacitance

## Slide 14: Vccq parasitic resistance
Everything included
C_comp effect excluded
C_comp and lumped decap cell effect excluded

## Slide 15: Vccq parasitic capacitance
Everything included
C_comp effect excluded
C_comp and lumped decap cell effect excluded

## Slide 16: Pull_up and Pull_down resistance

## Slide 17: Pull_up and Pull_down capacitance

## Slide 18: Conclusions
C_comp is frequency and state dependent
C_comp split ratio is also frequency and state dependent
C_comp and its split ratio are very important factors for correct power integrity simulations
Existing C_comp and I/V table may not completely model the frequency dependent property of I/O buffer, even at steady state.

## Slide 19: Q&A
?